## Slide 1: Other considerations of cryomodule design
Genfa Wu and Saravan Chandrasekaran

## Slide 2
Strong Back Design Transportation

## Slide 3
Spaceframe Design Transportation (ESS)

## Slide 4: Spaceframe Design
Past experiences
  Cryomodule demonstrated in SNS
  Mature procedure
Experience of partner lab
  CEA on ESS cryomodules
Experience of US labs
  SNS, JLAB
Coupler bottom mounted
Standardization
  Alignment consistency with SSR cryomodules
  Tooling design consistency
  Traveler and procedure consistency
  QA/QC consistency
  Ease of Maintenance/repair at host (Fermilab)
Experience of SSR1/2 cryomodules
Coupler side mounted
Strong Back Design

## Slide 5: The case of strong back design: benefits of standardization
PIP-II: 2 SSR1 and 7 SSR2 cryomodules have adopted strong back design
Standardization benefits:
  Consistent alignment procedure
  Consistent tooling design
  Consistent QA/QC
  Consistent assembly travelers and procedures
  Consistent maintenance and repair strategy

## Slide 6: The case of spaceframe design: demonstrated design at JLAB
Significant cryomodule experiences from SNS and ESS
  Mature engineering analysis from SNS and ESS
  Proven procedures
  Demonstrated transportation

## Slide 7: Other consideration
Current spaceframe design has power coupler bottom mounted (SNS and ESS)
Strongback design has power coupler side mounted.
  Design change of power coupler mounting introduces procedural change and requires design validation of a spaceframe design for PIP-II.
  Fermilab horizontal test cryostat supports only side mounted power coupler.
    Retrofit of current STC or HTS requires 12-18 months of design change, procurement and commissioning.