## Slide 1: Superconducting Magnet R&D for Accelerator Science at KEK Cryogenics Science Center
Toru Ogitsu
Head Cryogenics Science Center, KEK

## Slide 2: Item
HL-LHC and FCC
  D1
  Nb3Sn conductor R&D
J-PARC
  COMET
  g-2/EDM
  MLF second target
High Radiation SC Magnet R&D
HTS Magnet R&D

## Slide 3: Item
HL-LHC and FCC
  D1
  Nb3Sn conductor R&D
J-PARC
  COMET
  g-2/EDM
  MLF second target
High Radiation SC Magnet R&D
HTS Magnet R&D

## Slide 4: Japanese Contribution to HL-LHC: D1 magnets
Beam separation dipole (D1) by KEK
  Design study of D1 for HL-LHC within the framework of the CERN-KEK collaboration since 2011.
  150 mm single aperture, 35 Tm (5.6 T x 6.3 m), Nb-Ti technology.
  Development 2-m long model magnets (3 units) at KEK
Deliverables for HL-LHC
  1 full-scale prototype cold mass (MBXFP)
  6 series cold masses (MBXF1-6)
MOU’s were signed on July 6, 2018 at MEXT, Tokyo
↓
Budget partially approved

## Slide 5: Test Results
Training Performance
  Almost satisfactory for 2nd Model
Quench Protection
  Satisfactory with renewed QPH design
  Irradiation effect being checked
Field Quality
  Large b3 due to structure deformation?

## Slide 6: Item
HL-LHC and FCC
  D1
  Nb3Sn conductor R&D
J-PARC
  COMET
  g-2/EDM
  MLF second target
High Radiation SC Magnet R&D
HTS Magnet R&D

## Slide 7
Kobe Steel / JASTEC
Furukawa Electric
Fabrication
• Optimization of HT condition
• Microstructure observation
• Compositional analysis
• High field magnet facility
• Evaluation of deff
• Evaluation of Jc, Bc2
28 T HM
• In-depth characterization
HT, Jc, composition, deff ...
• Program coordination
• Defining specification
• Conceptual design
Tohoku University
R&D billets
Specification,
design
CERN
15 T VSM
Tokai University
KEK
High Jc Nb3Sn conductors in Japan for FCC
Design and Characterization

## Slide 8
Current Achievement
KSL/JASTEC
  DT method
  non-Cu Jc of 1137 A/mm2 at 4.2 K and 16 T
  Diffusion length optimization
  Ternary additive optimization
Furukawa electric
  Nb tube method
  Workability issue was significantly improved
  Jc will be evaluated soon.
Nb
Nb
Sn
Nb
Ti content: C > D > E

## Slide 9: Item
HL-LHC and FCC
  D1
  Nb3Sn conductor R&D
J-PARC
  COMET
  g-2/EDM
  MLF second target
High Radiation SC Magnet R&D
HTS Magnet R&D

## Slide 10
g-2/EDM
J-PARC Facility is jointly operated by KEK and JAEA
Bird bye view 2009
Superconducting Magnet R&D at J-PARC Cryogenics Section
J-PARC Cryogenics Section: KEK Cryogenics Science Center & KEK IPNS Cryogenics Group

## Slide 11
g-2/EDM
COMET
MLF Second Target
J-PARC Facility is jointly operated by KEK and JAEA
Bird bye view 2009
Superconducting Magnet R&D at J-PARC Cryogenics Section
J-PARC Cryogenics Section: KEK Cryogenics Science Center & KEK IPNS Cryogenics Group

## Slide 12: COMET Magnet System (Phase-I)
ColdBox
CurrentLeadBox
Pion Capture
Solenoid
Muon
Transport
Solenoid
Detector
Solenoid
TransferTube
to MTS
TransferTube
to PCS
Capture Solenoid Winding
Transfer Tube Assembly
Transport Solenoid Installation
US-JP Collaboration for Aluminum Stabilized Pion Capture Solenoid

## Slide 13: Neutron Irradiation Effects
Tcs
Y. Yang et al., IEEE Trans. App. Supercond., 28(3), 4001405 (2018).
Pion Capture Solenoid: heat up by irradiation
(max. 35mW/kg @ 56kW)
Temperature rise with thermal conductivity degradation by irradiation
Irradiation damage in Aluminum: recovered 100% by thermal cycling to room temperature.
(~85% for Copper)
RRR of stabilizer will decrease by irradiation.
May affect to quench protection
Temperature at quench is estimated with MIITs
  adiabatic condition

## Slide 14: J-PARC g-2/EDM status
Stage 2 is approved from IPNS in Nov. 2018
*H-line being constructed !
Oct. 2017
SiC Aerogel Target
NMR probe system R&D
First Muon Acceleration

## Slide 15: Magnet Design
Design work in collaboration with Japanese Company
2900 mm
Muon storage orbit
Dia. : 666 mm
Iron yoke
  Adjust field shape
Cooled by liquid Helium
  Cryocoolers to recondense LHe
Separated cold box from magnet cryostat
  Isolate vibration of cryocooler
Superconducting coils : NbTi
  Main solenoid
    Persistent current operation
  Weak focusing coil
    Power supply operation
  Shim coils
    Power supply operation
Field tuning system using iron pieces
Storage region :
  radius : 33.3±1.5 cm
  height : ±5 cm
Field strength : 3T
Uniformity : 0.1 ppm (Azimuthal integral)
Weak focus field: -5e-4 T/m of Br at max.
Cold box
Main solenoid
  Current : 419 A
    Cond. size : 2.2 x 1.5 mm
    RRR : 4
  Stored Energy : 14.78 MJ
  Inductance : 168 H
  Max. B on Cond. : 4.9 T
US-JP Collaboration for Field Measurements

## Slide 16: HTS Solenoid for MLF 2nd Target
Advantages of mineral-insulated HTS magnet
High temperature margin
(Operation in temperature range of high thermal conductivity of metal)
High radiation tolerance of ceramics insulator
Suppression of refrigerant activation by conduction cooling system
Aluminum stabilized ReBCO conductor
Muon Capture Solenoid
(Axial field ~1.5T)
directly attached to neutron target

## Slide 17: Item
HL-LHC and FCC
  D1
  Nb3Sn conductor R&D
J-PARC
  COMET
  g-2/EDM
  MLF second target
High Radiation SC Magnet R&D
HTS Magnet R&D

## Slide 18: R&D for Radiation Resistant SC Magnet
Superconducting Properties Evaluation System
@IMR-Oarai Hot Lab.
VTI
15.5 T Magnet
Irradiation tests
Neutron (REBCO, BT-GFRP, MI-sample) -ray (Organic Materials)
US-JP Collaboration
LBNL Samples
Jan9-Mar.22
8.5MGy
Jan9-Jun
~20MGy
In JFY 2019
Up to 80MGy
is approved
(CTD101K, mix61, ATLAS ECT)

## Slide 19: R&D for Radiation Resistant SC Magnet
Design study of muon source
Demonstration of RR cooling system
Customized pulse tube cryocooler

## Slide 21: Item
HL-LHC and FCC
  D1
  Nb3Sn conductor R&D
J-PARC
  COMET
  g-2/EDM
  MLF second target
High Radiation SC Magnet R&D
HTS Magnet R&D

## Slide 22: HTS Accelerator Magnet R&D with Kyoto University, NIRS and Toshiba
HTS cosθ coil
HTS combined function coil
Compact Gantry
for Carbon Ion
Cancer Therapy
Basic R&D for Medical Accelerator
Medium Field Magnet
↓
Expanding to High Field Magnet
for
High Energy Accelerator Application

## Slide 23
HTS Accelerator Magnet R&D (JSPS) Possibility for High Field High Rad. Application
In collaboration with LBNL (and BNL)
Wind Subscale coil with mineral insulation
Test with 10 T backup field
2019-2021

## Slide 24: Summary
KEK Cryogenics Center Magnet R&D
HL-LHC and FCC
  D1: On going 2nd model completed
  Nb3Sn conductor R&D: JASTEC achieved 1137A/mm2@16T4.2K
J-PARC
  COMET: Construction on going
  g-2/EDM: High accuracy field measurement collaboration (FNAL, ANL)
  MLF second target: Possibility for HTS explored
High Radiation SC Magnet R&D
  D1, COMET, MLF second target, CERN, LBNL, etc..
HTS Magnet R&D
  Many collaborations.

## Slide 25: Field integral (I=12.047kA)
n | RE (-1750 ~ -525) |  | SS (-525 ~ 525) |  | LE (525 ~ 1750) |  | Total (-1750~1750) | 
 | bn | an | bn | an | bn | an | bn | an
1 | 1925 (1871) | 0.61 (0.00) | 6259 (6267) | -0.20 (0.03) | 1816 (1862) | -6.01 (-2.73) | 10000 (10000) | -5.60 (-2.69)
2 | 1.18 (0.00) | -1.05 (-0.01) | -2.52 (-0.01) | 0.16 (0.01) | 1.03 (-0.03) | -3.66 (-0.08) | -0.31 (-0.04) | -4.55 (-0.08)
3 | -14.11 (-12.27) | -0.45 (0.00) | 24.81 (13.76) | 0.15 (0.11) | -9.74 (-9.61) | 7.30 (5.73) | 0.95 (-8.12) | 7.01 (5.84)
4 | 0.02 (0.00) | -0.30 (0.00) | -0.40 (0.01) | 0.16 (0.00) | -0.63 (-0.11) | -0.01 (0.05) | -1.00 (-0.11) | -0.14 (0.05)
5 | -0.40 (-0.90) | -0.02 (0.00) | 1.09 (0.26) | -0.14 (-0.10) | 2.62 (1.03) | -0.66 (-0.59) | 3.30 (0.39) | -0.82 (-0.69)
6 | 0.22 (0.00) | -0.02 (0.00) | 0.13 (0.00) | 0.09 (0.00) | 0.06 (-0.10) | -0.12 (0.04) | 0.41 (-0.10) | -0.05 (0.04)
7 | -1.25 (-1.05) | -0.04 (0.00) | -0.50 (-0.06) | 0.02 (0.07) | -0.39 (-0.26) | 0.42 (0.41) | -2.14 (-1.37) | 0.40 (0.48)
8 | 0.29 (0.00) | 0.05 (0.00) | -0.15 (0.00) | 0.07 (0.00) | 0.26 (-0.07) | 0.02 (0.06) | 0.40 (-0.07) | 0.14 (0.05)
9 | -0.98 (-0.99) | -0.06 (0.00) | 0.28 (0.07) | -0.05 (-0.03) | -0.50 (-0.64) | -0.04 (-0.08) | -1.19 (-1.56) | -0.15 (-0.12)
10 | 0.14 (0.00) | 0.01 (0.00) | -0.05 (0.00) | 0.01 (0.00) | 0.13 (-0.05) | 0.01 (0.04) | 0.21 (-0.05) | 0.03 (0.04)
11 | -0.37 | 0.01 | 0.06 | 0.02 | -0.29 | 0.03 | -0.60 | 0.06
(): OPERA
Unallowed multipole components small enough.
Issue: large b3 of 18 unit at Straight Section.