## Slide 1
Stoyan Stoynev
US Magnet Development Program
Fermi National Accelerator Laboratory
15 T: Diagnostics and Magnet Test Plan
MDP collaboration meeting
January 16, 2019

## Slide 2: Collaboration efforts
All diagnostics discussed among FNAL-LBNL collaborators
Instrumentation contributions from both FNAL and LBNL
Based on 11 T and CCT experience
The magnet testing will be at VMTF (FNAL)

## Slide 3: Instrumentation - overview
Voltage taps – for quench detection and characterization;
splice resistance measurements
Strain gauges on coils, poles, bullets/rods and shell – strain monitoring during cool down, warm up and quenches to build the full stress picture vs conditions
Protection heaters – for quench protection of the superconducting magnet
  In addition to heaters the magnet is protected by an energy extraction system
Quench antenna – for independent quench characterization
Acoustic sensors - for independent quench characterization
Temperature sensors – outside magnet/coil temperature
VMTF Facility limits
102 channels
for characterization
64 channels
2x2 independent units
(16 input channels)
13 channels (+ reserve)
LBNL (~6 channels)
From LBNL (~4-6 channels)
5 channels
In collaboration between FNAL and LBNL

## Slide 4: Voltage taps and heaters for 15 T coils
{
Layers: 4 3 2 1
Very similar
heaters
insulation
Layers 1 and 2 resemble the structure of a two-layer magnet
  Instrumented in a similar to past magnets way
  Voltage tabs at the inner- and outer-most surfaces of the structure
  Heaters at the outer-most surface
Layer 4 resembles the outer layer of a two-layer magnet (or layer 2 in our case)
Layer 3 is different from past
  Limited number of voltage taps instrumented
11 T
15 T
similar
4
3
2
1
15 T

## Slide 5: Voltage tap schematics
A1
A2
A3
A4
A5
A7
A8
A6
Coil instrumentation (seen from “above”)
A9
B1
B2
B4
B5
B3
B7
B8
B6
C3
C4
C7
C5
C6
D3
D4
D7
D6
D5
D1
D2
C1
C2
Not shown: NbTi-NbTi splices (between coils and coil-to-leads)
All of them will have voltage taps as well
Innermost layers are slightly more instrumented, in particular around the pole where
most of quenches are expected.
Layer 1
Layer 2
Layer 3
Layer 4

## Slide 6: Strain gauges – half bridges where possible
P+ (red)
S- (wht)
S+ (grn)
P- (blk)
ACTIVE GAGE
Bonded in Axial Direction
TEMP-COMPENSATING GAGES
“Floating”
ACTIVE GAGE
Bonded in Transverse Direction
from LBNL 23N928 SPEC DWG
LBNL COIL INSTRUMENTATION
We are using the
typical LBNL SG
configuration where
possible
(coil and bullet gauges
are exceptions)

## Slide 7: Layer 1 pole and coil strain gauges – positions and type
At several inches from the pole block separation
Schematics
There are 8 SG per coil ( ) – all azimuthal.
So 16 active coil SG.
There are 4 SG per coil pole ( ) –
half of them axial, half - azimuthal.
8 pole SG (“half bridge”) in total.
There are 2 more single gauge
(“quarter bridge”) azimuthal gauges per pole for assembly purposes (~same positions as
“half bridges”).
Those are “standard” positions for the
measurements but now we read both
azimuthal/axial directions

## Slide 8: Layers 3-4 pole strain gauges – positions and type
Each groove hosts one azimuthal and one axial gauge.
12 L3 and L4 pole SG (“half bridge”)
L3
L4
4 SG
2 SG
Used for wiring
Locations were discussed
with LBNL.
16 skin SG (“half bridge”) and 18 bullet SG (including TC) will also be instrumented.

## Slide 9: Wiring – “traces”
Traces: 25 m SS on 1 mil Kapton; etched
Incorporate heaters and wiring for VT and SG
  Minimal distance of 2 mm between
  VT strips and 5 mm from heaters
All wiring for coils 2, 3 and 4 goes
through the traces on layer 2 and 4
Wiring for layer 1 is “old-fashioned”
  Traces in layer 2 and 4 carry the coil voltage/strain gauge signals and make the heaters
Layers: 4 3 2 1
heaters
insulation
Developed together with LBNL

## Slide 10: Quench antenna
Two types of quench antenna
  “Conventional” (used in HD magnets)
  It will be supplied by LBNL
  It will be inserted in the warm bore (warm finger)
  “Trace” (flexible; first successful test in a MQXF magnet)
    80 mm long coils on a trace
    To be attached to the cold side of the warm finger
Non-continuous coverage
  Seven wire wound sections separated by 14 cm (23 mm OD)
  Traces will cover both sides of a coil, ends + the straight section (close to the trasition region) for both innermost coils : 3 x 4 = 12 channels
~ 3’’
“Trace” QA tested
in MQXFS1
Warm finger radial dimensions: 1.25” (31.75 mm) OD Tube x .035” wall or ~ 1.18” (~ 29.97 mm) ID.
Sketch of the
assembled quench
antenna
and photo of the
antenna sections

## Slide 11: Acoustics
New improved electronics and sensor options allow
to use the technology in difficult locations
1 MHz aquisition rate for the DAQ
Locations – on the end parts (pusher plate) and skin
  Likely four sensors on the end parts (reading only two)
  Three or six sensors on the skin (reading only three),
  close to the magnet center axially and
  separated by 120o azimuthally
Installation will be after magnet assembly
Sensors and
adjacent electronics
All supplied by LBNL
Location of sensors on
the pusher plate (the other
displaced 180o azimuthally)

## Slide 12: Magnet Test Plan Overview
At 300 K
  Electrical Checkout, including RRR measurements before cool down
  Hi-pot schedule: Coil to ground (with heaters grounded or floating) at 1000 V, protection heater to ground (with coils grounded or floating) at 1000 V
  Magnetic measurements
At 4.5 K
  Electrical checkout and quench detection checkout, Hi-pot
  Manual trip at 1000 A
  Protection heater provoked quenches at Imax ≤ 5 kA
At 1.9 K
  Magnetic measurements up to 5000 A (before training)
  Quench training at 20 A/s, or at mixed ramp rates (start at 50 A/s and then continue at 20 A/s)
  Quench ramp rate dependence study (10-400 A/s)
  Voltage Spike Analysis for training and ramp rate quenches
  Magnetic measurements
  Quench temperature dependence study at 20 A/s
At 4.5 K (after 1.9 K)
  Check quench plateau at 20A/s, or at mixed ramp rates (start at 50 A/s and then continue at 20 A/s)
  Magnet inductance measurement at 50 A/s and 300 A/s
  Splice resistance measurements
  RRR measurements (cold at warm up)
At 300 K
  RRR measurements after warm up

## Slide 13: Magnetic measurements
Z-scan, 300 K (10 A)
Z-scan at 5000 A (~half of expected current)
(after quench training)
Z-scan at injection current (FCC)
Z-scan at ¾ current reached
Z-scan at Imax – 500 A
“Stair steps” measurements (500-1000 A steps)
“Loops” measurements (20/40/80 A/s)
Accelerator profile (FCC/LHC/...) measurements
The full plan will be finalized in the Test Readiness Review before magnet testing

## Slide 14: Summary
Instrumentation plan developed with LBNL
  Based on previous experience and succesful tests
  All steps in the plan being completed
Non-invasive techniques massively applied
Magnet test plan draft based on previous experience
  To be finalized during the forthcoming Readiness Review

## Slide 15: Back up

## Slide 16: Magnet safety
MIITs budget:
conservative
estimates for various
failure scenarios
Vittorio M.
and Stoyan S.

## Slide 17: Skin and bullet strain gauges
16 skin SG (“half bridge”).
Example from 11 T models
Two positions (~ 70 cm apart longitudinally) around the magnet center to be instrumented
- At 75o and 45o
- Azimuthal and axial gages
- Two opposite sides of the magnet circumference
bullet
15 T model
Instrumented
skin gages
There are 8 bullet holes on the LE and 10 bullet holes on the RE
- A bullet is instrumented with 2 SG
- One TC on each side of the magnet
- Only part to be instrumented
18 bullet SG (including TC).
Bullet
with
SG
Those are all “standard” positions

## Slide 18: Protection heaters
Protection heaters cover layer 2 and 4
  25 m SS in four strips over the
  lenght of the coil
  23/32 mm widths at layer 2
  25 mm widths at layer 4
  The low field region is supplied with higher
  power density at same current (smaller width)
  In 11 T we had 21.5 vs 26 mm heater widths
  (low/high field regions)
They cover 60-80% of the layer coil surface
Together with the dump resistor heaters are enough to protect the magnet
Layers: 4 3 2 1
heaters
insulation

## Slide 19: DAQ channels
Voltage Taps: 50 coil channels to use
  Splices will take about 10 more channels
  102 channels available (the “spare” ones can be used for other type of data –
  a back up option)
Strain gauges – all 64 channels to use
  All gauges as discussed except: 10 skin SG (“half bridge”) instead of 16
  One half of the skin will be fully read, and the other will have a single station (azimuthal, longitudinal readings) read out – 10 channels in total
Protection heaters: 12 channels to use
  Includes the additional (non-trace) heaters – see later
  There are still four spare channels
Quench antenna – 12 dedicated channels to use
  There are 13 available
  Several additional independent channels will be read by the independent LBNL DAQ
  (high rate)
Acoustics – between 4 and 6 channels
  The whole measurement system will be provided by LBNL
  High read-out rate (1 MHz)

## Slide 20: Documentation
Magnet description
  The draft of the document is prepared and resides
  in the usual test folder (in Run Support area:
  S:\Run Support\VMTF\LIST_of_MAGNETS\15Tdemonstrator)
  It contains the usual information for this type of document
Check-out forms
  Being generated during the coil instrumentation process
  Once the magnet is assembled “official” forms for the magnet are to be generated (consistent between IB3 and IB1 as for each magnet tested so far)
  All reside in the Run Support area
Presentations
  This and previous presentations serve as status updates
  Information of various types was/is provided
Drawings
  Traces were fabricated based on drawings available in Teamcenter
  (F10071120 and F10071151)

## Slide 21: Risks and mitigation
Magnet protection in case of heater failure
  We are to install four more heaters (8 strips, similar to 11 T)
  in layer 4 over the traces (Kapton insulation)
  Existing heaters need 8 channels and we have 16 (enough)
Voltage tap failures
  Two quench antenna and acoustics (all non-invasive techniques) will help with reducing the risk of quench localization failures, especially in the innermost layer
Temperature sensor failure
  We typically need two properly positioned sensors for safe cool-down
  and we’ll have five
  There are more back up readings from facility measurements
  (not as acurate for the magnet)