## Slide 1
V. Nagaslaev
Muon Department
November 1, 2018
Mu2e Resonant Extraction in Operations

## Slide 2: Why Slow Extraction for Mu2e?
Detectors will not be able to digest all intensity in one pulse
Instead - 25,000 m-pulses from one 1e12p bunch during 43ms (spill)
Timing between m-pulses is 1.7ms – ideal for Mu2e

## Slide 3: Beam Intensity diagram in RR and DR

## Slide 4: Mu2e Slow Extraction in the Delivery Ring
Parameter | Value | Units
MI Cycle time | 1.4 | sec
Number of spills per MI cycle | 8 | 
Duration of each spill | 43 | msec
Number of protons per micro-pulse | 3.9x107 | protons
Maximum DR Beam Intensity | 1.0×1012 | protons
Reset Time Gap between spills | 5 | msec
Operation point (Qx/Qy) | 9.650/9.735 | 
Extraction efficiency | >98 | %
Spill uniformity | <50 | %
Notes: At the pulse-pulse level, the intensity variations should not exceed 50% of average.

## Slide 5: Motion in ideal linear machine
Non-perturbed machine
Horizontal tune

## Slide 6: Nonlinear fields
Magnets are not ideal
Dedicated multipoles:
  Chromaticity sextupoles in DR
  Correction sextupoles in ACC
  Multipole magnets in ACC
  Skew sextupoles in ACC
Dynamic aperture
Resonances
Machine operating point (tunes)
Debuncher tune diagram (P195)

## Slide 7: Sextupole field
What happens near sextupole resonance
Horizontal tune
1st ISA magnet
Notes: Addition of Sextupole field
Ellipse shape changes
Most importantly: dynamic aperture: unstable region
Size of stable region can be controlled
Delta and G factors
ISA sextupole: started receiving

## Slide 8: Beam Phase Space Formation in the Ring
Moving machine to the resonance: extraction starts
Notes: When squeezed, part of the beam becomes unstable
Drifts along branches
Intercepted and kicked
Different from one turn kick!

## Slide 9: Circulating and Extracted Beam at Upstream End of ESS1
Cathode
Foil Plane
Clearing Electrode
60 mm
E
-100 kV
Beam center
S.Werkema
Notes: Beam shape deceiving
Circulating part and unstable parts
Kick in ES field

## Slide 10: Beam Phase Space Formation in the Ring
Notes: The initial part of the squeeze is skipped

## Slide 11: Simple cartoon of extraction
Q=2/3
Beam
A
Stop-band
Qh
Notes: Beam tune
Stop band opening
Dynamic aperture
Continuous extraction

## Slide 12: Traveling in tune space
Tune scan in Debuncher, July 2010 - B.Drendel
Tune diagram, up to 8th order
BD, 2010
Mu2e, SX
Notes: Search for non-linear resonances
Only 3rd order can be seen
3rd order is not harmful – will clean it up AND move away from coupling
5th order is touched, not seen (0.600) AND we are far away from it
4th order interesting, but not touched
Mu2e path is in safe place, but could be issues with 4th order!

## Slide 13: Mu2e Resonant Extraction – General Map
SS10-60
SS40-50
SS20-30
RFKO kicker
Tune ramp quads (3)
Sextupoles (2x3)
ES septa (2)
DEX bump trims (4)
RFKO kicker (1)
Spill Monitor (1+1+1)
Spill Regulation (NS)
Skew quads (2)
Notes: SX elements
Most (except of SRS and SQ) are shown in photos here

## Slide 14: Driving the H-tune to the resonance
Spill Ramp (FF regulation -JPARC)
Spill Ramp (FF regulation – Synergia)
Beam squeeze by the tune ramp
CQA magnet for tune ramping (3)
DQ~G
Notes: Tune change proportional to the gradient
If the gradient is ramped linearly – non linear spill
Will learn out the correct curve
Variations: slow and fast
Will try to regulate variations as much as possible with quads, same SRS
Limitations of FB regulation with quads

## Slide 15: Spill Regulation with RF Knock-Out (BL)
Transverse RFKO- fast betatron beam heating
Will be used for the regulation of fast spill ripples.
  Very effective in medical applications
  It’s cheap (reusing hardware)
Needs special waveform: FM and AM
Did studies for the EGR (emit. growth rate)
Potential problem: can only heat the beam, can not inverse heating
Notes: Principle of RFKO regulation
Why RFKO
Modulation
What we learned so far
Potential problem

## Slide 16: Spill Monitoring
Wall Current Monitor at SS-50
Also:
DCCT
Extinction Monitor (Main)
Extinction Monitor (U)
Notes: Spill Monitoring
First device – WCM, will be available immediately
Is it used in g-2?
Others

## Slide 17: Orbit control at extraction
NDB trim magnets:
H206
H301
H305 moved from 302
H209 new
H206
H209
H301
H305
ESS
Notes: Horizontal extraction orbit is controlled by 4 fast dipole correctors, NDB type.
1 moved, 1 new; all moved to optimal placements as much as practically convenient
Shown is H301

## Slide 18: Why dynamic orbit bump
Max deflection angle is 0.4mR
Notes: Most important – dynamic bump
Phase diagram: angle at septum is changing during the spill
Max angle 0.4mR

## Slide 19: Dynamic orbit bump
ΔImax=7A
Q203 X=0; X’=4mR
Q205 X=5.3mm X’=0
Q301 X=-5mm X’=0
Q303 X=-5.3mm X’=0
Notes: Initial bump design made in OptiM
Fine adjustment by variation analysis in Synergia
Large deviations
Static counter bump

## Slide 20
Extra Slides

## Slide 21: SX operation sequence
Inject beam into the resonance
  Sextupoles always ON
  ESS and LAM/CMAG always ON
  DEX correctors: at nominal
  Tune ramping quads at zero
  Note: SX is sensitive to injection errors
Squeeze (43ms):
  Ramp up tune quads and DEX bump
Reset (5ms):
  Reset back tune quads and DEX bumps
Abort any beam left-over

## Slide 22: What’s important for SX
  Monitoring losses: local & distributed
  Septum alignment
  Dynamic bump
  Chromaticity control
  Separatrix alignment – orbit studies
  Maximum aperture
  Minimum emittance
  Coupling!
  Optics
  Etc.

## Slide 23: Important diagnostic
Fast tune tracking
BPM: COD and TBT at 2.36MHz
Loss Monitoring
Emittance monitoring
Beam profile

## Slide 24: BPM orbits
Closed Orbits:
Bumped orbits change, non-linear corrections
Cusped at sextupoles
Need for lattice studies
Turn by Turn Orbits:
With sufficient bumping, follow the triangle shape in phase space
Information about the resonance strength and phase
Helpful to tune the sextupole circuits
Notes: The initial part of the squeeze is skipped

## Slide 25: Hardware - magnets
Tune ramping quads – installed in 30, 10, 50
  Need new PS (still unknown)
Harmonic sextupoles
  Not installed
  2 families in 60 and 50
  Issue in 50
  Issue in 10
  Need new PS (still unknown)
Skew quads
  In place (60)
  PS are there
  Need to re-cable
DEX bump magnets
  In place
  Need new PS (coming)

## Slide 26: Hardware - other
ESS installation
  At Q203 (left & right)
  Will be the latest
  Quick access & maintenance
  Vacuum
ESS HV PS
  In AP30
  Will start moving soon
ESS Fluorinert skid
  In AP30
  Pending Construction funds
Spill Regulation System
  In AP30

## Slide 27: List of studies BEFORE ESS installation
    Improving beam lifetime
    RF studies
    Beam transport, matching beam lines
    Injection errors
    Establish tune tracking
    Tune ripples
    Chromaticity
    Ramping quads *
    Sextupole resonance:
      Sextupole phase tuning; orbit distortions;
    Aperture studies and improvements
    Loss monitor commissioning and studies *
    Optics measurements/Lattice improvements
    DEX bump studies: bumps, ramp, leaks
    X-Y coupling, skew quads
    Emittance monitoring
    Beam profile monitoring?
    Machine protection modes