## Slide 1
Ihar Lobach (UChicago)
Budker Seminar
Monday November 12th, 2018
Quantum effects in undulator radiation: Proposed experiments and results of theoretical analysis
Thesis advisors:
Sergei Nagaitsev,
Giulio Stancari

## Slide 2: Outline
Introduction
How to get a single electron in a storage ring
Theoretical predictions for undulator radiation produced by a single electron
Experiment ideas for IOTA

## Slide 3: Introduction
Quantum effects in undulator radiation: 1) quantized radiation (more than one photon can be emitted per pass) 2) quantum nature of electron (electron wavefunction’s size may be considerable)
Undulator radiation:
When we detect two photons we want to be sure that they were produced by the same electron
We need to keep a single electron in the ring

## Slide 4: IOTA ring: first beam Aug 21, 2018
A 40-m ring (electrons and protons)
Design beam energy: 150 MeV (electrons)

## Slide 5: A proposed experimental setup in IOTA
We have two undulators that we
can borrow, from SLAC and JLab
Both have 55mm period.
(N=11 and N = 30) Variable K.

## Slide 6: Single electron in a storage ring
Experiments in VEPP-3 in Novosibirsk (1993):
Metrology Light Source (MLS) in Germany (2008):
Mechanical scraper
SR intensity measurement by cooled photodiodes
Reducing RF voltage for a moment
SR intensity measurement by PMTs

## Slide 7: Single electron in IOTA 100 MeV (2018)
In this specific case they were simply waiting as electrons were lost due to residual gas.
Beam current was measured through synchrotron radiation detected by a PMT. Also by cameras.

## Slide 8: Single electron injection
Block laser with shutter to get only dark current
Insert several OTR foils in LE and HE lines
Decrease last injection quadrupole to stretch phase volume and distort incoming trajectory
*Sasha Romanov’s slide

## Slide 9: Single electron capture probability
To test selected method of intensity attenuation 53 injections were done with interval of 21 seconds
Resulting probability of single electron injection: 32%
  For purely Poisson distribution maximum probability is 36.8%
*Sasha Romanov’s slide

## Slide 10: Theoretical predictions for undulator radiation produced by a single electron
Two models were considered:
  QED approach with Dirac-Volkov solution (classical undulator field + quantum electron + quantized radiation)
  Glauber’s approach (classical current + quantized radiation)
* figure from http://old.clio.lcp.u-psud.fr/clio_eng/FELrad.html
Differential rates?
Photons’ arrival times?
Dirac-Volkov approach has already been used for electron in constant uniform magnetic field
Multi-photon emission
Formation length in uniform field
For undulator, formation length will
be the entire length of undulator

## Slide 11: Theoretical part; General remarks
The probability to detect a single photon of any energy at location at time is given by correlation function of first order
The probability to detect two photons at location at times and is given by correlation function of second order
If there is a filter, then only allowed components of electric field operator should be left with corresponding weights. If there is a filter with infinitesimal band, then the time dependence is lost (plane waves occupy all space) and for single photon and classical current we get
If the electron is quantum the trace is also calculated over electron’s states and the usual QED matrix element will emerge in the calculation
One can obtain similar results for two-photon differential rate.
electron + undulator + radiation
interaction
*introduced by R.J. Glauber

## Slide 12: Dirac-Volkov model
Volkov states are exact solutions of the Dirac equation for electron in plane electromagnetic wave
Positive and negative energy solutions:
Where
How is it related to an electron in an undulator?
Weizsäcker-Williams approximation
In electron’s rest frame undulator’s field looks like a plane wave
*this problem has been considered in dissertation of Daniel Seipt
*these are spinor functions

## Slide 13: Dirac-Volkov model
Takes into account:
Quantum nature of radiated field
Quantum nature of electron, i.e.
  Finite size of electron’s wavefunction
  Electron’s spin
Furry picture
*see Daniel Seipt’s dissertation
Single-photon emission
Two-photon emission

## Slide 14: Crucial parameters
Field strength parameter (undulator parameter)
Quantum parameter (electron recoil parameter)
Scattering amplitude can be conveniently decomposed as a series in powers of
*see E. Lötstedt and U.D. Jentschura Phys Rev A 80, 053419 (2009)

## Slide 15: Differential rates in Dirac-Volkov model
Single-photon rate
Basically this is a classical result for . See for example V.I. Ritus, Journal of Soviet Laser Research 6.5 (1985): 497-617.
Two-photon rate
For , I obtained
which agrees with classical results from Jackson and, for example, V. Kocharyan and E. Saldin, arXiv:1202.0691v1
where
*a factor of ½ will emerge after integration over a detector

## Slide 16: Differential rates in Dirac-Volkov model
Single-photon rate
Two-photon rate
Factorization of two-photon differential rate means absence of correlation between the two photons. To increase correlation one has to increase . Is it at all possible to see correlation on experiment? Yes:
In D. Seipt and B. Kampfer, Phys Rev D 85, 101701(R) (2012):
*a factor of ½ will emerge after integration over a detector
Optical undulator:
Spin does not change. Essentially electron can be regarded as spinless
Energy spectrum for two-photon emission for on axis photons
Exact solution The factorized form
*some difference can also be seen at 150 MeV and optical undulator
FACET-II parameters:
Color represents
differential rate:

## Slide 17: Glauber’s model
Takes into account:
Quantum nature of radiated field
Assumptions:
Negligible electron recoil (classical current)
Classical current
Operator
Displacement operator (creates coherent state):
Final state is a coherent state:

## Slide 18: Glauber’s model: results for correlation function
For infinitesimally thin filter (spectral correlation function):
Definition of correlation function from the beginning of presentation:
- classical result. See for example V.I. Ritus, Journal of Soviet Laser Research 6.5 (1985): 497-617.
Some noteworthy properties:

## Slide 19: Part 2: Ideas for experiment in IOTA
  Measurement of difference of arrival times of two photons in two-photon emission
  Is photon statistics Poissonian? (for number of emitted photons/in time)
    Experiment with two PMTs with non-overlapping filters. “Violation” of Poisson statistics
  Experiments with a 2D array of single photon detectors (Correlation/entanglement in emitted photon pairs?)
  Experiments with undulators of different lengths (peak intensity if the formation length is equal to undulator’s length)
  Other vague (for now) ideas

## Slide 20: Two-photon events: time spread
Capabilities of presently available PMTs:
Classical formula from Jackson:
TTS=
Experiment idea #1
*S.V. Faleev in arXiv:hep-ph/9706372v1 found for dipole radiation
It’s important to have two photons, because it is easier to measure , then absolute time of arrival of a photon

## Slide 21: Hong-Ou-Mandel interferometer
The original HOM interferometer (1987):
Later papers (2018), Attosecond-Resolution HOM interferometer:
Measured Accuracy
Never used for synchrotron radiation before!

## Slide 22: Hong-Ou-Mandel interferometer: theory
One photon at each port of a beam splitter:
HOM signature:
For two indistinguishable photons:

## Slide 23: HOM interferometer for undulator radiation
PMT2
Coincidence Counting
PMT1
Attosecond time resolution
We will be able to see what is longer: photon or electron?
Older Novosibirsk’s experiment in VEPP-3:
1 ns time resolution.

## Slide 24: Photon counts estimates
Parameter | Value
IOTA circumference | 40 m
Turns per second | 7.5 MHz
Electron energy | 150 MeV (up to 200 maybe)
Undulator length | 60 cm (SLAC)/1.8 m (JLab)
Undulator period | 5.5 cm
Photon energy | 2.6 eV
Photon wavelength | 475 nm
SRW simulation for 200 MeV electron and 60 cm undulator:
PMT’s QE
Expected
Single-photon counts:
Two-photon counts:
But we need to exclude dipole radiation:

## Slide 25: Suppressing dipole magnet radiation
Small aperture detector:
Narrow filter:
System of lenses:
Dipole radiation is defocused.
Undulator radiation is focused.
Vertical orientation of undulator + polarizer
Polarizer
*Also, with HOM interferometer we might actually be able to resolve dipole photons and undulator photons in time. So we do not really need to suppress dipole radiation.

## Slide 26: Photon statistics
Emission probabilities form Poisson distribution:
An idea on how to “violate” Poisson statistics:
Experiment idea #2
PMT1
PMT2
Filters with non-overlapping
energy bands
Experiment idea #3
Beam splitter
If probability to detect a photon in PMT1 is and probability to detect a photon in PMT2 is , then the probability to detect one photon in each PMT will be , not (which would be true if the filters were identical)
Also does distribution of emissions
in time correspond to Poissonian?
(for single-photon and for two-photon
events)

## Slide 27: Experiment with 2D array of single photon sensors
It will allow us to measure the angle at which a photon is detected
It will be possible to see if there is any correlation between these angles in emitted photon pairs
Also experiments aimed at polarization correlation in photon pairs may be done
Example: Large Area Picosecond Photon Detector
Experiment idea #4
There is some correlation and entanglement for optical undulator (much bigger ):

## Slide 28: Length of formation of radiation
A bunch of electrons can be used for this experiment
Experiment idea #5
Has it been done before?
If formation length is shorter than undulator:
We might have two undulators (SLAC/JLab) of different lengths to check the square law.
One cannot determine formation length with big detector because after integration over the detector the dependence on length is linear:
here
If formation length is shorter than undulator:
Small aperture/small energy band detector:

## Slide 29: Other ideas for experiment
Develop a barrier across separatrix. Split separatrix into two islands. Control width of the RF barrier. What is the probability of a single electron tunneling through the barrier into the 2nd separatrix? (Timur Shaftan’s idea)
We can do something like Hanbury-Brown and Twiss experiment for interference of light coming from far away double-stars, but for two electrons in an undulator. (Bernhard Adams’ idea)
Experiment idea #6
Experiment idea #7

## Slide 30: Optical stochastic cooling with single electron
*figure from Andorf, Matthew et al. Phys. Rev. Accel. Beams 21 (2018) no. 10
At certain delay the probability to emit a photon will be zero!
Experiment idea #8

## Slide 31: Conclusions
It is possible to keep a single electron in IOTA
Electron recoil and spin effects are negligible
Glauber’s model with classical current is sufficient
Still, electron wavefunction’s size may be measurable
Difference in time of arrival of photons in a photon pair can be measured with unprecedented accuracy (attosecond). We can determine what is longer: photon or electron
Photon statistics (number distribution/independence in time)
Transverse correlations can be tested with 2D array of single photon detectors
Experiments with small aperture/small energy band detector for formation length of radiation
RF Barrier tunneling/ Hanbury-Brown and Twiss interferometer for two electrons
Theoretical predictions:
Ideas for experiment:

## Slide 32
Thank you for your attention!