## Slide 1
Ben Freemire
FAST/IOTA Department Meeting
November 16, 2018
Run Coordinator Report

## Slide 2: Monday
Morning:
  Controlled access
    Leak check & RGA scan
      Highest peak on RGA was water (as expected)
      Need to perform more thorough leak check
D604 reversing switch replaced
  Reported that firing circuits had been wet at one point due to rust on circuit board screws
Afternoon:
  During startup, some oscillation noticed on flattop of CC2, cavity tuner and feedback gain adjusted to minimize
Evening:
  Controlled access made to align cameras and connect PMTs
    PMTs ready, last camera (M1L) not properly working

## Slide 3: Tuesday
Morning:
  CM cavities retuned (4)
Afternoon:
  BPM firmware updated
Evening:
  Closed orbit & lattice corrections

## Slide 4: Wednesday
Morning:
  BPM firmware tested
Afternoon:
  BPM data analyzed
  Beam centered on sync light cameras
  RF tuning to understand phase oscillations, frequency centered so that N:IRFMOD now 0
Evening:
  BPM work finished

## Slide 5: Thursday (Moving Day)
Morning:
  Discovered that Q114 & Q116 not datalogged; Now on NML: 1 min
  Controlled access to
    Connect RF probe
    Realign mirror on M1L
    Adjust focusing stages to regain range
Afternoon:
  Coincidence trigger module tested at ESB to provide 7.5 MHz sync trigger for BPMs based on clock $A5 with moderate success
    All BPM TBT data collected in one output array
    Work still to be done
Evening:
  M1L camera repositioned to find beam
  Orbit corrections
  Injection routine tested post-D604 switch replacement
    MPS needs to be updated to correctly account for switch position

## Slide 6: Friday
Morning:
  Problem injecting into IOTA as a result of CC1 energy different from previous days even though settings are the same
    CC1 energy lowered and injection works fine
  Bearing on dry pump of north fridge replaced
  Elements of nonlinear magnet connected to power supply

## Slide 7: FAST/IOTA: Next Week
Normal Monday Morning Controlled Access:
  Contact RunCo Ben Freemire with all requests
    No requests yet – vacuum needs 6-8 hours to perform a thorough leak check
Update BPM software (per Nathan Eddy):
  Fix issues with current readout (John)
  Implement scheme to request stored beam TBT (orbit TBT) via system state device (John & Chip)
  Implement stored beam kick measurements (after Thanksgiving)
Work on commissioning of nonlinear magnet
  First using sync light cameras, then with addition of BPMs when available
Thanksgiving holiday – limited personnel
  Assuming no Department meeting next Friday, next RunCo is Jonathan – send him requests for week beginning 11/26