## Slide 1: FAST Facility Department: ~ Past Week
No accesses this week
Priorities:
  Resolve IOTA BPM issues for turn-by-turn data
  Resolve IOTA RF-noise issues
  Demonstrate successful operation of horizontal kicker
  Complete full injection routine: delivery to HE dump
Continued commissioning of IOTA BPM system (turn-by-turn): extensive work on the triggering system
Investigating noise in IOTA’s RF system
Some limited beam-based RF calibration and emittance studies on the LE beamline
Notable Achievements:
  Achieved limited turn-by-turn BPM functionality
  Powered the nonlinear magnet for the first time last week; very strong effect on beam
  Used horizontal kicker to ping the beam for the first time
  Demonstrated vertical kicks without beam loss

## Slide 2: FAST: Issues This Week
Frequent trips of IOTA quads (all on right side of the ring) based on erroneous temp readbacks.
  Suspect module that feeds temps to PLC for the right side of the ring
  Issue progressively worse (# of quads and freq.) as the week progressed
  Discovered that IOTA magnet flows and temperatures weren't in the data logger; resolved
Mark Averett diagnosed issue and affected repairs; replaced 16-ch input module…working fine now

## Slide 3: FAST: Next Week
Normal Monday Morning Controlled Access:
  Contact FAST RunCo, Jonathan Jarvis, with all requests
MPS firmware update and validation; requires ~15-min downtime, but ~1hr of online testing.
RF-noise investigations continue; access on Mon. to gnd cav.
Nonlinear-magnet studies contingent on BPM work
Complete full injection routine: delivery to HE dump
Low-emittance lattice implementation and optical diagnostics testing; access on Mon. to install polarizer and bandpass filter in a sync.-light station: which station is best?