## Slide 1: FAST Facility Department: This Week
Multiple accesses for IOTA RF & diagnostics work throughout the week
Went supervised access on Wed. afternoon for AAC tour
Dropping interlocks on the FAST catwalk this morning for crane ops.
Priorities:
  Improve IOTA BPM noise level
  Resolve IOTA RF-noise issues
  Complete full injection routine: delivery to HE dump
Thorough inspection of IOTA RF system; tested with different generators and LLRF setups; repaired damaged connector & stub-tuner hardware
Ongoing BPM work to reduce noise; access today to test a preamp
Worked on delivery to HE dump, but ran into issues with BPM electronics
Notable Achievements:
  Stable BPM turn-by-turn functionality in two triggering modes (injection & on demand)
  Assembly and QA for first batch of sextupole yokes
  ~30x reduction in PMT background; important for single-electron experiments
  Achieved <20 min start-up time for FAST+IOTA

## Slide 2: FAST: (minor) Issues This Week
North-compressor manifold temperature alarmed; system opened water valve to 100%
Compressor body and piping felt room temp when touched
Was determined to be a sensor failure & replacement resolved the issue.

## Slide 3: FAST: Next Week
Normal Monday Morning Controlled Access:
  Contact FAST RunCo, Jinhao Ruan, with all requests
Next Week’s Priorities:
  Focused campaign on BPM performance continues
  Continue RF-noise investigations
  Nonlinear-magnet studies contingent on BPM work
  Resolve BPM issue in FAST HE-dump line and complete full injection routine
  Parasitic studies with linac and IOTA as able