## Slide 1
Vladimir Nagaslaev
US/Japan Collaboration Meeting, SLAC
14 January, 2018
FNAL SE Overview and plans for Mu2e

## Slide 2: Beam Facilities at Fermilab
Proton Source
Recycler
Main Injector
Muon Campus
Ext. Beamlines

## Slide 3: Main Injector Slow Extraction Program
Three main user areas for slow spill beam:
1 – Mtest (Detector development)
2 – Mcenter (Detector development)
3 – Neutrino/Muon Hall (SeaQuest/Drell-Yan experiment)
1
2
3
The Fermilab Main Injector :
120GeV/c
53MHz RF structure
588 RF number
486 bunches @ 2e10 ppb
4 second slow spill

## Slide 4: Main Injector Slow Extraction Program
Particle extraction occurs through two 3 meter electrostatic septum
Each septum uses 0.1mm Tungsten (75%) Rhenium (25%) wires to isolate circulating protons from the high voltage extraction field region of the septa.
We have experimented with 0.05mm wire septa. Extraction losses were reduced as expected but the wires experienced a high failure rate.
Field Free
Region
Wire plain
100 Kvolt
cathode
14mm
Extraction
Gap (14mm)

## Slide 5: Muon Campus
Delivery Ring
G-2
Mu2e
Booster
Recycler/Main Injector

## Slide 6: Mu2e Experiment
Beam Flash
Stopped -
Signal
Mu2e proposes to measure the ratio of the rate of the neutrinoless, coherent conversion of muons into electrons in the field of a nucleus, relative to the rate of ordinary muon capture on the nucleus:
Mu2e TDR, arXiv:1501.05241
Single event sensitivity ~ 3*10-17
Improved sensitivity by ~4 orders of magnitude
Positive result = Evidence of new physics

## Slide 7: Muon Campus Slow Extraction Program
Mu2e Beam specs
Pulsed beam structure period | 1.69msec
Intensity per spill | 1e12p
Average beam power | 8kW
#spills in 1.4 sec MI cycle | 8
Duty factor (time) | 25%
Spill length | 43ms/spill + 5ms reset
Efficiency | >98%
Spill uniformity | <±50%
Uniformity Duty Factor | 93%

## Slide 8: Legacy Debuncher Ring (aka Debuncher)
Lattice functions in 1/3 of the Debuncher
(original design)
  Strong focusing, space constraints
  Max beta = 15m
  Machine acceptance = 36 p-mm-mr
  Light enclosure shielding
  Vacuum > 1e-8 Torr
Parameter | Value | New Value
Circumference | 505m | 
# of FODO cells | 57 | 
Max beta | 15m | 
Operating point | 9.763/ 9.769 | 9.650/ 9.735
Max Intensity | 3e8 | 1e12 p
Acceptance (unnorm.) | 36 pm | 
Parameter | Value | New Value
Circumference | 505m | 
# of FODO cells | 57 | 
Max beta | 15m | 
Operating point | 9.763/ 9.769 | 9.650/ 9.735
Max Intensity |  | 1e12 p
Acceptance (unnorm.) | 36 pm | 
Installed
Installed
Built

## Slide 9: Mu2e SE: Extraction Region SS30-20
Space constrained both US and DS – very tight
Conflicts with the g-2 EKIK
No good space to place a collimator
Need local in-tunnel shielding
ESS1
ESS2
Elevation view
SS-30
SS-20

## Slide 10: Electrostatic Septum: Geometry
Q205
MS1
MS2
Q204
Q203
Q202
ESS2
ESS1
2mR total kick
L1<L2
Two modules – “interchangeable”
Diffuser in ESS1
Small phase advance to MS1
1.75m
1.25m
Elevation view

## Slide 11: Electrostatic Septum: Technical Specs
Production of the Full Scale prototype in progress
Infrastructure is in place:
    Tools
    Clean room
    HV testing cave
    Transportation cart, foil cleaning, measurement station, assembly fixtures. Etc.
Details in Matt’s presentation tomorrow

## Slide 12: Spill Regulation system: started implementation
Completed the Construction Readiness Review
Board testing began
Details in Aisha’s presentation later today

## Slide 13: Schedule
G-2 run ends mid FY2020
Commissioning of the beam line with single turn extraction after 2020 shutdown
Remove the EKIK and install the ESS, start SE commissioning beg FY2021
Operations taking over mid FY2021