## Slide 1: Spill Regulation at J-PARC Main Ring Slow Extraction
2019-1-14 US-Japan Meeting
Ryotaro Muto

## Slide 2: Contents
・Introduction : J-PARC MR slow extraction
and purpose of the spill regulation system
・Spill feedback system
・Transverse RF system
・Another approach : Ripple canceller
・Attempt for further improvement of spill regulation system
(with machine learning?)

## Slide 3: Purpose of the spill regulation
One of the main issues of slow extraction
at J-PARC Main Ring
: Improvement of the spill structure
Large current ripples of the main power supplies induce
spiky time structure of the extracted beam
We want to reduce the time structure and produce flat beam
time
intensity
~2s

## Slide 4: Slow extraction using 3rd-order resonance
Horizontal phase space
at a certain position in ring
Excite 3rd-order resonance using sextupole magnets phase space is divided into
stable region and
unstable region
・Particles with large amplitude become
unstable and their amplitudes
increase turn by turn until excess the
septa of ESS and extracted
・Gradually make dn small
 particles are slowly extracted
ESS
S : strength of
sextupoles
Size of stable region
Unstable Region
Stable Region

## Slide 5: Slow extraction using 3rd-order resonance
Instantaneous rate of the extraction beam is
roughly proportional to
(ddn/dt) * (particle density around the separatrices)
The time structure of the extracted beam is determined by the time structure of the dn
Current ripples of the main magnet power supplies
are harmful to the time structure of the extracted beam.

## Slide 6: Current Ripple of the Magnet Power Supply (PS)
600 Hz
1.2 kHz
1.8 kHz
Ripples by the switching and rectification
Time [s]
DI (Amps)
Current Ripple
Noise enhanced by the feedback properties of the PS system（<200 Hz）
DI / I
From Y. Kurimoto
(J-PARC MR PS group)
FFT

## Slide 7: Extraction without spill regulation
I : beam intensity
〈〉: mean during the extraction
Spill duty factor :
time
Beam intensity
time
Beam intensity
F = 100%
F = 50%
extraction
extraction
beam in ring
spill
Spill Duty Factor : 3%
2s

## Slide 8: Correction to tune ripples
J-PARC MR has tune correction quadrupole magnets, EQ (x2) and RQ
We want to cancel out the tune ripples using these correction magnets
We cannot measure the betatron tune directly during the extraction
Feedback control using extracted beam intensity
(Spill feedback system)
Calculate the tune ripple by the PS current ripple and make correction (Ripple canceller)
Another approach : Smear out the amplitude distribution of the particles
(Transverse RF)

## Slide 9: Spill feedback system
Spill
Beam Intensity
Gate
Start and end of the extraction
Extracted beam intensity
Particle number in ring
Magnet control signal
Spill monitor
DSP
Control Unit
PC
Communication
Board
LAN
sampling :
100 kHz
EQ,RQ magnet
MR
DCCT

## Slide 10: Correction quadrupole magnets
EQ
RQ
t 0.1mm
lamination steel
Ceramics duct
≲100 Hz
Δhtune : 0.011/100A
≲1 kHz
Δhtune : 0.0014/100A
Notes: スペック

## Slide 11: Spill monitor
Near
Far
Vacuum partition (Al, 0.1 mm)
~1m
Proton beam
~0.4 m
Spill monitor : plastic scintillator + PMT
detects secondary particles generated at the vacuum partition in the beam duct

## Slide 12: Spill feedback block diagram
Feedback Gain (Feb. 2018)
  EQ: Ki= 62.89
  RQ: Kp=1.0, Ki= 20000, Kd=0.00002, K=0.75
by T. Kimura

## Slide 13: Effect of the spill feedback
beam in ring
spill
(Trim coils of B&Q magnets are shorted in flat top)
Duty Factor 18%
beam in ring
spill
EQ
RQ
EQ
RQ
OFF
Duty Factor 3%

## Slide 14: Transverse RF
By A. Schnase, T. Toyama,
M. Okada & J-PARC RF group
Increase and smear the betatron oscillation amplitude of the beam
by transverse RF on stripline kickers
RF noise
Generator
AMP
AMP
Beam
3kW
3kW
0.1-100MHz
Solenoids to suppress multipactor effect
Stripline kickers

## Slide 15: Transverse RF
separatrix
Amplitude
Without transverse RF
# of particles
separatrix
Amplitude
# of particles
Transverse
RF
Transverese RF smear the amplitude distribution of the particles in ring
 Beam becomes less sensitive to the tune ripples
stable
unstable (extracted)

## Slide 16: Transverse RF
f ~ 47.47 MHz
Fractional tune ~1/3 Parameters are searched
to maximize spill duty factor
Spill duty factor was improved
to ~50% with 51 kW beam
Time [s]
Time [s]
Freq [MHz]
Fractional tune

## Slide 17: Ripple Canceller
We are now testing ripple canceller to correct tune ripples.
(developed by Y. Kurimoto, D. Naito (J-PARC main power supply group))

## Slide 18: Real-time n correction with the magnet current
①
②
①
Bend Error
→ COD@Sext
②
Quad Error
Conceptual Setup
The correction quadrupole works up to ~ kHz
The DI→Dn conversion is done by FPGA within 10 us (ignorable)
Target frequencies of n correction are less than 200 Hz (5 ms)
DI→Dn
(Real-time !)
Real-time n correction is possible
From Y. Kurimoto
(J-PARC MR PS group)

## Slide 19: Families and Power Supplies
One power supply drives several magnets connected in series. These several magnets are collectively called “a Family”
Ex. Bending Magnets
#mags : 96
#families : 6
#power supplies : 6
Family | Type | #mags
BM1,BM2,BM3,BM4,BM5,BM6 | B | 16
QFN,QDN,QFX | Q | 48
QDX | Q | 27
QFR | Q | 9
QFP,QFS,QFT,QDR,QDS,QDT | Q | 6
SFA,SDA,SDB | S | 27
#Families = #Power Supplies
Magnet Families in J-PARC MR
Used for the n correction
16
From Y. Kurimoto
(J-PARC MR PS group)

## Slide 20: Experimental Setup
A/D Board @ each PS
FPGA /CPU Board @ Each building
DI s from each PS are collected and transferred to another building.
FPGA board for the real-time DI → Dn conversion
A/D board
Issues
Several PSs are separately located at different buildings
The PS of the corrector is located at only one building
DI is digitized and converted to optical signals
From Y. Kurimoto
(J-PARC MR PS group)

## Slide 21: Direct Measurement and Prediction
Real-time Dnx prediction
Time (s)
Time (s)
Reasons for the discrepancy
Not all magnets are included
Prediction is done by not magnetic field but magnet current
dn~0.008 (peak-to-peak) for both prediction and measurement
Similar time structure
Before correction, the real-time prediction was compared with the direct measurement
Direct nx measurement
Similar
Correction can be safely done
From Y. Kurimoto
(J-PARC MR PS group)

## Slide 22
FFT
nx correction
nx measurement with and without the real-time correction
dn around f=100 Hz is by 1/3~1/2 reduced
dn @ f > 200 Hz is increased
From Y. Kurimoto
(J-PARC MR PS group)

## Slide 23
1x10-6
1x10-6
Current Deviation
Magnetic Field Deviation
dI vs dB
Magnetic field at f>200 Hz is reduced by the eddy current
Our system is effective below 200 Hz
Bending Magnet
Quadrupole Magnet
t=2mm
t=3mm
Stainless Duct
Magnetic Pole
dB/dt
Induced B
Duct
Eddy Current
From Y. Kurimoto
(J-PARC MR PS group)

## Slide 24: Spill Duty with the Correction
To see the effect of the n correction, the spill feedback and transverse RF was turned off
The spill duty is defined as (: beam intensity)
FFT
Duty 3.2 %→28.1 %
Spill intensity fluctuation is reduced at f < 200 Hz while enhanced at f > 200 Hz (consistent with n measurement)
From Y. Kurimoto
(J-PARC MR PS group)

## Slide 25: To improve the spill regulation system
Weak points in spill feedback :
・Spill signal cannot be negative
 appropriate spill feedback is difficult especially with large tune ripple
・Delay (~200us) from a ripple in tune to the correspondent beam extraction
Weak points in ripple canceller :
not effective to the components which is not reproduced by the current ripples
e. g.
・Magnet field with high frequency
・Transverse RF
Ripple canceller + TrRF is currently lower performance (~30%) than
Spill feedback + TrRF (~50%)
Further improvement of the spill feedback system with the information of current ripples is possible ?

## Slide 26: Model to predict next value of spill
Δtune by EQ ([t-1], [t-2],…[t-nEQ])
Δtune by RQ ([t-1], [t-2],…[t-nRQ])
Δtune calculated by
Main Mag current ripple ([t-1], [t-2],…[t-nMM])
Spill monitor ([t-1], [t-2],…[t-nSM])
model
Predict next value of spill
and determine EQ[t] & RQ[t]
Trial to make a sufficient model
has just begun

## Slide 27: Summary
One of the main issues of J-PARC MR SE is the time structure of the extracted beam.
We currently use spill feedback system and transverse RF system to improve the time structure from ~3% to ~50% in spill duty factor.
We are now testing the ripple canceller, which corrects tune ripples using current ripples of the power supplies.
So far we obtain spill duty factor of ~30% with the ripple canceller.
Further improvement of the spill structure is desirable and we are now searching other possibilities.