## Slide 1: Cable PRR Intro & Charges
Giorgio Ambrosio
Magnets L2
U.S. HL-LHC Accelerator Upgrade Project
Production Readiness Review of the HL-LHC AUP MQXF Cable Fabrication Task 302.2.03
January 22, 2019

## Slide 2: Introduction
The HL-LHC AUP project is expecting CD-2/3b approval in mid-February, and is planning to start MQXFA Cable Fabrication production immediately after that.
Cable fabrication is performed at LBNL, where all prototype and pre-series MQXF cables were fabricated. Cable insulation, performed by external vendor, is included in the Cable Fabrication task and in the scope of this review.

## Slide 3: Introduction
Production Readiness Review (PRR) is a major review step in the HL-LHC Accelerator Upgrade Project (AUP). It is held prior to the start of series production, and is intended to be a largely technical review, but include assessment of the planned cost, schedule, and personnel needs to complete the production.
Scope of PRR:
  - Parts and materials for cable fabrication and insulation
  - Manufacturing and test procedures
  - Interfaces (Internally reviewed on Dec 13, 2018)
Goal of PRR:
  - Approval of plans and procedures for cable fabrication task
  - Validate plan to start manufacturing

## Slide 4: CHARGE I
The committee is requested to answer the following questions:
Scope and interfaces: is the L3 task scope clearly defined and are interfaces with other tasks sufficiently well-defined for executing the series production?
Manufacturing: are the manufacturing work flow documents and travelers —including scheduling, personnel needs, floor space, and facilities requirement—appropriate to execute the series production?
QA/QC: is the QA/QC plan adequate? Are there appropriate documentation for quality control procedures, manufacturing and inspection plan, and data reporting?
Cost and Schedule: are the cost and schedule estimates sufficiently well-defined and of adequate maturity to support the series production?

## Slide 5: CHARGE II
ES&H: Have all hazards been identified and addressed? Are ES&H policy and documentation sufficient for the series production?
Risk: are risks understood and appropriately managed for the series production?
Reviews: are all closeout recommendations for this L3 task from Final Design Review addressed?
Is this L3 task ready for series production?

## Slide 6: Backup Slides

## Slide 7: AUP MQXFA Magnet Deliverables
20 Magnets
  16 magnets for Q1/Q3 to be installed in LHC tunnel
  4 magnets for 2 Q1/Q3 commissioning spares
  (assuming: 4 re-assemblies = post test re-work)
  (assuming: 1 damaged during handling or shipment)
Cryo-assembly
(LQXFA)
Magnet
(MQXFA)
Cold Mass
(LMQXFA)

## Slide 8: MQXFA Performance Requirements
Listed in Magnets FRS
Approved by CERN
Accepted by AUP
  approved July 2017
US-HiLumi-doc-36
Engineering & Equipment Data Management Service (EDMS)
Electronic signature on DocDB

## Slide 9: Performance Requirements (FRS)
Requirements are classified into two groups:
  Threshold requirements (23) are requirements that the project must achieve.
  Objective requirements (6) are challenging requirements that the project should achieve and will strive to achieve.
All requirements are traceable
ID | Description
R-T-01 | The MQXFA coil aperture requirement is 150 mm. This aperture is the coil inner diameter at room temperature, excluding ground insulation, inner layer quench heaters, cold bore, and beam screens. (…)
R-T-02 | The MQXFA physical outer diameter must not exceed 614 mm.
R-T-03 | The MQXFA magnet must be capable of operate at steady state providing a gradient of 143.2 T/m in superfluid helium at 1.9 K and for the magnetic length specified in R-T-04, when powered with current of 17.9 kA.
R-T-04 | The MQXFA magnetic length requirement is 4200 ± 5 mm at 1.9 K.
R-T-05 | MQXFA magnets must be capable of operation in pressurized static superfluid helium (HeII) bath at 1.3 bar and at a temperature of 1.9 K.
R-T-06 | The MQXFA cooling channels must be capable of accommodating two (2) heat exchanger tubes running along the length of the magnet in the yoke cooling channels. The minimum diameter of the MQXFA yoke cooling channels that will provide an adequate gap around the heat exchanger tubes is 77 mm.
R-T-07 | At least 40% of the coil inner surface must be free of polyimide.

## Slide 10: Acceptance Criteria for MQXFA Magnets
Acceptance Plan for Cryo-assembly has 3 parts with Acceptance Criteria:
Acceptance Criteria Part A for MQXFA magnets approved by CERN
  EDMS# 2031083
Accepted by AUP
US-HiLumi-doc-1103

## Slide 11: Acceptance Criteria (with examples)
Based on Acceptance Plan for MQXB magnets (present IT quads at LHC)
Content: Verification Method, Procedure summary and References,

## Slide 12: MQXFA Final Design Report
Final Design Report was reviewed by external team
  Details will be presented by L3s
FDR and Drawings are available on Review website
US-HiLumi-doc-948
Electronic signature on DocDB

## Slide 13: MQXFA/B Main Parameters
Parameter | Unit | MQXFA/B
Coil aperture | mm | 150
Magnetic length | m | 4.2/7.15
N. of layers |  | 2
N. of turns Inner-Outer layer |  | 22-28
Operation temperature | K | 1.9
Nominal gradient | T/m | 132.6
Nominal current | kA | 16.5
Peak field at nom. current | T | 11.4
Stored energy at nom. curr. | MJ/m | 1.2
Diff. inductance | mH/m | 8.2
Strand diameter | mm | 0.85
Strand number |  | 40
Cable width | mm | 18.15
Cable mid thickness | mm | 1.525
Keystone angle |  | 0.4
G. Ambrosio et al., “MQXFS1 Quadrupole Design Report” LARP DocDB 1074
P. Ferracin et al., “Development of MQXF, the Nb3Sn Low-β Quadrupole for the HiLumi LHC ” IEEE Trans App. Supercond. Vol. 26, no. 4, 4000207