## Slide 1
HEBT beam line overview
A. Shemyakin
PIP2IT HEBT Final Design Review
13 February 2019

## Slide 2: Outline
Introduction: PIP2IT in its final configuration
HEBT specifications and scheme
HEBT in operation
Measurements to be carried out

## Slide 3: Final configuration of PIP2IT
Expectations for state of PIP2IT in Spring 2020
  Ion source, LEBT, RFQ, MEBT are in a working shape as they were in May 2018, plus:
    MEBT chopping system is installed and ready to produce a bunch-by-bunch chopped beam
    Downstream portion of the MEBT is assembled particle –free
  Two cryomodules are assembled and RF-commissioned
  HEBT is ready to accept the beam
The main goal: accelerate in the cryomodules a beam that is eventually suitable for Booster injection
  22 MeV x 2 mA x 0.55 ms x 20 Hz to dump; aperiodic bunch structure
Ion source and LEBT
30 keV
RFQ
MEBT
2.1 MeV
HWR
SSR1
HEBT
Dump
22 MeV
10 MeV

## Slide 4: The HEBT goals
The main goal: safely accept the beam from cryomodules
  No beam damage
  No cryomodule contamination by dust or outgassing
Do not create difficulties for future conversion of the PIP2IT cave into PIP-II cryomodule test facility
Also, measure the beam properties to the level of ensuring that there are no large deviations from simulation predictions. While doing that,
  Take into account budget and schedule constrains
  Assume that more measurements will be made after installation of the front end into the PIP-II tunnel

## Slide 5: HEBT specifications (ED0008220)
Table 1: Nominal beam parameters in the HEBT
Parameter | Value | Unit
Ion type | H- | 
Beam (kinetic) energy | 22 | MeV
Macro-pulse length | 0.55 | ms
Macro-pulse repetition rate | 20 | Hz
Frequency of bunches (within macro-pulse) | 162.5 | MHz
Beam current (averaged over 1 µs) | 2 | mA
Nominal charge per bunch | 30 | pC
Beam size (X/Y) at the exit of the SSR1 cryomodule (rms) | 2.2 | mm
Bunch length at the exit of the SSR1 cryomodule (rms), sz | 20 | ps
Table 2: Range of beam parameters that the HEBT shall be able to accommodate
Parameter | Value | Unit
Beam (kinetic) energy | 10 - 25 | MeV
Macro-pulse length | 5 - 550 | µs
Macro-pulse repetition rate | 1 - 20 | Hz
Beam current (averaged over 1 µs) | 0.2 - 2 | mA
Charge per bunch | 3 - 60 | pC

## Slide 6: HEBT scheme
Two quadrupoles, 3 dipole correctors
  On hand (made by BARC, India). Identical to MEBT magnets.
3 pumping stations; fast acting valve + 1 “slow” valve
Beam dump in a concrete “doghouse”
  Moved as far as possible from SSR1 and diagnostics
Set of diagnostics
SSR1
Pumping station
Quads
Dump
Cavity
Solenoid

## Slide 7: Beam envelope
The beam envelope in the HEBT will be heavily determined by settings of the last solenoid and cavity in the SSR1 cryomodules
  Assuming that upstream elements’ settings are optimized for acceleration
Nominal transverse (left) and longitudinal (right) beam rms envelopes. A.Saini

## Slide 8: Some of considerations for the HEBT scheme
The highest priority: do not damage the cryomodules
  Proper positions for the pumping stations, fast acting valve,…
  Quadrupoles are mainly for convenience of measurements; placed at the beginning so the beam can’t be focused at the dump
Strong preference to use either existing parts or new ones that could be re-used at PIP-II
  In diagnostics lines
Will heavily rely on the experience gained with the MEBT
Extra attention to the high-power mode

## Slide 9: Preventing a damage by the beam
2 mA x 0.55 ms x 20 Hz x 22 MeV = 484 W
  Instantaneous power density at the beam center ~2∙107 W/cm2
Passive measures
  The dump is placed as far as possible from focusing elements
    The beam can’t be focused tightly (details later)
  Large-aperture pipe upstream of the dump
  Quads are off for high-power operation
Active
  Machine Protection System
    Comparison of current readings
      Dump vs ACCT
    Loss monitors
Step-by-step path to high power
Transverse rms beam envelope with quads off. A.Saini

## Slide 10: Path to high-power operation
Start with low-emittance mode
  5 mA from the RFQ, 10 µs x (1 – 20) Hz; kickers off
  The beam is heavily scraped in the MEBT
    Decreasing the beam current by 2-10 times
    It has been demonstrated at the MEBT. Scraping ~40% of the beam in one plane (“flat beam”) decreases the rms emittance by a factor of ~2.5
  Pass the beam to the dump; correct large errors
  Commission operation with the chopping system on
Full bunch charge, low duty factor (10 µs x 20 Hz); no big scraping; the MEBT chopping system removes 60% of bunches
  Understand the transverse envelope
Turn off quads; increase the pulse length by steps

## Slide 11: Dump
The plan is to use the dump used at SNS then HINS then PIP2IT MEBT
Was designed (and used at SNS) for 16 kW at 7.5 MeV
  Used at up to 5 kW at MEBT
    B. Hartsell simulation: can sustain up to 20 kW CW if beam is large
  C. Baffes: In-pulse thermal cycling should not have detrimental effect at expected σ~6 mm
  “Halo Scrapers” to indicate a too large or misplaced beam
  O-ring seal is somewhat a concern because of radiation

## Slide 12: List of baseline measurements
ED0008280; details about diagnostics are in Vic’s talk
Beam parameter | Nominal value | Accuracy of the measurement
Beam energy | 22 MeV | ±2 %
Current (averaged over 1 ms)* | 2 mA | ±1.5 %
Transmission through both cryomodules | 98% | ±2 %
Beam position (averaged over the macro-pulse) | N/A | ±10 µm (relative)
Transverse emittance (rms, normalized) | 0.25 µm | ±10 %
Longitudinal emittance (rms, normalized) | 0.4 µm | ±20 %
Bunch extinction | < 5×10-3 | ±10-3
Transverse phase space distributions | N/A | 0.1% (relative)†
* The beam current should be measured at the exit of the SSR1 cryomodule (to measure beam transmission) and at the end of the beam line (i.e. the beam dump).
† Relative phase space density at the tails of the distribution

## Slide 13: Diagnostics in HEBT line
Details are in Vic’s presentation
Dump
ToF
FFC
RWCM
ACCT
BPM
BPM
BPM
Front slits and Wire scanner
Back slits and Wire scanner
Insertable Faraday Cup

## Slide 14: Energy
Initial measurement: Time-of-Flight monitor (ToF)
  Was successfully used at the MEBT (0.3% accuracy)
    http://accelconf.web.cern.ch/AccelConf/ipac2017/papers/tupva139.pdf
  A capacitive pickup (BPM) precisely moved longitudinally
  The slope of the recorded phase vs ToF position gives the bunch velocity
  The slope decreases for higher energy
    Expected accuracy in HEBT is ~1%
For routine measurements, will use phases of 3 fixed-position BPMs
  Also, for phasing the last SSR1 cavity
ToF model and example of a measurement in MEBT

## Slide 15: Bunch structure
MEBT chopping system will produce an aperiodic bunch sequence within each pulse to mimic future optimization for Booster injection
Need to measure the amount of beam populating the “empty” buckets to 0.1%
  Modified version of the RWCM used at MEBT
Part of the MEBT RWCM signal recording the 0.55 ms Booster injection sequence (orange), superimposed over the signal when the kicker is off (blue).
http://accelconf.web.cern.ch/AccelConf/hb2018/papers/thp1wc03.pdf

## Slide 16: Longitudinal measurements: FFC
Plan to use the Fast Faraday Cup from the MEBT
  Measured beamlet rms length down to 0.1 ns
  Found that the beamlet length depends on the radial position of the FFC
Unlike MEBT measurements, the fast scope needs to be outside of the cave because of radiation concerns
  May significantly affect the resolution
Principle of FFC operation and its 3D model (D. Sun).

## Slide 17: Bunch length and longitudinal emittance
To calculate the rms length of the entire bunch, FFC measurements are performed at various transverse locations
Longitudinal emittance is reconstructed from comparing the measurements of beamlet length vs settings of the last SSR1 cavity with simulations
Comparing FFC measurements in the MEBT with simulations. J.-P. Carneiro et al., CPO-10/ICAP’18 conference
Bunch length vs cavity phase. Simulation by A. Saini

## Slide 18: Trajectory
3 stationary BPMs (4-buttons capacitive pickups)
  Possibility to use ToF’s pickup as well
To tune the beam through the HEBT into the dump
To help with transverse optics reconstruction
  Differential trajectories method (as in the MEBT)
Response of trajectories to changing the current in the first dipole correctors by 0.4 A: horizontal x (red) and vertical y (green). http://accelconf.web.cern.ch/AccelConf/hb2018/papers/MOP1WB03.pdf

## Slide 19: Beam size and transverse rms emittance
The main tool is two Wire Scanners
  A prototype was preliminary tested at MEBT
  Measurement of two profiles (X/Y) in one pass
  <1% of beam is intercepted => low radiation
  Can be biased positively or negatively
    Signal amplitude vs cross-talk and intercepting stray particles
Emittance can be reconstructed from analysis of the beam size vs quadrupole current (quad scan)
Schematic of the Wire Scanner.
V. Scarpine, http://pip2-docdb.fnal.gov/cgi-bin/ShowDocument?docid=2249

## Slide 20: Beam transverse distribution
  The pixel’s angle is defined by a deflecting electric field
Proposal: measure the beam transverse phase space in HEBT with a slit-slit emittance scanner
  2 pairs (X/Y) of independently movable slits
  Phase space pixels are defined by position of slits
    E.g. front slit defines X
    back slit defines X’
Beam
Front slit
Back slit
Faraday Cup
Allison scanners were extensively used in LEBT and MEBT
  One scan gives a complete description of a plane
  Rms parameters as well as tails
Comparison of two phase portraits recorded with MEBT Allison scanner, for a full beam and after cutting 10% with a scraper

## Slide 21: Slit-slit scanner discussion
Possible difficulty for resolving far tails: secondary electrons
  Dipole correctors between slits should help
Allows to understand growth of tails in the cryomodules and efficiency of scraping in the MEBT
  Important to prepare a realistic distribution for PIP-II beam simulations
  can measure correlations between transverse planes
Drawbacks: slow; intercepts the entire beam
  Measurements speed and the amount might be limited by radiation issues
Dipole
Dipole
Dipole
Front slits
Back slits
Insertable Faraday Cup

## Slide 22: Summary
The HEBT design allows for safe beam operation
Set of diagnostics is large enough to tune the beam and comprehensively characterize it in transverse planes
  FFC measurements would catch a large deviation from expectations