## Slide 1: P6 schedule: SSR2 DAE cavities delivery
DAE#1 Receive 6/1/2021, Qualify 8/12/2021
DAE#2 Receive 6/15/2021, Qualify 8/26/2021
SSR2-0 String Assembly Starts 3/18/22
Notes: String Assembly finish

## Slide 2: Major RF Parameters
Parameters | SSR2 v 2.6 Comsol | SSR2 v 3.1 Comsol
Optimal beta βopt | 0.475 | 0.472
Aperture [mm] | 40 | 40
Frequency [MHz] | 325 | 325
Effective length 2βoptλ/2 [m] | 0.438 | 0.436
Epeak/Eacc | 3.39 | 3.51
Bpeak/Eacc [mT/(MV/m)] | 5.93 | 6.75
G [Ohm] | 115 | 115
R/Q [Ohm] | 296.6 | 305.2
Epeak [MV/m] @ 5 MeV | 38.7 | 40.2
Bpeak [mT] @ 5 MeV | 67.7 | 77.4
Max energy gain [MeV] | 5.0 | 5.0
Max gradient [MV/m] | 11.42 | 11.47
Multipacting : Acceptable Superior

## Slide 3: Options for path forward
Options | Pros | Cons
Option 1: RF volume v2.7 Nb 3.15 mm | RF design finalized by BARC Material at BARC Fastest track for delivery to FNAL for integration in SSR2-0 CM | Parallel mechanical design effort needed Thinner material may turn out to be an issue for pressure safety Not optimal performance for LFD and dF/dP
Option 2: RF volume v3.1 Nb 3.15 mm | Improved design, overall better for PIP-II Material at BARC Common design effort, more resources available | Design not finalized yet Same as above for safety and performance
Option 3: RF volume v3.1 Nb 4 mm | Improved design, overall better for PIP-II Better performance Same design under all aspects, more resources available | Design not finalized Material not ordered yet Longest turn-around