## Slide 1
Review of Wideband Cavity Technology
Chihiro Ohmori
KEK/J-PARC

## Slide 2: Contents
1.Wideband Cavity Technology
2.J-PARC MR Cavity
3.J-PARC RCS Cavtiy
4.CERN LIU-RF Collaboration
5. Extension of Frequency band
    ELENA – 100 keV, 100 kHz RF
    40 MHz Wideband Cavity Technology
6. Large Core Production for Transportation System

## Slide 3: 1. Wideband Cavity Technology
Good Finemet® core
RF B-field
RF B-field
Domain Wall
Domain Wall displacement
Magnetic Domain Rotation
Annealing under B-field
~2013 for large cores
Cavity Impedance is improved by magnetic annealing.

## Slide 4: Mass Prodution : J-PARC/KEK-made magnetic annealing oven
J-PARC MR: 300 Cores, CERN PSB:342

## Slide 5: Magnetic Annealing
Keeping high permeability, increase Q
With B-field
w/o B-field
With B-field
w/o B-field

## Slide 6: 2. MR Cavity
MR is high intensity machine & periodic transient beam loading
6 Cavities for acceleration
2 Cavity for 2nd Harmonic RF
1 Spare
H=9
Q=26
H < Q

## Slide 7: 3. J-PARC RCS Cavity
RCS is high intensity machine & 2nd Harmonic RF & large frequency change => Q=2
External inductor in tube amplifier
for Q=2

## Slide 8: Longitudinal Profiles with High Intensity Beam of 500 kW equivalent
(100 kV, 0 kV)
Bunching factor
0.2 ~ 0.3
Bunch length
~200 ns
(100 kV, 70 kV)
Bunching factor
0.3 ~ 0.4
Bunch length
~400 ns
Simulation
(100 kV, 0 kV)
Simulation
(100 kV, 70 kV)
F. Tamura

## Slide 9: 4.LIU-PS Booster RF
Replacements of all ferrite-loaded cavity systems to new Finemet®-base wideband system
All systems to install in LS2 are ready.
KEK contributes:
  Cavity Design using FT3L
  Productions : Oven & 132 cores
  Tests : Quality control
CERN Courier 2017, July

## Slide 10: Power Test of new PSB cavities ： Mixing of 3 harmonics
All cavities can work as fundamental (acceleration), 2nd Harmonic RF and blow-up one.
H=1
H=1,2
H=1,2,10
M. paoluzzi
Reliability
10-Cell Finemet Cavity shows >99% availability
Maria Elena Angoletta

## Slide 11: PS Damper for longitudinal instability
Longitudinal Coupled bunch instability at CERN PS causes emittance growth for LHC-type beam.
Wideband Damper system works for dipole mode.
But, Qudarupole mode was observed at >2e11 ppb. Need to damp the mode by a Landau cavity.
H. Damerau

## Slide 12: Landau cavity
Beam studies with a Landau cavity.
  Existing 40 MHz cavity to damp Quadrupole Mode
This year, reached 2.6 E11 ppb, 25 ns 72 bunches !
H. Damerau

## Slide 13: Intensity evolution (25 ns, 72 bunches)
Wealth of beam measurements at 2.6 ∙ 1011 p/b (LIU intensity)
No more protons until end of 2020
Finemet dipole-mode
coupled-bunch feedback
Optimization 2017
Suspected feedback saturation
Multi-harmonic feedbacks
C40-78 as Landau RF system
Reach with C10-86/96 coupled-bunch feedback (2005)*
LIU baseline
*Intensities >1.3 ∙ 1011 ppb were delivered <2016, but not with sufficient quality for LHC
Intensity per bunch at extraction
Bunch profile/length
Study WG started
H. Damerau

## Slide 14: . Rad-Hard Solid-State Amplifier
To use many solid state amplifier in Accelerator Tunnel, Rad-Hard type is developed .
Control of bias point of each MOSFET improves life time.
We have tested the scheme at: 3 Co-60 facilities, J-PARC, CERN-CHARM, PSI
CHARM: 1.9 kGy mixed field- 100 years in PSB & QST-Takasaki (Co-60):8.8 kGy
Small gain change (~ 1dB)
Next Test at J-PARC for 10 kGy mixed field for 10 years in PS to improve feedback.
8.8 kGy gamma-ray
1.9 kGy mixed field
The results were submitted to IEEE TNS. The work is supported by KEK,CERN,JSPS-Kakenhi.
>10 kGy mixed field at J-PARC
~1kGy/day in T2K run

## Slide 15: 5. Benefits of Wideband Technology Success of Deceleration
Maria Elena Angoletta
ELENA needs deceleration from 5.3 MeV to 100 keV !
Revolution Frequency :1.045 MHz to 144 kHz

## Slide 16: 40 MHz Wideband Cavity Technology Finemet®-base Landau Cavity R&D
The test at CERN shows a good result.
Test cavity is under testing at KEK/J-PARC with the best MA cores.
40 MHz Cavity R&D may be useful for future applications.
M. paoluzzi

## Slide 17: 6. Technology Transfer and Contribution to Society
KEK/J-PARC has developed a large core production system- magnetic annealing oven in 2013.
The oven may be used to produce transformer cores for power supplies of transportation systems. KEK and Hitachi Metal Ltd. agreed to use the system and R&D has been started in 2018.
Wideband Cavity Technology will contribute to downsize transformers, to reduce power consumption and to Conservation of the global environment.
KEK-made Mag. Annealing oven

## Slide 18: Comparison of material for transformer uses
Hitachi Metal Co.

## Slide 19: Wideband Cavity Technology is spreading !
J-PARC PSB PS
Large Core Production
Magnetic Annealing
Public Transportation
LEIR ELENA Med-Autstron