## Slide 1
US-Japan Collaboration on high-intensity neutrino beams
Laser manipulation of H- beams -- JFY2018 Progress status at J-PARC
Pranab K. Saha
On behalf of J-PARC laser stripping group
2019 collaboration meeting at Fermilab, March 21

## Slide 2: Introduction and collaboration outlook
■ Laser manipulations of the H- beam for utilization in stripping,
chopping, beam diagnostic and other purposes are an important
subject for the present and next-generation high-intensity
proton accelerators.
■ Non-destructive and highly required not only for the existing
high intensity machines but also to realize multi-MW beam power.
The collaboration aims at
Developing a framework for an effective laser manipulation
of the H- beam
 Achieve maximum efficiency with a minimum laser power.
Explore for multi-dimensional applications.
. . . . . . . . . . . .

## Slide 3: Activities at J-PARC
Two major activities for:
1. Proof-of-principle (POP) demonstration for 400 MeV H- stripping to protons by using only lasers.
--- Ultimate goal is to realize laser stripping of 400 MeV
H- charge exchange system.
2. Multi-dimensional laser manipulations of 3 MeV H-
at RFQ-TF.
--- H- neutralization, transverse and longitudinal H- beam diagnostics, etc by using roof-top laser profile and/or two-mirror non-resonant laser cavity.
 Strong feedback to the 400 MeV laser stripping and beam instrumentations.

## Slide 4: Progress highlights in JFY 2018
1. Collaboration between JAEA & UEC (Univ. of Electro-Communications)
has been established for development of the laser systems for 400
MeV H- laser stripping POP demonstration and also for ultimate goal.
Development of the laser system is in progress.
2. David Johnson from Fermilab visited J-PARC in March 2-16
as KEK short-term invited fellow.
Demonstrated two-mirror laser cavity
with roof-top laser profile. We used
HeNe laser for the demonstration.
Ultimately, we will develop a system
with YAG laser.
Would be highly essential for laser
stripping, future applications of beam
diagnostics.

## Slide 5
Materials & Life Science Facility (MLF)
3 GeV Rapid Cycling Synchrotron (RCS)
400 MeV H- Linac
30 GeV Main Ring Synchrotron (MR)
J-PARC
KEK & JAEA)
Transmutation Experimental Facility (TEF)
Fast Extraction
Neutrino experiment (NU)
Slow Extraction
Hadron experiments (HD)
H- p

## Slide 6: Principle of H- stripping by only lasers
H-
H0
H0*
p
e-
e-
e-
e-
UV laser
l ~ 200 nm
Step 1:
H- + g → H0 + e-
Step 2:
Excitation of H0
H0 + g → H0* (n=3)
Step 3:
H0* + g → p + e-
Nd: YAG Laser
l=1064 nm
Nd: YAG Laser
l=1064 nm
50°
90°
90°
Isao Yamane, Hiroyuki Harada, Saha Pranab and Shinichi Kato
PASJ, Vol. 13, 2016, 1-11 (in Japanese)
Doppler effect of the 400
MeV H- beam:
b = 0.713, g = 1.426
l = l0 (1 + b cosa)g
Process | Eph (eV) | l (nm) | a (deg.) | l0 (nm) | Laser
H- H0 | 1.67 | 1064 | 90 | 743 | Nd:YAG
H0H0* | 12.1 | 212 | 50 | 102 | 5th H of YAG
H0*p | 1.67 | 1064 | 90 | 743 | ND:YAG
DE=12.1 eV
DE = hc/l0
l0= 102 nm

## Slide 7
POP Experimental area, beamline
The POP experiment will be performed at the end section of
L-3BT (Linac to the 3-GeV Beam Transport)
H-
H-
H0
p
All three charge fractions
can be simultaneously measured.

## Slide 8: POP experimental devices setup
QM61
~1.5m
H- beam
Chamber for the
POP demonstration
End section of Linac to 3-GeV
Beam Transport

## Slide 9: Vacuum chamber for the POP demonstration --- Installed
H- beam
Nd:YAG laser
UV laser
×
Vacuum
chamber
Ｙ
X
Z
Big laser windows: For UV laser with angle variation one can try H0 promotions to different state up to direct ionization.
a = 27o , l0 = 91.2 nm l = l0(1 + bcosa)g

## Slide 10: Laser energy/pulse for POP demonstration
. . .
3.08ns
Micro pulses (324 MHz)
814ns
456ns
. . .
Intermediate pulses (1.2285 MHz)
(Structure @ injecting into the RCS)
0.5ms
40ms
. . .
Cycle (25 Hz)
RCS
Macro pulse
For the POP demonstration, we will use
only a single 324 MHz micro pulse of ~100ps.
The IR laser energy/pulse is ~10 mJ
for > 90% neutralization and stripping.
The laser energy strongly depends on
the H- beam sizes, which are adjustable.
For the H0 excitation, SNS demonstrated
> 90% excitation efficiency by using
~1 MW peak power UV laser.
We will also need a similar UV laser power.
0.1ns

## Slide 11: R&D Status of the Lasers
The present Nd:YAG laser: (25 Hz, 0.2J)
Temporal profile: Spiky and also pulse
length too broad (>10 ns).
10ns/div
Measured by
biplanar
photodiode
A new Nd:YAG laser system is under development
J-PARC-UEC (Tokyo) collaboration
Laser specification: 100 ps, 10 mJ/pulse
For 324 MHz laser pulse we also have to
develop optical cavity
Modulator (EOM)
(0.1 nJ, <100 ps, 81 MHz)
Preamplifier
double core fiber
LMC fiber
amp
YAG rod amp
1mJ
~10mJ?
Optical cavity
To be assembled
JFY2019
RF
Clock
US-Japan
Collaboration
JFY2019 bottom line

## Slide 12: Laser angle control and variation tested
H. Harada
Laser
Angle control system
Rotation
Moving
Monitor (IP)
Glass plate
IP
（pinhole）
Δθ = 0 Deg.
Δθ = 10 Deg.
Δθ = 15 Deg.
l = l0 (1 + b cos a)g
Eventually changing a0
The POP chamber windows are made wider for large angle variation.
・ Different excitation level
and even direct ionization
・ Wavelength dependence
cross section, etc.
The interaction angle, a is very important,
especially for the H0 excitation

## Slide 13: To reduce the laser power, especially for the H0 excitation 1) Dispersion derivative (D’) and 2) minimization of betatron angular spread (ax ~0) are very essential.
Reduce betatron
angular spread
Required maximum angular spread of the laser pulse
to cover ion beam (Ref: I. Yamane)
Utilize dispersion
Derivative, D’
Eliminate transition frequency spread
g1
g2
g3
gn
a
H0
H0*
Uniform laser beam
● Laser beam with no divergence
● Hydrogen atom with different energies
have the same laser light frequency
in their rest frame.
 Gain on the laser peak power.
= = -1.3
V. Danilov, PRST-AB, 2003

## Slide 14: Optimization of betatron angular spread
X
X’
Transverse beam emittance:
e = gx2 + 2axx’ + bx’2
g = (1+a2)/b
tan(2f) = 2a/(g-b)
a, b, g, e are twiss parameters
Angular spread is controlled by optimizing a to zero and also with large b.
a = 0
X
X’
{
f
a = 0, b enlarge
As for the vertical size of the H- beam, a smaller size is required to
gain on the beam density. At SNS, sv = 0.15 mm achieved.

## Slide 15: Possibility to obtain D’=-1.3 at the IP: Simulation results
D’ = -1.3
Experimental studies will be done
Simulations
Laser power reduction by utilizing dispersion derivative.
 1/5 reduction possible

## Slide 16: Laser stripping of 400 MeV H- beam --- Scheduled step by step
JFY 2019: A set of IR laser system for 400 MeV H- neutralization.
JFY 2020: The 400 MeV H- neutralization studies.
For stripping, UV laser is needed for H0 promotion to higher states.
JFY 2021: Hopefully, 400 MeV H- stripping studies can be started.
H- neutralization
study first.

## Slide 17: Laser manipulations of 3 MeV H- beam at J-PARC RFQ-TF -- Multi-dimensional studies are planned
In addition to 400 MeV laser stripping, we also planned for establishment of multi-dimensional applications of laser
manipulations of H- beam for 3 MeV first at J-PARC
RFQ TF as follows:
H- neutralization, beam diagnostic systems, beam cleaning/extinction, chopping, etc.
IS
RFQ
324 MHz
Bend
LASER
23°
11°
H-
H0
0°
Schematic view of J-PARC
RFQ-TF beam line:
3 MeV H- neutralization studies
were done for only 10W beam
for another purpose.

## Slide 18: Application of Fermilab two-mirror laser cavity
Applicable to 400 MeV laser stripping
Laser power can be significantly reduced by the
application of two mirror laser cavity system.
Finding ways for applying J-PARC laser stripping.
1/10 reduction of the laser can
easily be achieved
Feasibility, stripping efficiency both improved.
Two-mirror UV laser cavity for the H0 excitation?
Even if 1 pass gives 75% excitation eff.,
> 95% by 3 passes
UV mirror coating are
big Issues. UEC already
started a separate program.
p
Courtesy:
D. Johnson
T. Johnson

## Slide 19: Development of a new transverse H- beam profile monitor system
Laser: 1064 nm Nd:YAG and
Utilize roof-top transverse laser profile.
H- + g = H0 +e-
Measure H0 profile by using a MWPM.
(H0 by a MWPM was previously measured)
Easy and straightforward way to measure
transverse H- beam profiles.
Intensity/SC dependent profile
(should have advantages than using electron
collection or H- wire profile scanner..)
Measurement easy at the arc section, but
in the straight section, local bump (chicane) can
be done to separate H0 and H- for measurement.
 Measurement possible for any section of the Linac
J-PARC L3BT beam pipes diameters: 12 cm
H0
Roof-top laser
transverse
profile
H-

## Slide 20: Development of Longitudinal H- beam profile monitor system
324 MHz H- temporal profile
time
Intensity
Scan laser through the micro pulse.
Measure H0 yield (through stripping to p by foil)
or estimate the reduction of H- yield with laser on
Gives the longitudinal H- profile.
Shot pulse Laser
. . . . .
・Measurement can be done by BPM.
・Completely non-destructive.
Short pulse laser is required.
Micro pulse width: >100 ps (s) at
the L-3BT  Possible to measure.
However, it is may be <<100 ps at the
RFQ exit.  Difficult to measure?

## Slide 21
Summary
We are progressing step by step to demonstrate 400 MeV H-
stripping by using only lasers at J-PARC and also for the ultimate
design of the laser system for the laser stripping injection.
The laser system is under development collaborating with UEC.
● The H- neutralization studies is expected to start in JFY 2020.
● The POP demonstration of 400 MeV H- stripping in 2021.
David Johnson’s visit to J-PARC was one very remarkable event.
We had two fruitful weeks. Learned about roof-top laser profile
generation and use that for the two mirror cavity.
We have planned multi-dimensional laser manipulations of the
3-MeV H- beams at J-PARC RFQ-TF.
Would be very essential for the laser stripping.
The US-Japan collaboration in this subject also plays significant roles
for next generation laser manipulations of the H- beam.