## Slide 1
Colin Narug
8 March 2019
Coil Support Structure Initial Design

## Slide 2: Requirements
Five coils broken up into two types, A and B
Arranged in pattern A B A B A
  B coils known as Side coils
  A coils known as Shield/Center Coils
Shield Coil
  6m from center
  Exerts 2.2 MN away from center
Side Coil
  2.5 m from center
  Exerts 6.81 MN at the center
Coil Dimensions of 25cm x 25 cm

## Slide 3: Minimum Requirements
Using generic aluminum and steel yields with SF of 2
  Allowable yield of 145 MPa for steel
  Allowable yield of 138 MPa for aluminum
Calculated minimum required area to prevent failure
  Without any cross supports, welds, bolts , etc.
  Final mass could be significantly larger
Steel
Shield to Side
  Area = 0.015 m^2
  Mass = 181.841 kg
Side to Center
  Area = 0.047 m^2
  Mass=938.136 kg
Aluminum
Shield to Side
  Area = 0.016 m^2
  Mass = 64.565 kg
Side to Center
  Area = 0.049 m^2
  Mass = 333.098 kg

## Slide 4: Minimum Requirements Cont.
Coil will apply pressure on support structure
  Pressure on Side Coil is about 1.196 MPa
  Pressure on Shield Coil is about 1.186 MPa
Assuming density of copper for Coil
  Side Coil is about 12,750 kg (125,100 N)
  Shield Coil is about 1,385 kg (13,580 N)

## Slide 5: Initial Design
Create 2 structures, Inner and Outer Frames.
Inner Frame
  Inner structure made of support rings, coils and coil connections
    Support each coil in a Support Ring
    Connect each support ring longitudinally
    Link inner and outer frames at coil B
Outer Frame
  Outer frame connects to outside world
  Supports weight of coils, resists inner forces
  Can serve other purposes
    Insulate, cable lead through, maintain environment

## Slide 6: Inner Frame Initial Design
Create 2 structures, Inner and Outer Frames.
Line Bodies used to create initial analysis/design
  Not the most accurate, but quick and good for truss analysis
Using Aluminum Hollow Structural Sections an initial, solution has been found
  HSS 304.8 x 203.2 x 12.7
  Not optimized, crosses through stay clears, but workable
Front View
Iso. View
Side View

## Slide 7: Simulation Results

## Slide 8: Summary
Deformation Less than 2 mm
  1.07 mm vertical
  1.26 mm horizontal
Stress in structure less than allowable
  19.5 MPa
Edits to structure, methods of connection, etc. still needed.
  Currently has a mass of 4,391 kg in coil connecters
  Coil Support has mass of 23,010 kg