## Slide 1: Update of noise filtering in protoDUNE
Wenqiang Gu (BNL)
Carlos Sarasty (University of Cincinnati)

## Slide 2: Overview of the noise filtering
Noise filtering (NF) is a key step towards a high-quality signal processing (SP)
Sticky codes
FEMB clock
Undershoot
“50kHz” noise (collection plane)
“Ledge” effect
Coherent noise
Recently, revisited the performance of noise filtering
Some problems, some new ideas, …
Towards a high-quality NF soon
Not talked about today

## Slide 3: Sticky codes mitigation
Apply correction
  “noise-like”: linear interpolation + FFT resampling
  “signal-like”: FFT resampling
    Peak value > 15 ADC, nearby (+/- 1 tick) > 2*RMS
Some additional sticky codes need to be deal with
Also see prev. analyses by 1) David, 2) Wenqiang
Mod64 = 7
Extra sticky codes
other than Mod64=0,1,63
Resampling in freq.
Inverse FFT
Illustration of “FFT resampling”
Sticky on a ledge
Good correction for afterward steps

## Slide 4: An example of sticky code mitigation
Before mitigation
After mitigation
Deconvolved signal
An extreme sticky channel, an artificial “bipolar” shape after interpolation
=> fake charge
Sticky at baseline
Deconvolved charge from adjacent channels:
“2D” deconvolution
Need more detailed evaluation
  Exclude very sticky channels / time regions for SP
  Any over-correction for SP?

## Slide 5: FEMB 302 clock
128 channels in FEMB 302 is “slower” than others
The FFT resampling approach also works here
  Extend 5996 samples => 6000 samples in freq. domain
Before correction
After correction
Also see David & Tom’s talk for resampling in time domain

## Slide 6: Undershoot correction (i)
Undershoot can be successfully removed by deconvolving the RC response (~ 1.1ms) in frequency domain via FFT
After correction
(RC constant 1.1ms)
Before correction
Run 5424 Event 10447
Also see Tom’s time-domain RC fixer
= 1.1 ms (collection)
= 3.3 ms (induction)
deconvolved signal

## Slide 7: Undershoot correction: another example
Another example
After deconvolving RC response
Raw waveform

## Slide 8: Undershoot correction (ii)
In case that a large signal happens right before the readout window (“partial RC”), an adaptive baseline correction (linear) is applied
Before correction
After correction

## Slide 9: Undershoot correction (ii): another example
Another example of “partial RC” correction
Before correction

## Slide 10: Imperfect electronics response
The RC correction works well, however, still observed some imperfect electronics response even after small signals
  Imperfect pole-zero cancellation?
A dedicated calibration could help if indeed an electronics response issue
  Current pulser data: too short distance between the positive and the negative pulses
Need more samples for a conclusion
Time constant ~ 0.2ms
Imperfect pole-zero cancellation?

## Slide 11
Pulser calibration
Run 6068
Cosmic data
Seems to be not consistent?

## Slide 12: “50 kHz” noise in some collection channels
An automated spike filtering is implemented
  Zero-out extreme outliers of each sub-region in frequency domain
--- before NF
--- after NF
Also see previous analysis by Carlos: 1 2
--- before NF
--- after NF
Ticks [0.5us]
Freq. bins
Filtered noise component
Looks reasonable!

## Slide 13: Mask for “ledge” region
The bad region of the identified “ledge” will be masked and ignored in the SP
Still need some tuning for the range
Masked region for SP
Also see previous analysis

## Slide 14: Summary
Noise filtering are revisited and the general performance are good
Still need more detailed evaluation/hand scan for sticky code, ledge, undershoot, etc.
  Imperfect response shape in some channels
  Calibration pulser data could be helpful
Before we tune the SP algorithm, a solid performance of NF is necessary