## Slide 1: Optics of the LBNF Primary Proton Line “Lucky 13”
John A Johnstone
TSD Monthly Meeting.
March 21st, 2019

## Slide 2: The other “Lucky 13”

## Slide 3: Outline
Design Overview
  Trajectory
  Magnets
  Optics
    Lattice Functions
    Beam Envelope & Magnet Apertures
    Final Focus & Spot Size Tuning
    MI-10 Extraction
Summary
Moving Forward
Other
  Sensitivity to Gradient Errors
  Trajectory Control
  MARS Confirmation of Lossless Extraction
  Magnet Parameters
  Final Focus Gradients
  Conflict Examples Revealed by 3D Modeling

## Slide 4: Trajectory (1)
Beam is extracted vertically from MI-10 via 6 horizontal kicker modules d/s of MI quad Q100, and 3 Lambertsons plus a C-magnet straddling MI Q102.
A rolled dipole steers the beam through the enclosure wall, while bisecting the MI & Recycler magnet elevations.

## Slide 5: Trajectory (2)
In the LBNF tunnel 12 rolled dipoles (grouped as 3 sets of 4) bend the beam 7.2o horizontally to align with SURF in South Dakota, and upwards by 143 mr.

## Slide 6: Trajectory (3)
A second series of vertical dipoles bend the beam down through 244 mr to complete vertical alignment to SURF, with φ = -101 mr.
Target elevation is fixed at 750 ft (~10 ft above grade) & maximum BLC elevation is 770 ft (~3 stories above grade).
Distance from MCZERO (Target) to center of FD = 1286873.76 m ±

## Slide 7: Magnet Complement
All major magnets are well-understood, proven designs
  In the main body of the line all dipoles are Main Injector-style IDA (6m) & IDD (4m) magnets
  Quadrupoles are all of the MI-style 3Q120 (3.048 m) or the shorter 3Q60 version (1.524m)
  New IDS trims have 3” pole tip gap & design spec of 250 μr (RMS).
  IDA sagitta = 11.7 → 18.6 mm c.f. 16 mm design nominal
  IDD sagitta = 5.2 → 8.3 mm c.f. 7 mm design nominal
Magnet | Common Name | Steel Length | Strength at 120 GeV | Count
RKB | LBNF Extraction kicker | 1.295 m | 0.0589 T | 6
ILA | MI Lambertson | 2.800 m | 0.532 / 1.000 T | 3
ICA | MI C Magnet | 3.353 m | 1.003 T | 1
IDA | MI Dipole 6 m | 6.100 m | 1.003 – 1.604 T | 13
IDD | MI Dipole 4 m | 4.067 m | 1.003 – 1.604 T | 12
QQQ | MI 3Q120 quadrupole | 3.048 m | 9.189 – 16.546 T/m | 17
QQU | LBNF 3Q60 quadrupole | 1.524 m | 11.135 – 17.082 T/m | 4
IDS | LBNF trim dipoles | 0.305 m | Up to 0.365 T | 23

## Slide 8: Optics Overview
___________________________________________________________________________________________________
Subsequent discussions , unless stated otherwise, assume nominal MI beam parameters of 99= 30 mm-mr (normalized) & p99/p = 11.e-4, with σ* = 1.70 mm.
To avoid losses the beam size in the LBNF transfer line can not exceed that of the Main Injector circulating beam.
The ultra-clean transport requirements virtually compel the lattice to be configured from distinct optical modules.
  MI→LBNF matching
  LBNF 120o FODO cells
  Final Focus on target
Every focusing center has a dual-plane BPM & dipole corrector
Every half-cell has space reserved for a multi-wire or other diagnostics.
Spot-size on target must be tunable over a wide range: from  ~ 1.0 → ~4.0 mm to accommodate a beam power upgrade to 2.4 MW.
Physics dictates it must also be continuously tunable over the range 60 → 120 GeV/c for optimizing the neutrino oscillation spectrum.
To satisfy these conditions β* must be tunable by a factor of x32 over this range (!).

## Slide 9: Lattice Functions
Horizontal (solid) and vertical (dashed) lattice functions of the LBNF transfer line
[Dipoles are represented by boxes centered on the top axis, and quadrupoles are boxes extending up (F) and down (D)]
The final focus is tuned for x = y = 1.70 mm at 120 GeV/c with β* = 110.88 m with nominal MI beam parameters
ε99 = 30 mm-mr & Δp99/p = 11x10-4
[

## Slide 10: Beam Envelopes & Magnet Apertures
Dipole apertures, shown in blue, include the effects
of sagitta & rolls.
Quadrupole apertures are red.
The 99% envelopes (dashed) represent nominal MI beam parameters
[ 99 = 30 mm-mr & p99/p = 11.e-4 ];
The 100% envelopes (solid) correspond to the MI admittance at transition .
[ 100 = 360 mm-mrϮ & p100/p = 28.e-4 (t = 21.600) ]
The beamline can transport, without losses, the worst quality beam that the MI could conceivably spew forth.
__________________________
Ϯ 360 mm-mr → 10.6σ for a Gaussian

## Slide 11: Final Focus & Spot-Size Tuning
The extremes shown correspond to: 60 GeV/c with σ* = 1.0mm; β* = 19.184m and βmax = 104m (lower), and; at 120 GeV/c with σ* = 3.20mm; β* = 393 m and βmax = 483 m (upper). Horizontal values are displayed as solid curves & vertical values are dashed.
[In principle the spot –size can be tuned to σ* = 4.00mm, but the 3.20mm shown is a self-imposed maximum limit of 360π mm-mr horizontal acceptance (10.6σ) in the final down bend].
60 GeV : σ* = 1.0mm
120 GeV : σ* = 3.2mm
y

## Slide 12: MI-10 Extraction (1) -- Extraction Element Configuration
LBNF extraction Lambertsons and C-magnet straddling MI quad Q102
LBNF extraction elements and their configuration are clones of those found at other MI extraction points.
LBNF BEAM

## Slide 13: Extraction (2) -- MI-10 → LBNF Enclosure
Transport from the existing MI tunnel enclosure into the new LBNF enclosure showing the carrier pipe connecting the MI-10 & LBNF enclosures (left), and separation of Q203 at the u/s end from the Main Injector & Recycler Rings (right).

## Slide 14: Extraction (3) -- Closed Orbit & Extracted Beam Trajectories
CLOSED ORBIT BUMP QUAD OFFSETS (mm) |  |  | EXTRACTION ELEMENTS |  | 
QUAD |  |  | MAGNET | LENGTH (in) | FIELD (T)
Q100 | 2.464 |  | KICKERS (6) | 51 | 0.0589 / module
Q102 | 2.358 |  | LAM1 | 110.25 | 0.5270
Q104 | 2.573 |  | LAM2 & LAM3 | 110.25 | 0.9985
Q106 | 2.154 |  | C-MAG | 132 | 0.9918
120 GeV/c parameters of the circulating & extracted beam elements.

## Slide 15: Extraction (4) -- Beam-Beam Separation in Q102
60 GeV/c Circulating & Extracted beam ellipses at the entrance to LAM1 and the exit from Q102. (99 = 30 mm-mr )
Large Aperture Quad
55/8 x 55/8 Star Chamber
6 Kicker modules create 40.5 mm separation at the 1st Lambertson entrance between circulating & extracted beams.

## Slide 16: Summary to date
Beam is extracted at MI-10 & transported to a target above grade.
The lattice design is comprised entirely of proven MI-style magnets.
MI-10 extraction configuration & the beamline provide for loss-free transmission of a 10.6σ beam.
The final focus is continuously tunable from σ* = 1.00 → 4.00 mm over the entire momentum range 60 → 120 GeV/c

## Slide 17: After 3 years or so enforced LBNF beamline hibernation . . .
Lattice design is up & running again – major design features are all stabilized, but small adjustments are still needed:
  A few minor interferences still need to be resolved
  Some additional instrumentation & devices are being added
  Positions of a corrector/multiwire+bpm package are being interchanged in the FF triplet to improve steering control.
  Center of the far detector shifted by ~50m during the beamline hiatus so the line now needs to be re-aimed.
Coraggio ! Avanti !
'Fight on, my men,' Sir Andrew sayes, 'A little Ime hurt, but yett not slaine; Ile but lye downe and bleede a while, And then Ile rise and fight againe’.
Ω

## Slide 18: Other
  Sensitivity to Gradient Errors
  Trajectory Control
  MARS Confirmation of Lossless Extraction
  Magnet Parameters
  Final Focus Gradients
  Conflict Examples Revealed by 3D Modeling

## Slide 19: Sensitivity to Gradient Errors
Not An Issue!
Experience has shown the MI-style 3Q120 quadrupoles to be of very high accelerator qualityϮ
  (G/G)  0.08% or less, which can be reduced even further for the FODO section with only rudimentary sorting.
  A simple thin-lens calculation predicts that even the largest error-wave generated in the 99% beam envelope [3.74mm at  = 59.6m] would be < 70 microns.
_________________________________________________________________
Ϯ Magnet Test Facility measurement data base.

## Slide 20: Trajectory Control
Misalignments (including BPM’s)Ϯ
  (x,y) = 0.25 mm
  (roll) = 0.50 mr
Dipole Field Errors
  (B/B) = 10e-4
Uncorrected/corrected trajectories with random misalignments and dipole field errors
(Corrected trajectories appear as solid black)
The plot begins at the u/s end of the 1st Lambertson.
New IDS design spec is 250 μr (RMS).
________________________________
Ϯ Main Injector Technical Design Handbook

## Slide 21: MARS Confirmation of Lossless Extraction (1)
The extraction region in MI-10 was modeled in MARS for tracking
A 4-dimensional (x,x’ ; y,y’) surface in phase space was populated with a 360π mm-mr (100%, normalized) emittance in both planes.
10,000 particles were tracked through to the end of the 3rd Lambertson.

## Slide 22: MARS Confirmation of Lossless Extraction (2)
No particles were lost on any aperture
Entrance & exit of Q102

## Slide 23: Magnet Parameters

## Slide 24: Final Focus Gradients for Extremes of Spot-Size Parameters
 |  |  | σ = 1.00mm @ 60 GeV/c β* = 19.184 m | σ = 3.20mm @ 120 GeV/c β* = 392.89 m
QUAD | TYPE | L (m) | G (T/m) | G (T/m)
Q213 | 3Q120 | 3.048 | −6.97624 | −12.01223
Q214 | 3Q120 | 3.048 | +8.40581 | +17.38185
Q215 | 3Q120 | 3.048 | −7.64787 | −14.48899
Q216 | 3Q120 | 3.048 | +7.03514 | +7.68385
Q217 | 3Q60 | 1.524 | −8.56034 | −3.99561
Q219 | 3Q120 | 3.048 | −6.66201 | −11.74485
Q220 | 3Q120 | 3.048 | +10.76572 | +15.68461
Q221 | 3Q60 | 1.524 | −10.11021 | −12.62987

## Slide 25: Conflict Example #1: VT203 – MI Tunnel Wall
Problem:
  Trim IDS embedded in wall
Resolution:
  Interchange the d/s corrector and the u/s multiwire plus BPM

## Slide 26: Conflict Example #2: Q204 – LBNF Enclosure Wall
Problem:
  Q204 u/s water manifold embedded in wall.
Resolution:
  Reverse quad installation direction
  Roll through 90o to get the water connections out of the aisle & onto the top of the magnet.

## Slide 27: Conflict Example #3: RR Kickers -- HV201
bent load
Problem:
  RR kickers embedded several inches into LBNF dipole HV201.
Resolution:
  Bend the RR kicker loads out of the way.