## Slide 1
Matthew Alvarez
June 20, 2019
Mu2e Electrostatic Septa Volumetric Exchange of FC-40 Dielectric in High Radiation Environments

## Slide 2: Outline
Introduction
Background
Mechanical Design of HVF
Test Setup
Results

## Slide 3: Introduction
Mu2e Experiment
  8GeV Proton Beam needed to observe Muon to Electron Decay.
  Requires Septa to deliver beam from the storage ring.
Mu2e proposes to measure the ratio of the rate of the neutrinoless, coherent conversion of muons into electrons in the field of a nucleus, relative to the rate of ordinary muon capture on the nucleus:
Mu2e TDR, arXiv:1501.05241

## Slide 4: Background
Electrostatic Septa
  100kV nominal voltage is used to extract the beam for the Mu2e experiment.
  MARS simulations show
    HVF sees 1e7Gy/yr
  High radiation was observed during extraction near the septa in the AP-30 region.
  Radiation exposure of the HVF indicate likely breakdown of the FC-40 insulating capabilities.- Voltage Instabilities)
  Creates toxic gases.
    5 ppm/hr
JPARC Test Results

## Slide 5: Background
5PPM/hr of Fluorine ions generated
  Free fluoring ions can recombine into hydrofluoric acid and Perfluoroisobutlylene (PFIB)
    Very dangerous when inhaled or in contact with your skin. Therefore, it is bad for the equipment.
What is the danger level for humans?
  3ppm in air according to National Research Council Subcommittee on Acute Exposure Guideline Levels.
We need to mitigate this by having an FC-40 Recirculating HVF with chemical filters.

## Slide 6: Mechanical Design of HVF
Recirculating FC-40 through the HVF

## Slide 7: Test Setup
Water as the working fluid
StellarNet Portable Black-Comet-SR Spectrometer (190nm-850nm)
1.9LPM flow rate (0.5GPM)
10Hz sample rate (for 15s) measured 350nm to 846nm wavelengths

## Slide 8: Results: Raw Data Spectral Intensity
Low spectral intensity (SI) observed due to the dye absorbing the light. Note: The mockup was filled with dyed water first then purged.
More light passes through the region of interest therefore increasing the SI

## Slide 9: Results: Transparency
Spectral Transparency (ST)- ratio of collected light to emitted light
ST nears 1-> region becomes more transparent

## Slide 10: Results: Integrated Relative Transparency
Integrated each time step which contains spectral intensities for each wavelength from 350nm to 846nm to get one number.
  150 points show in figure above. (0.1s sample rate)
It takes 10s to exchange the volume given an incoming flow rate to the feedthrough of 1.9LPM
Or 3.2 exchanges per liter of incoming water.
Time to exchange volume=~10s

## Slide 11: Results: Integrated Relative Transparency
6 exchanges per minute of operation @ 1.9LPM
3.2 exchanges per liter of incoming water
360 exchanges per hour

## Slide 12: Conclusion
Water test was successful
  Measured 6 volume exchanges per minute or 360 volume exchange per hour of operation at 1.9LPM
  3.2 exchanges per liter of incoming fluid
360 exchanges per hour is greater than the Fluorine ions generated on an hourly basis (5PPM/hr) when exposed to radiation.
The fluorine ion production of the entire system will be investigate further to see if it is below 3PPM (Hazardous to humans and likely equipment) given 1.9LPM flowrate.
Test the setup with FC-40 to estimate the volume exchange of the region.
Link to Paper: https://ipac2019.vrws.de/papers/wepmp044.pdf