## Slide 1
Matthew Alvarez (FNAL), Yoshitsugu Arakaki (JPARC), Bruno Balhan (CERN), Jan Borburgh (CERN), Noah Curfman (FNAL)
July 24, 2019
ICFA Mini-Workshop on Slow Extraction Workshop: Engineering Session Summary

## Slide 2: Outline
Septum Wire Deflection Under High ES Field
Frame Adjustment Bar Test
CNT Wire Inspection and HV Testing
Recirculating HVF Water Test
Alternative Material Choices to Reduce Activation of Extraction Equipment
Motion System Selection

## Slide 3: Septum Wire Deflection Under High ES Field - CERN

## Slide 4: Wire deflection measurement setup
Under vacuum ZS equipped with upstream flange viewport.
Optical system installed to allow observation of the wire due to the electrical field; cross hair aligned on the wire centre.
Displacement could not be measured directly due to the angle between the wire array and the line of sight.
Using the radial displacement system of the anode, the anode position was manually adjusted to line up the wire with the previously set cross hair of the theodolite.

## Slide 5: Wire deflection measurement
Wires 󠄍ø [µm] | Calculated at 11 MV/m | Measurement at 12.5 MV/m | 
100 | 31 | 51 | 45
60 | 154 | 120 | 105
Wires 󠄍ø [µm] | Calculated at 11 MV/m | Measurement at 12.5 MV/m | 
100 | 31 | 51 | 45
60 | 154 | 120 | 105

## Slide 6: Derived deformation along Z
Derived upstream wire deformation along Z at nominal field.
80 mm

## Slide 7: Conclusions
Septum straightness measured at construction better than 20 µm.
Wires being deflected towards cathode due to E-field.
ZS tank alignment survey does not take into account the offset.
Analytic calculation of wire deflection was done; wire deflection directly proportional to the spring load.
Diameter of the wire not really taken into account in the formula, not intuitive. Too simplified?
Measurement of the deflection done; more deflection than anticipated.
Fluka simulations show that the varying wire deflection at the extremities of the anode do not influence the extraction efficiency too much.

## Slide 8: Alternative Material Choices to Reduce Activation of Extraction Equipment-CERN

## Slide 9: Activation in operation for various tank/anode material combinations
Chart: Global radiation hazard factor for a ZS tank in operation
| inox/invar | inox/inox | inox/ti | Al6061/Invar | Al6061/Inox | Al6061/Ti | Al5083/Ti | Al2219/Ti | Ti/Invar | Ti/Inox | Ti/Ti
Case 2: Activation occuring at 10 cm lateral disctance to the target | 139.7405 | 123.6028 | 103.5067 | 85.917 | 69.7792 | 49.6831 | 50.4632 | 51.2432 | 95.8916 | 79.7538 | 59.6577
First estimates obtained using ActiWiz [2].

## Slide 10: Measuring and Maintaining Septum Frame Rail Straightness (MI-52 Septum)-FNAL

## Slide 11: MI-52 Electrostatic Septa
12ft. (3.7m) in length
0.004in (.1mm) W25Re Wires under 2.9N of tension
0.1in (2.54mm) wire spacing
Intentionally bowed 0.006” (0.15mm) out of true
-100kV cathode

## Slide 12: Initial Measurement Results
Frame is 0.0047” (4700μin) bowed out of true
Stabilized conditions would improve measurement quality
  Prohibitively expensive to achieve at this time

## Slide 13: Effect of Wire Retainer Bolt Torques

## Slide 14: Stepping motor system (SPS diffuser)

## Slide 15: Stepping motor system features
Precise resolver/motor combination
Ball screw back-lash compensated by vacuum force. Linearity n.a.
Position step size 5 µm
Mechanical position with respect to tank mid-plane
Needs possibly regular calibration
Minimal torque available when not powered
Max. torque available limited
Absolute system precision dominated by calibration system
Notes: Regular calibration: to be confirmed when used in operation over longer periods

## Slide 16: JPARC ESS Foil and Rail Flatness

## Slide 18
Surface of the yoke
Ribbons
Floating (Small dust might be caught between ribbon and surface of yoke)
Twisted
The difective ribbons were exchanged to new one.
Upper side
Down side
Center

## Slide 19
Result of alinement error of the ribbons seen from standard
The effective thickness of the ribbons are 30+28=58μm
Titanium ESS1
Center
Upper side
Down side

## Slide 20: Frame Adjustment-FNAL

## Slide 21: Frame Adjustment
Frame has a convex curvature relative to the optical head
Strong back/ Adjustment bar capable of flattening the profile of the frame by 30um with 40kg (87lb) load
Unistrut Channel
Frame
F=43lbs
F=43lbs
Optical head

## Slide 22: CNT Wire Investigation and Preliminary HV Testing-FNAL

## Slide 23: DexMat vs. JPARC CNTs
Smoother Surface
Easy to Cut with Scissors
Round Profile
  Dia. 76-80um
Breaking Load 3.3N~3.5N
Course Surface
Required wire Snips to cut the wire
Elliptical Profile
100 um ±30um
Breaking Load: 6.45 ± 1.87N
JPARC CNT using SEM
DexMat CNT using SEM

## Slide 24: High Voltage Testing of DEXMAT CNTs

## Slide 25: High Voltage Testing of DEXMAT CNTs
CNT wires did not allow me to reach 100kV
Knowing that the CNTs had a coarse profile and potential whiskers, we conditioned the CNTs by spoiling vacuum (5e-5 torr to 5e-4 torr)
  We achieved 33kV over
Currently we do not see any difference between HV CNTs vs. new wires….will investigate the CNTs tested in HV soon.

## Slide 26: CNT Wires in HV Environments
HV Test Wire
New Wire

## Slide 27: CNT Wires in HV Environments

## Slide 28: Recirculating HVF Water Test-FNAL

## Slide 29: HVF- Water Test
We create 5ppm/hr of fluorine ions that recombine into HF and PFIB.
We found that it takes 10s to exchange the volume to achieve a relative transparency of 1.
3.6 volume exchanges per liter of incoming water