## Slide 1: A compact, low-field, broadband mode launcher for X-band DLA structures
Yelong Wei*, Alexej Grudiev
CERN, European Organization for Nuclear Research
Email: yelong.wei@cern.ch
1

## Slide 2: Outline
2
Research progress on the dielectric disk accelerating (DDA) structures operating at TM02 π-mode
Design of a compact, low-field, broadband mode launcher
Tolerance studies
    Geometry sensitivity
    Sensitivity for corner defects
Summary & Outlook

## Slide 3: Outline
3
Research progress on the dielectric disk accelerating (DDA) structures operating at TM02 π-mode
Design of a compact, low-field, broadband mode launcher
Tolerance studies
    Geometry sensitivity
    Sensitivity for corner defects
Summary & Outlook

## Slide 4: DDA Structures-TM02 π-mode
4
D. Satoh, et al. Phys. Rev. Accel. Beams 19, 011302 (2016)
High order mode operation reduces the wall power loss;
The electromagnetic fields can be controlled by dielectric parts;
High power efficiency.

## Slide 5: Regular cell (original-type)
Transverse magnetic fields
Longitudinal electric fields
Electric energy density
Magnetic energy density
Most of the RF energy is stored in the vacuum region;
The total RF loss including both the wall loss on the conducting cylinder and dielectric loss in the DDA structure can be drastically reduced, thereby resulting in both an extremely high quality factor and a very high shunt impedance at room temperature.
5

## Slide 6: Further optimization and consideration (modified-type)
6
Fillet the dielectric corner with a radius of 1.0 mm to reduce the / 2.0 ;
Add a gap between ceramics for evacuation with a gap of 0.25 mm;
Add a dielectric to improve thermal contact.
Optimum parameters | Original | Modified
Dielectric constant εr | 9.64 | 9.64
Dielectric loss tangent δ | 6E-6 | 6E-6
Inner radius r0 [mm] | 3.15 | 3.15
Outer radius c1 [mm] | 20.5 | 20.5
a1 [mm] | 11.10 | 11.10
b1 [mm] | 13.16 | 13.50
d1 [mm] | 2.0 | 2.0
L1 [mm] |  | 5.0
x1 [mm] |  | 0.9
z1 [mm] |  | 0.7
Structure period length L [mm] | 12.50 | 12.50
Phase advance | 180° | 180°
Acceleration mode | TM02 π-mode | TM02 π-mode
Frequency [GHz] | 11.9969 | 11.9949
Unloaded Q0 | 134542 | 112639
r’/Q0 [Ω/m] | 6089 | 5488
r’ [MΩ/m] | 819 | 618

## Slide 7: RF to beam efficiency for CLIC main linac
18
RF properties | CLIC-G (26 regular cells, damped) | Original DDA (1 cell) | Modified DDA (1 cell)
Dielectric loss tangent δ |  | 6E-6 | 6E-6
Acceleration mode | 2π/3 | TM02 π-mode | TM02 π-mode
Shunt impedance r’ [MΩ/m] | 92 | 819 | 618
Peak input power [MW] | 61.3 | 1.64 | 1.69
Loaded gradient [MV/m] | 100 | 100 | 100
Filling time [ns] | 67 | 110 .6 | 135.8
[ns] | 155.6 | 155.6 | 155.6
RF to beam efficiency | 28.5% | 53.0% | 47.0%
RF properties | CLIC-G (26 regular cells, damped) | Original DDA (1 cell) | Modified DDA (1 cell)
Dielectric loss tangent δ |  | 6E-6 | 6E-6
Acceleration mode | 2π/3 | TM02 π-mode | TM02 π-mode
Shunt impedance r’ [MΩ/m] | 92 | 819 | 618
Peak input power [MW] | 61.3 | 1.64 | 1.69
 | 100 | 100 | 100
 | 67 | 110 .6 | 135.8
 | 155.6 | 155.6 | 155.6
RF to beam efficiency | 28.5% | 53.0% | 47.0%
7
Design of the CLIC main linac accelerating structure for CLIC Conceptual Design Report, Proceedings of LINAC2010, A. Grudiev, W. Wuensch.

## Slide 8: Considerations on the maximum number of cells
Reference: Nagle, Knapp and Knapp, 1964 and 1968
Bandwidth
To avoid mode overlapping: ;
The frequency separation for modes: ;
;
Maximum number of cells can be 255
8

## Slide 9: Short-range Wakefields
DDA-TM01 (Standing Wave)
DLA-TM01
DDA-TM02 structure shows lowest short range Wakefields: abour 2/3 of the CLIC-G
CLIC-G: 28*8.332 ↔ DDA TM02-π: 18*12.5, so the number of regular cell is 18, no end cells are included;
Convergence studies: dx = dy = dz = 0.05 mm;
Bunch charge Q = 1.0 nC, bunch sigma = 1.0 mm, offset = 0.5 mm.
Charge Density
DDA-TM02-original (Standing Wave)
CLIC-G-42
9
DDA-TM01
CLIC-G
DLA-TM01

## Slide 10: Outline
10
Research progress on the dielectric disk accelerating (DDA) structures operating at TM02 π-mode
Design of a compact, low-field, broadband mode launcher
Tolerance studies
    Geometry sensitivity
    Sensitivity for corner defects
Summary & Outlook

## Slide 11: An X-band DLA structure
11
 | CLIC-G iris structure (undamped) | MCT-16
Dielectric constant |  | 16
Dielectric loss tangent |  | 0.0001
Structure length [mm] | 8.33 | 8.33
Phase advance | 120° | 120°
Inner radius [mm] | 3.15 | 3.0
Outer radius [mm] |  | 4.675
Frequency [GHz] | 11.9943 | 11.9984
Unloaded | 7245 | 2468
[Ω/m] | 15924 | 9489
[MΩ/m] | 115 | 23
/c | 0.018 | 0.068
/ | 2.4819 | 1.069
/ [dielectric] |  | 1.0
Power required to generate 100 MV/m [MW] | 45.0 | 287
 | CLIC-G iris structure (undamped) | MCT-16
 |  | 16
 |  | 0.0001
Structure length [mm] | 8.33 | 8.33
Phase advance | 120° | 120°
 | 3.15 | 3.0
 |  | 4.675
Frequency [GHz] | 11.9943 | 11.9984
 | 7245 | 2468
 | 15924 | 9489
 | 115 | 23
 | 0.018 | 0.068
 | 2.4819 | 1.069
 |  | 1.0
Power required to generate 100 MV/m [MW] | 45.0 | 287
Longitudinal Electric fields

## Slide 12: An X-band mode launcher for DLA structures
DLA structure material? One more slide about DLA structure design is needed
, loss tangent δ = 0.0001;
mm, mm;
Working frequency GHz
Matching section????
Using existing design of the X-band mode launcher for metallic prototypes (Converting TE10 mode into TM01 mode)
Output circular waveguide has a diameter of 21.9 mm
21.9 mm
12

## Slide 13: Standard methods for matching between a DLA structure and a circular waveguide
13
Circular waveguide has a radius of mm;
DLA has a inner radius mm and outer radius mm;
Two methods are being used:
  Quarter wavelength waveguide;
  A matching cell.
(1) Quarter wavelength waveguide
(2) A matching cell

## Slide 14: S Parameter Simulation
f = 11.9933 GHz
S11 = -48 dB
14
f = 11.9942 GHz
S11 = -54 dB
Good S11 can be achieved;
Further simulation studies are needed to reduce the maximum field in the matching sections.

## Slide 15: Adding dielectrics into matching section
f = 11.9936 GHz
S11 < -42 dB
15
L1 = 1.82 mm, D2 = 3.135 mm;
The maximum field in the matching section is lower than in the DLA, but still pay special attention to the fields in the corners.
Bandwidth is much larger and it is limited by the waveguide cut-off frequency

## Slide 16: Electric fields in the corners
There are two peak fields in the corner 1 and dielectric corner 2, respectively;
We need to reduce these two peak fields;
16
Corner 1
Corner 2
Corner 3

## Slide 17: Adding a skew angle θ for Corner 1
17
90°
85°
75°
70°
60°
45°
37.08°
For each skew angle, it is perfectly matched with a S11 < -40 dB;
The peak fields in the corner 1 are decreased with a smaller skew angle θ;
When , the peak fields in the corner 1 equal to the accelerating fields in the DLA structure; is a critical skew angle;
is chosen for the following optimization.
65°
80°
55°
50°
40°

## Slide 18: Fillet Corner 2 at a skew angle of 60°
2.0 mm
18
0.5 mm
1.0 mm
1.5 mm
For each curve, it is perfectly matched with a S11 < -40 dB;
The peak fields in the corner 1 are decreased with a larger fillet radius ;
2.0 mm is chosen for the following optimization.
Corner 3
2.0 mm

## Slide 19: Chamfer Corner 2 at a skew angle of 60°
19
3.0 mm
2.5 mm
2.0 mm
1.5 mm
1.0 mm
0.5 mm
For each curve, it is perfectly matched with a S11 < -40 dB;
Only when 2.0 mm, the peak fields in the corner 2 equal to the accelerating fields in the DLA structure.
2.0 mm

## Slide 20: Skew angle θ = 60°, Fillet Corner 2 with a radius = 2.0 mm
20
Fillet Corner 3 with a radius of 0.5 mm;
The peak fields in the Corner 1, Corner 2 and Corner 3 are greatly reduced so that the maximum fields are located in the DLA structure;
For S11 < -30 dB, the bandwidth = 12.0216 GHz -11.9680 GHz = 53.6 MHz;
For S11 < -20 dB, the bandwidth = 12.0855 GHz -11.9131 GHz = 172.4 MHz
f = 11.9943 GHz
S11 = -45.4 dB

## Slide 21: Whole X-band mode launcher
21
f = 11.9978GHz
S11 = -42.3 dB
Input power from klystron (Peak power: MW, repetition rate: 100 Hz, pulse width: 100 ns), the average power is 1 kW.
The power loss in dielectrics is 32 W for a DLA with length of 10 cm; The power loss in surface copper is 1.87 W.

## Slide 22: Outline
22
Research progress on the dielectric disk accelerating (DDA) structures operating at TM02 π-mode
Design of a compact, low-field, broadband mode launcher
Tolerance studies
    Geometry sensitivity
    Sensitivity for corner defects
Summary & Outlook

## Slide 23: Geometry Sensitivity
f = 11.9950 GHz | dB | dB | dB
mm | [-0.008, +0.006] mm | [-0.014, +0.012] mm | [-0.024, +0.023]
mm | [-0.020, +0.015] mm | [-0.033, +0.028] mm | [-0.056, +0.053] mm
 | [-, +] | [-, +] | [-, +]
mm | [-0.041, +0.048] mm | [-0.078, +0.080] mm | [-0.150, +0.133] mm
mm | [-0.062, +0.052] mm | [-0.120, +0.092] mm | [-0.190, +0.159] mm
mm | [-0.006, +0.009] mm | [-0.011, +0.015] mm | [-0.019, +0.029] mm
mm | [-0.008, +0.006] mm | [-0.015, +0.011] mm | [-0.028, +0.019] mm
Dielectric constant | [-0.077, +0.078] | [-0.135, +0.144] | [-0.242, +0.268]
f = 11.9950 GHz |  |  | 
 | [-0.008, +0.006] mm | [-0.014, +0.012] mm | [-0.024, +0.023]
 | [-0.020, +0.015] mm | [-0.033, +0.028] mm | [-0.056, +0.053] mm
 | [-0.041, +0.048] mm | [-0.078, +0.080] mm | [-0.150, +0.133] mm
 | [-0.062, +0.052] mm | [-0.120, +0.092] mm | [-0.190, +0.159] mm
 | [-0.006, +0.009] mm | [-0.011, +0.015] mm | [-0.019, +0.029] mm
 | [-0.008, +0.006] mm | [-0.015, +0.011] mm | [-0.028, +0.019] mm
 | [-0.077, +0.078] | [-0.135, +0.144] | [-0.242, +0.268]
is most sensitive to , , and ;
is least sensitive to , , , , ;
Really depends on the fabrication tolerances and dielectric material.
is not taken into account because it is a geometry form existing prototype.
23

## Slide 24: Outline
24
Research progress on the dielectric disk accelerating (DDA) structures operating at TM02 π-mode
Design of a compact, low-field, broadband mode launcher
Tolerance studies
    Geometry sensitivity
    Sensitivity for corner defects
Summary & Outlook

## Slide 25: Sensitivity for corner defects
0.02 mm
0.01 mm
0.02 mm
25
< -40 dB for both 0.01 mm and 0.02 mm at frequency of 11.9950 GHz;
So 0.02 mm can still be accepted in the practical fabrication in consideration of electric fields.

## Slide 26: Summary & Outlook
26
Further optimization and wakefield studies on DDA TM02 π-mode structure;
Collaboration with ANL researchers for the fabrication studies of the DLA prototypes.
DDA structures operating at TM02 π-mode structure:
  Extremely high quality factor and shunt impedance: Q0 = 134542, r’ = 819 MΩ/m for original-type and Q0 = 112639, r’ = 618 MΩ/m for modified-type;
  High RF-to-Beam efficiency of 50%;
  The number of acceleration cells can be up to 255 due to high bandwidth;
  Low short-range wakefields.
A compact low-field, broadband mode launcher has been designed:
  The maximum fields are located in the DLA structure;
  Good reflection coefficient with S11 < -40 dB has been achieved;
  Geometry sensitivity has been carried out.