## Slide 1: Breakdown study with short rf pulse at awa
drhgfdjhngngfmhgmghmghjmghfmf
Maomao peng
Visiting student at AWA from Tsinghua University
August 21-23, 2019
AWANOW Workshop
Argonne, IL
Mission Statement:
Developing the science and technology of electron beam generation, manipulation and acceleration for beam-driven wakefield acceleration and other applications.

## Slide 2: Outline
Background and motivation
Long pulse high power test-stand at Tsinghua University
Short pulse generation at AWA
Single-cell design for high gradient test
Experiment plan
Summary

## Slide 3: Background and motivation
RF breakdown
- One of the main limitations of high gradient structures
- Gradient could be improved by using shorter RF pulse
Argonne Flexible Linear Collider (AFLC)
- >250 MV/m with 20 ns rf pulse (CLIC: 100 MV/m, 200 ns)
Jing C, Kanareykin A, Schoessow P, et al. in Proceedings of IPAC2013.
Grudiev A, Calatroni S, Wuensch W. PRST-AB, 2009, 12(10): 102001.

## Slide 4: Background and motivation
Power extractor
Beam
Metallic/ DLA/ DDA structures for breakdown study and accelerating
Short RF pulse
1st stage
2nd stage
Proposed study
- Single cell test with long pulse (100 ns – 1.5 μs) from klystron with compressor
- Single cell test with short pulse (<10 ns) from beam-driven power extractor

## Slide 5: High power test stand at Tsinghua
Parameters |  | Unite | Value
Repetition rate |  | Hz | 40
Frequency |  | GHz | 11.424
Output power | w.o. PC | MW | 50
 | w. PC |  | 
 |  |  | 200
Pulse width. | w.o. PC | ns | 1500
 |  |  | 100
 | w. PC |  | 
Faraday Cups
structure
Pulse compressor
Modulator
Klystron
TPoT-X (Tsinghua X-band high Power Test stand)
- Accelerating structure high power test
- Breakdown study
- Cathode test (planning)

## Slide 6: Short pulse generation at awa
Parameters |  | Value
Aperture diameter | mm | 17.6
Group velocity |  | 0.22
Shunt impedance |  | 3.92
Length | cm | 30
Quality factor |  | 6500
Pulse width | ns | 3
Expected power | 8 bunches, 30 nC/bunch | 117 MW
 | 8 bunches, 60 nC/bunch | 471 MW
Parameters |  | Value
Aperture diameter | mm | 17.6
Group velocity |  | 0.22
Shunt impedance |  | 3.92
Length | cm | 30
Quality factor |  | 6500
Pulse width | ns | 3
Expected power | 8 bunches, 30 nC/bunch | 117 MW
 | 8 bunches, 60 nC/bunch | 471 MW
Regular cells
Matching cells
Metallic power extraction and transfer structure (MPETS)
- 11.7 GHz, 9th harmonic of AWA’s beam frequency
- 2π/3 mode, consists of 36 normal cells, 2 matching cells, 2 couplers

## Slide 7: Short pulse generation at awa
Diagnostics
Integrating current transformers (ICT): charge and transmission
rf probe: generated and reflected rf power
YAG screens: beam transverse profile
ICT2
Experimental layout

## Slide 8: Short pulse generation at awa
1 bunch
waveform
power
8 bunch
1 bunch
8 bunch
Experimental results
- 8-bunch train, maximum charge of 500 nC, 100% transmission
- Maximum power of 280 MW, 44% lower than simulation
- Power loss due to multipacting of the RF pickup
Downstream pickup
Upstream pickup

## Slide 9: Short pulse generation at awa
Multipacting of the pickup
- May have caused power loss in previous experiments
- Issues: short distance between two openings; short distance between probe
and openings; in-vacuum environment
Newly designed directional coupler
- Waveguide-to-SMA connector installed in air
- Currently under fabrication at Tsinghua
Jing C, Antipov S, Conde M, et al. NIMA, 2018, 898: 72-76.
Shao J, Jing C, Wisniewski E, et al. arXiv:1907.01069, 2019.

## Slide 10: Single-cell design for high power test
Position
Time
dt
dz
Field probes
Port 1
Port 2
Calculation of accelerating gradient
- Only consider the field synchronized to the beam
; dt = dz/c;

## Slide 11: Single-cell design for high power test
Input RF
Center of the cavity
Over all gradient
Comparison between long pulse and short pulse
- The gradient with short pulse (<10 ns from the power extractor) is ~80% of
the steady state
120 ns long pulse
10 ns short pulse
Average
Peak

## Slide 12: Single-cell design for high power test
Parameters (elliptical ) | Unit | Value
Resonate frequency | GHz | 11.7001
Iris | mm | 6.1
Iris thickness | mm | 2.9
Cavity length | mm | 8.541
Mode |  | 
Filling time | ns | 2.5
Group velocity | c | 0.0114
Gradient @ 400 MW, 100ns RF | MV/m | 348
Gradient @400 MW, 3 ns RF | MV/m | 273
Q |  | 6072.5
r/Q |  | 14047.9
Es/Ea |  | 1.59
Parameters (elliptical ) | Unit | Value
Resonate frequency | GHz | 11.7001
Iris | mm | 6.1
Iris thickness | mm | 2.9
Cavity length | mm | 8.541
Mode |  | 
Filling time | ns | 2.5
Group velocity | c | 0.0114
Gradient @ 400 MW, 100ns RF | MV/m | 348
Gradient @400 MW, 3 ns RF | MV/m | 273
Q |  | 6072.5
r/Q |  | 14047.9
Es/Ea |  | 1.59
Optimized results
- Compromise between vg and r/Q
- Elliptical iris used for lower surface field

## Slide 13: Experiment plan
High power generation at AWA (2020.02)
- Improve previous results with the newly designed directional coupler
Single cell test at AWA (2020.03)
Single cell test (scaled from 11.7 GHz to 11.424 GHz) at Tsinghua (2020.05)
RF breakdown study of X-band DLA and DDA (2020)

## Slide 14: Summary
The study aims to explore high gradient structure performance with short RF pulse and compare with that using long pulse
The long pulse experiment is planned at Tsinghua University with klystrons with pulse compressor
The short pulse experiment is planned at AWA with X-band power extractor
- 280 MW power generated, will be further improved with direction coupler
- Single-cell metallic disk-loaded structure design completed, aiming to achieve
250 MV/m gradient with low BDR
The high power at AWA will also enable high gradient research for other structures (DLA, DDA, DAA, PBG, metamaterial, etc.)

## Slide 15
Thank you!