## Slide 1: Brazeless Accelerator R&D
Sergey Antipov
Euclid Techlabs LLC

## Slide 2: Introduction
Phase I SBIR grant from DOE – DNN (PM Dr. Donald Hornback)
Based on Euclid’s Patent US9913360B1
9 month project duration
RF Design of 1 MeV accelerator
Mechanical design
Full fabrication
Microwave tuning
… High power conditioning to designed gradient of 12 MV/m!
Notes: Shortest development cycle in PI – SA 15 years experience. Dealing with multiple vendors with their lead times, especially brazing

## Slide 3: Brazeless accelerator benefits: cost + flexibility
Conflat – like technology + batch copper plating
Structure cost ~ $20K
Additional embedded features in brazeless assembly. A) Efficient heat spreader channel cooling. B) Halbach array magnetic optics. C) Traditional permanent magnet quadrupole
Copper plating is robust
Notes: Take time to explain the assembly
Take time to explain benefits like exotic cooling, built in magnets, etc.

## Slide 4: 1 MeV Standing wave accelerator
1 MeV
9 GHz
π - SW
12 MV/m
200kW

## Slide 5: Engineering
1 MeV, ~9 GHz, π – SW, 12 MV/m, 200kW
partikelaccelerator
Notes: Lego accelerator
Ikea accelerator: partikelaccelerator, röntgenmaskin – if gamma ray production

## Slide 6: Initial microwave testing and tuning
1 MeV Brazeless accelerating waveguide prototype
Chart: Frequency, GHz
Before plating
After plating
Transmission
Notes: Shift due to undercompression [if asked]. Good place to point out, that we don’t care to have exact frequency – magnetron is broadband

## Slide 7: Initial microwave testing and tuning
Chart: Coordinate along the structure
Field balance tuning
initial
final
Chart: frequency, GHz
Reflection
Notes: Field balance tuning is done by honing stainless steel structure.
Same process as refurbishing car engine cylinders
Thin copper plating does not change field balance.
After all said and done – S11 with excellent coupling

## Slide 8: High power test
pump
magnetron
copper plated brazeless structure
RF tract
reflection \
transmission monitoring
2.5e-7 HPa achieved

## Slide 9: BRAZELESS SPLIT BLOCK
CONDITIONED TO 12 MV/m

## Slide 10: BRAZELESS SPLIT BLOCK IDEA

## Slide 11: 1 MEV BRAZELESS SPLIT BLOCK

## Slide 12
1 MEV SPLIT BLOCK DESIGN

## Slide 13
1 MEV SPLIT BLOCK TESTING

## Slide 14: Brazeless Power Extractor at the AWA

## Slide 15: INDEPENDENT CELL + WAVEGUIDE COMBINER
e-beam
*Low Loaded Q=225 for short pulse wakefield

## Slide 16: BRAZELESS SPLIT BLOCK ENGINEERING
SS – knife edge
1.33 CONFLAT
Copper bottom half
e – beam

## Slide 17: Power extraction simulation

## Slide 18: Double-cell power extractor
e-beam
e-beam

## Slide 19: Power extractor performance parameters
Parameters | Q=25 nC | Q=50 nC
RF Frequency | 11.7 GHz | 11.7 GHz
Q-factor | 220 | 220
Bunch train frequency | 11.7/9 GHz | 11.7/9 GHz
Bunch length | 1.2 mm | 1.8 mm
Max. surface E-field | 530 MV/m | 1030 MV/m
Max. surface H-field | 1.23 MA/m | 2.38 MA/m
Pulsed temperature rise | 65 | 240
Shunt impedance 1 cell/4 cells | 88 k/325 k | 88 k/325 k
Pulse duration | 10 ns | 10 ns
Output power (4 cells) | 240 MW | 900 MW

## Slide 20: Engineering of the split block

## Slide 21: Summary
Brazeless split blocknew – high gradient brazeless technology!
Power extractor for the AWA (11.7GHz, 10ns, 900MW) designed
Structure is being fabricated
Looking forward to test at the AWA !
Funded by DOE SBIR Phase II
AWA Staff
My group at Euclid:
Sergey Kuzikov
Pavel Avrakhov
Edgar Gomez
Ed Dosov
Acknowledgement
Collaborator
Alexander Vikharev IAP (Russia)