## Slide 1: Experiments with Metallic Metamaterial Structures for Wakefield Acceleration
Xueying Lu, Julian F. Picard, Michael A. Shapiro, Ivan Mastovsky, Richard J. Temkin
Massachusetts Institute of Technology (MIT)
Manoel Conde, John G. Power, Jiahang Shao, Eric E. Wisniewski,
Maomao Peng, Gwanghui Ha, Jimin Seok,
Argonne National Laboratory (ANL)
Chunguang Jing
Euclid Techlabs LLC
August 21, 2019
AWA Needs and Opportunities Workshop
Lemont, IL

## Slide 2: Outline
Introduction
Metamaterial Design and Theory
Stage I Experiment
Stage II Experiment
Conclusions

## Slide 3: Metamaterials
Metamaterial (MTM):
  An artificial material with a subwavelength structure
  Exhibits properties not usually found in natural materials
  Especially a negative refractive index : simultaneous ε, μ < 0
Metamaterial with split ring resonators on dielectric boards*
Left-handed materials
  Negative refraction
* S. Antipov et al., J. Appl. Phys. (2008)

## Slide 4: Reversed Cherenkov Radiation
Cherenkov Radiation
  Electron velocity exceeds wave phase velocity
  ε, μ > 0
  Wave vector and energy flow parallel
Reversed Cherenkov Radiation
  ε, μ < 0
  Wave vector and energy flow anti-parallel
Hongsheng Chen and Min Chen. "Flipping photons backward: reversed Cherenkov radiation." Materials Today 14.1-2 (2011).

## Slide 5: Motivation
Science:
  Verify reversed Cherenkov radiation in a metamaterial structure from a direct measurement
Application:
  High power microwave generation for wakefield acceleration in both collinear and two-beam acceleration regimes
  All-metal structure to survive high RF power

## Slide 6: Experimental Setup at AWA
Diagnostics:
ICT (Integrating current transformer): Bunch charge
YAG screen:
Bunch transverse size
RF probes:
Output microwave

## Slide 7: Outline
Introduction
Metamaterial Design and Theory
Stage I Experiment
Stage II Experiment
Conclusions

## Slide 8: Wagon Wheel Structure Unit Cell
Wagon wheel structure
  Periodic subwavelength structure
    Period: 2 mm
    Free space wavelength at 11.42 GHz: 26 mm
  Negative group velocity
  Fundamental mode: TM mode
  Interaction frequency: 11.42 GHz
    Cutoff frequency of an empty waveguide: 14.2 GHz
Dispersion Curve
Stainless steel
Copper

## Slide 9: CST Simulation
CST Wakefield solver, single bunch
  45 nC, σz = 1.2 mm
26 MW steady state in the backward port
Much lower power in the forward port
  Reversed Cherenkov radiation
Analytical theory:
= 25 MW
Beam
Backward Port
Forward Port
Simulation

## Slide 10: Electric Field Structure
“Artificial dielectric” structure with all metal
  Similar “bouncing feature” of the electric field in the wagon wheel structure and a dielectric tube
  Very easy to tune the effective dielectric constant with the huge parameter space in the metamaterial design
Dielectric tube
Wagon
Wheel

## Slide 11: Advantages of Wagon Wheel Structure
Rugged all-metal structure
Enhanced beam-wave interaction
  Large beam aperture => low shunt impedance, high group velocity
  Small beam aperture => high shunt impedance, low group velocity
  MTM with negative group velocity: High group velocity and high shunt impedance at the same time
Structure | Beam aperture (mm) | Group velocity | r/Q (kΩ/m) | Output power1 (MW)
Wagon wheel | 6 | -0.158 c | 21 | 25
Alumina-loaded tube | 6 | 0.106 c | 10 | 13
1 Output power is calculated for a single 45 nC drive bunch.

## Slide 12: Outline
Introduction
Metamaterial Design and Theory
Stage I Experiment
Stage II Experiment
Conclusions

## Slide 13: Single Bunch Experiment
High RF power from a single 45 nC bunch
  Experiment: 25 MW
  Simulation: 26 MW (steady state)
  Analytical theory: 25 MW
Reversed Cherenkov radiation verified
  Coherent radiation at 11.4 GHz
  Backward port has much more power
100 GSa/s, 16 GHz BW scope
Lu et. al., PRL 122, 014801 (2019).

## Slide 14: Stage I Highest Power Shot
Two bunches with a total charge of 85 nC
80 MW extracted RF power
50 MV/m decelerating electric field
  75 MV/m available accelerating gradient for a possible witness bunch

## Slide 15: Outline
Introduction
Metamaterial Design and Theory
Stage I Experiment
Stage II Experiment
Conclusions

## Slide 16: Stage II Experiment: Design
Design goal: achieve higher RF power / gradient from a train of 8 bunches with a rep rate of 1.3 GHz
Longer structure: 100-cell structure (20 cm long), 11.7 GHz
Higher total charge in the bunch train: > 200 nC
8-bunch Train
To Output Ports

## Slide 17: Stage II Experiment: Preliminary Results
RF pulse shape and frequency spectrum agree well with beam simulations.
Highest power is estimated to be 380 MW peak from 224 nC in 8 bunches
  110 MV/m gradient
1-bunch spectrum
8-bunch spectrum
8-bunch power

## Slide 18: Conclusions
Two wagon wheel metamaterial structures at X-band have been tested at the Argonne Wakefield Accelerator as power extractors.
Reversed Cherenkov radiation has been verified in a metamaterial structure with a negative group velocity.
High microwave power was generated, in agreement with analytical theory and CST simulations.
  Stage I (40-cell structure): Two bunches, 85 nC, 80 MW, 50 MV/m decelerating gradient, 75 MV/m accelerating gradient
  Stage II (100-cell structure): Eight bunches with a total charge of 224 nC, estimated peak power of 380 MW
Wagon wheel structure has unique advantages for wakefield acceleration
  Rugged all-metal structure, no dielectrics
  Enhanced beam-wave interaction

## Slide 19: Acknowledgement
Funding agency:
ANL: U.S. Department of Energy, Office of Science under Contract No. DE-AC02-06CH11357.
MIT: U.S. Department of Energy, Office of Science, Office of High Energy Physics under Award Number DE-SC0015566.
ANL
MIT