## Slide 1: Charge Particle Detection by Detuning of a Microwave Resonator
Sergey Antipov
Euclid Techlabs

## Slide 2: Concept: diamond beam halo monitor
Tungsten/carbon wire
Intercepts charge
scan
Main beam
Resonator
scan
Diamond wire / blade
Halo
Diamond: radiation hard material with excellent thermal properties
limited by the damage threshold of these materials
scan
scan
Change in resonator
properties = halo signal

## Slide 3: Example: green laser peak power measurement using silicon in a resonator
Resonator
515nm laser
silicon
S11 measurement (reflection)

## Slide 4: Measurement considerations
Non-linear measurement
Sensitive element – dependent
Time-domain measurement
Retuning of the cavity
Sensitivity
Correlation of signal to charge
Scanning patterns

## Slide 5: Diamond membranes
We are ablating diamond to produce thin 10-20 um membranes (drum heads).
We also can polish diamond to few-nm Ra roughness

## Slide 6: Halo Measurement Resonator Design 9.2 GHz

## Slide 7: Engineering design

## Slide 8: Insides: All – UHV vacuum compatible
UHV sma feedthrough (accuglass)
UHV kapton sma cable inside (accuglass)
Huntington linear actuator
Copper cavity
UHV sma connector (accuglass)
Aluminum adaptor
Vented screws, vacuum relief, etc..
In-vacuum RF cable is a problem!

## Slide 9: “Simplified” resonator – no scanning

## Slide 10: “Simplified” resonator fabricated and tested

## Slide 11: “Simplified” resonator fabricated and packaged
The plan is to have a simple preliminary measurement

## Slide 12: Controller (RF Box)

## Slide 13: Baby Halo Monitor test result (beam energy 10 keV; beam current 4.6 uA; RP 100 Hz)
DC gun Voltage DC gun Current Halo Monitor signal

## Slide 14: Fluorescence on diamond
S. Antipov, S. Stoupin measured at 1BM APS, 2015
For example, a 15-micron-thick diamond screen will transmit 90% of the x-ray flux at 5 keV.
At 8 keV, a very comfortable 60-micron thickness can be used.
~50 um diamond beam position monitors are commercial product

## Slide 15: Microwave resonator design

## Slide 16: Engineering: UHV design!
diamond

## Slide 17: Overall device for experiment at CHESS
No experiment due to CHESS schedule

## Slide 18: Fabricated device
Replace stainless steel part with 3D printed plastic one for bench tests (to preserve knife edge)

## Slide 19: Bench testing
Measurement at the AWA-ACT?

## Slide 20: Testing at the AWA: two options
“Baby” resonator ~ Faraday Cup
Simple, easy
End of beamline
Available in UHV configuration
X-ray resonator
More involved,
Dedicated installation (blocking beam)
Flourescence + beam measurement = publication – worthy
Ready in split block form

## Slide 21: Summary
Beam measurement via resonator detuning
Faraday cup configuration
BPM + charge measurement
Scanning for halo measurement
Funded by DOE SBIR Phase I
AWA Staff
My group at Euclid:
Sergey Kuzikov
Pavel Avrakhov
Edgar Gomez
Ed Dosov
Ernie Knight
Acknowledgement
Collaborator
Alexander Vikharev IAP (Russia)