## Slide 1: EUCLID/AWA COLLABORATIVE WORK ON ADVANCED WAKEFIELD ACCELERATOR DEVELOPMENT
Alexei Kanareykin,
Euclid Techlabs LLC
On behalf of Euclid Techlabs/AWA collaboration
AWA Needs and Opportunities Workshop
August 21-23, 2019, Argonne National Lan, Lemont IL

## Slide 2
Euclid Techlabs LLC
Euclid TechLabs LLC, founded in 1999 is a company specializing in the development of advanced materials and new designs for beam physics and high power/high frequency applications. Additional areas of expertise include dielectric structure based accelerators, pulsed electron microscopy, and "smart" materials technology and applications.
www.euclidtechlabs.com
Fermilab
IARC
Euclid Techlabs
Argonne
2 offices: Bolingbrook, IL (lab) and Gaithersburg MD (administrative).
Tight collaborations with National Labs: Argonne, Fermi, CERN, BNL, JLab.
Actively participate in Accelerator Stewardship DOE Program

## Slide 3
LAB FACILITY IN BOLINGBROOK IL
11,000 sq ft - total
2,000 sq ft – office
9,000 sq ft - lab
Compact electron accelerator test facility (bunker)
Time resolved TEM beamline
Clean room/magnetron sputtering (TiN, copper, dielectrics)
Field Emission cathode DC test stand
Femtosec laser
RF lab
…other beam physics related equipment - www.beamphysics.com
ANL/AWA accelerator, ANL/CNM - cathodes, ANL/APS- diamond based X-ray optics
Jlab and Fermi: SRF tests
15 PhDs,
22 staff total
2 locations: Chicago IL and Maryland/DC

## Slide 4
Key Euclid’s technologies:
Ultra-compact low energy accelerator (dielectric based)
Stroboscopic pulser for Transmission Electron Microscope
Electron guns for accelerators: Photo-, thermo-,
field emission (FE)- and (new !) SRF guns.
Ferroelectric based fast tuner.
UNCD based FE cathodes.
Accelerator components (RF windows, couplers…)
Other beam physics instrumentation.
Fast ferroelectric 400 MHz tuner successfully tested at CERN
L-band RF window
for AWA ANL
5 GHz kicker for TEM, BES/NIST

## Slide 5
How we collaborate ?
Ideas, Projects, Proposals
Materials,
Technology
Design,
Prototype
Fabrication,
Cold Test
Beam test,
High power,
Paper…
AWA/Euclid, funded by HEP/SBIR
Commercialization ?
Other project funded by
HEP, BES, NP, NIH, DHS …
Product ? Never directly … HEP is fundamental science !

## Slide 6
History: Research on Dielectric Wakefield Accelerating structures, since 2001
Experiments with DWFA were done by Euclid Techlabs at Argonne,
Externally powered dielectric structure: Naval Research Lab
designs: 7-26 GHz
scalable to THz
Brookhaven, SLAC

## Slide 7
Scheme I---Single
Triangular Bunch
Scheme II---Ramped
Bunch Train
Reference: Bane et. al., IEEE Trans. Nucl. Sci. NS-32, 3524 (1985)
Reference: Schutt et. al., Nor Ambred, Armenia, (1989)
z
d
d
W
-
W
+
d
r
(z)
C. Jing et al., PRAB 14, 021302 (2011)
B. Jiang et al., PRAB 15, 011301 (2012)
TR=3.4
K. L. F. Bane, SLAC-PUB-3662 (1985)
V.Tsakanov, EPAC 88), Rome, Italy, 1988, 1040
Transformer Ratio Enhancement for Collinear Wakefields
Theory
Experiment

## Slide 8: Highest Measured Transformer Ratio
R @ 122 GHz
4.65 (measured)
4.51 (wake fcn)
R @ 131 GHz
4.94 (measured)
4.86 (wake fcn)
Q. Gao et al., PRL 120, 114801 (2018)
5 nC / 48 MeV
Triangle
z
z
Train
Rectangle
z
Trapezoid
z
Train
y
Triangle
y
Rectangle
y
Trapezoid
y
AWA Group, C.Jing of Euclid Techlabs

## Slide 9
Configuration used for the pulse-shaping simulations using a S-band rf gun (a). A temporally shaped laser pulse (b) is optimized to result in a photoemitted electron-beam with current profile (c).
F. Lemery and P. Piot. Phys. Rev. Accel. Beams 18, 081301 (2015).
The method that relies on the extraction of shaped bunches directly from the photocathode of a photoinjector, where it provides full flexibility of bunch shape in the transverse bunch particle distribution as well.
Laser Pulse Shaping Method for TR Increase
I Kuzmin, …A.Kanareykin et al. Laser Physics Letters, V.16, N1, 2018
A.Kanareykin, AAC’2018, Breckenridge, CO, 12-17 August 2018
SBIR HEP, 2018

## Slide 10
 G. Loisch et al., Phys. Rev. Lett. 121, 064801 (2018)
Time [ps]
No Plasma
np ~ 2x1013 cm-3
To achieve flexible temporal shaping of the laser pulse a Šolc fan filter type of configuration was employed. In the PITZ laser pulse shaper the initial 0.7 ps long (RMS) Gaussian laser pulse is split into 14 quasi-pulses that are individually delayed and coherently added to form a longitudinal laser profile of tunable shape and a length of 20 ps (measured as the delay between first and last pulses.
G. Loisch et al. NIM-A, 2018
TR=4.6
Laser Pulse Shaping Method for TR Increase,, DESY, Zeuthen, Germany

## Slide 11
What is next?
2018
2013
2008
2023
2028
Transformer ratio
AWA activities for high transformer ratio
RBT, DWFA, First demo
RBT, DWFA, 3.4
Triangular, DWFA, 3.5
Triangular, DWFA, 5
Triangular, PWFA, 6, 100 MeV/m
Triangular, DWFA, 10
CWA demo module
with R=5
EEX shaping
demonstration
Gwanghui Ha. Talk at AAC, 2018.

## Slide 12: Staging Demonstration at AWA (2017)
11.7 GHz metallic iris loaded structures
70 MeV/m
C. Jing et al., Nucl. Instr. Meth. in Phy. Res. A 898, 72-76 (2018)

## Slide 13: Two-beam acceleration experiment (2017)
11.7 GHz metallic iris loaded structure
300 MW
150 MeV/m
C. Jing et al., Nucl. Instr. Meth. in Phy. Res. A 898, 72-76 (2018)

## Slide 14
The 26 GHz Full Dielectric Short Pulse TBA Test (2018)
DLA
DPETS
ID=7mm, L=30cm
ID=3mm, L=10cm
55MW rf power output were measured.
1.8MeV witness energy gain, eqv. to 54MeV/m gradient.
Note: RF power/gradient is lower than the ideal case due to the combination of RF loss in the waveguide, miss-match of the phase advance, and inefficient rf coupling, etc.

## Slide 15
The 11.7GHz Dielectric PETS (2018)
High power test
200 MW generated with 8-bunch train, total 360 nC
No rf breakdown observed
Possible factors for reduced power:
1. Bunch length
2. Launching phase
3. Multipacting in rf
pickup
J. Shao, C. Jing, E. Wisniewski, et al., submitted to PRAB

## Slide 16: Dielectric Disk Accelerator (DDA) Collaboration with CERN (12 GHz)
High order mode operation reduces the wall power loss;
The electromagnetic fields can be controlled by dielectric parts;
High power efficiency.
One can adjust r0, c1, D and εr to get the desired frequency of 12 GHz.
Such a structure has a periodicity L which can be used to slow down the group velocity of accelerating mode.
The group velocity for a DDA TM01-mode structure gradually decreases to 0;
The phase shift generate a low group velocity
12 GHz structure to be fabricated by Euclid/AWA and tested at CERN
Talk by Yelong Wei, CERN

## Slide 17: The Accelerator in a Suitcase for Isotope Replacement and for Active Interrogation Systems
Description:
  The project is to demonstrate a 1 MeV dielectric accelerator based suitcase X-ray source and also produce a cost-effective and compact medium energy (~4 MeV) design. Till present, the 1MeV dielectric accelerator is ready for assembling and bench test. Expected output: (prototype in 2019)

## Slide 18: Diamond Structure High Gradient Test at AWA
factor 4.5 field enhancement
50nC  250 MV/m
S.Antipov et al. Diamond and Related Materials, 2014.
35 GHz diamond polycrystalline structures

## Slide 19: Diamond X-Ray Lens
Laser ablation of diamond for x-ray lens
X-Ray Optics Group (APS)
S.Antipov
Diamond Beam Halo Monitor, AWA
Electrodeless measurement of the charged particle-induced conductivity in the diamond
S.Antipov
DC gun Voltage DC gun Current Halo Monitor signal
Diamond scraper for halo sensing
Measurement: resonator detuning due to beam interception in active element
Laser power measurement with silicon switch

## Slide 20: ACT AWA TEST OF AN IRIS DIAPHRAGM DETECTOR
Euclid is developing an iris diaphragm detector (PI: Ao Liu, # SC0019538) for beam profile and halo measurements. A very cost-effective, highly-compact, efficient direct measurement apparatus.
Version alpha experiments at ACT test the charge current collection ability of blades with different stopping power and thickness, checks the ceramic plate insulation, vacuum compatibility, signal extraction, etc.
contactor
insulated
from
holder
holder
(mounts to rotary feedthru)
YaG and W
holder insulated
from adapter
Linear
feedthru
adapter
Cable guide
YaG
Proof-of principle done, AWA
Version Beta to be tested!
(version alpha)

## Slide 21: Laser ablation of copper for 250 GHz corrugated waveguide
Courtesy of A. Zholents (APS)
Brazeless Power Extractor for AWA
8 bunches 50nC  11.7 GHz, 10ns, 900 MW
S.Antipov
S.Antipov
Soft x-ray FEL facility with an array of collinear wakefield accelerators:

## Slide 22
Traveling Wave Gun, funded by HEP 2019
Breakdown decreases with reduction of the RF pulse length. To mitigate the breakdown problem and enable large charges to be generated in a high gradient field at the cathode, Euclid Techlabs proposed to develop an ultra-high gradient electron gun fed by a very short RF pulse.
Power extractor installed in the AWA beam line to be used for the TW Gun prototype testing.

## Slide 23
UNCD Field Emission Cathodes
S.Baryshev, Phase I, BES, 2014
In collaboration with E.Simakov, LANL
High Quantum Efficiency UNCD Photocathode.
G.Chen et al. , APL, 2019
K. Quintero et al. APL, 2014
S.Baryshev, Phase II NP, 2015-2018
SRF Test BNL

## Slide 24
History: Tunable Ferroelectric-Based Accelerator
ε(E) for ferroelectric dielectric composite
NONLINEAR CERAMIC
US patent 8,067,324
US patent 7,768,187

## Slide 25
The first ever FE-FRT test with a superconducting cavity has been performed and successfully demonstrated frequency tuning. The timescale in which the FE-FRT is able toshift the cavity frequency across the entire tuning range was measured to be < 50 𝜇s, this is significantly faster than any other cavity tuning device. A maximum frequency tuning of ≈ 12 Hz was observed with an applied voltage of 3 kV, this could easily be increased by coupling more power to the tuner.
Fast Tuner Testing, CERN 2019
A case study of an FE-FRT applied to PERLE show RF power could be reduced by a factor of ≈ 15.
Direct observations of the frequency shift caused
by the FE-FRT made with the signal analyser.
PERLE- Powerful Energy Recovery LINAC, Orsay

## Slide 26
Phase II 2016 Ferroelectric Tuner results

## Slide 27: Ceramic with Increased DC Conductivity
The main innovation: a new low-loss microwave ceramic material with a increased DC electrical conductivity and low loss tangent. The electrical conductivity will drain the field-emission induced charge away. The low loss tangent will allow realizations of high efficiency RF power transmission.
We developed technology for sintering Mg,Ti oxide materials providing lower loss tangent ceramics in the GHz frequency range, and exhibiting 2–3 orders of magnitude increased conductivity (102 –103 times).
We observed and studied the interesting new phenomenon of abnormal ~104 conductivity increase of the developed MgTi ceramic in the 250C–1000C temperature range, while the loss tangent variation at 1000C did not exceed a 20% change compared to the room temperature value.
Motivated by dielectric structure development for AWA, funded by NP for RF windows application

## Slide 28
DC beam test using TEM DC gun:
DC 200 kV electron beam for charging testing
DC 200 kV BEAM CHARGING TEST OF CERAMIC
We are currently carrying out beam tests on the developed ceramic. Using the 200-keV DC gun available at the Euclid lab facility, we are exposing two types of ceramics to the DC beam: the standard MgTi ceramic and our new (Mg,Ti) ceramic with increased conductivity. The goal of the ongoing experiments is to quantitatively study the charging – discharging mechanism of the MgTi.

## Slide 29
Beam Charging Test Results
The beam images at the downstream YAG, which were captured at different times. T=0 second represents the turn-on time of the DC beam: with the regular ceramic sample beam disappeared in 15 sec, with the new MgTi ceramic it is stable in hours…

## Slide 30
100 MHz - 10 GHz Stroboscopic Solution for Ultra-Fast Electron Microscopy
Commercial contract with NIST, installed and operational
Funded by BES PII and PIIA,
Currently is installed at BNL,
and is being commissioned
First presentation of the Strobo -
TEM at M&M Conference, Portland OR

## Slide 31
Commercialization
www.euclidtechlabs.com
Latest Noticeable Contracts:
NIST (2016-2018) – “Time Resolved TEM” GWU (2017) – “UNCD Emission Chamber” UMD (2016-2018) – “Single Crystal Diamond FET” SJTU (2016-2019) – “Photoinjector”, “Thermionic Gun”
Two periods: 2003-2014 - spinoff from Argonne Wakefield Accelerator group (DOE SBIR) 2014- now - commercialization of advanced material technologies and TEM.
11 patents +5 currently in progress
JEOL, Inc. installation at the US facility, then BNL and NIST
Fast Ferroelectric Based Tuner
- Phase II 2016 Nuclear Physics
Tuner is purchased, installed and tested in 2019 by CERN, SRF’2019 invited talk by CERN. 80MHz – new project !

## Slide 32
Summary
Our collaboration is…
researchers,
ideas, and projects,
materials and technologies,
design and prototyping,
beam or high power testing,
.. and commercialization, if we are really, really lucky….

## Slide 33
Acknowledgments
DOE, Office of Science High Energy Physics:
L.K.Len, Ken Marken, John Boger, Eric Colby
DOE Office of Science, Basic Energy Science,
Eliane Lessner
DOE, Office of Science Nuclear Physics:
Michelle Shinn, Manouchehr Farkhondeh
Argonne National Laboratory, HEP,
Manoel Conde, John Power and AWA Group