## Slide 1
Rob Ainsworth
FAST/IOTA Collaboration Meeting and Workshop on High Intensity Beams in Rings
10 June 2019
Fermilab Complex Beam Physics Challenges

## Slide 2: Outline
Accelerator Complex
Challenges
  Beam physics
  Operational

## Slide 3: Accelerator complex
H- linac
Booster
  h = 84
  15 Hz
  400 MeV -> 8 GeV
Recycler
  h = 588
  Slip-stack 12 batches (double bunch intensity)
Main Injector
  8 GeV -> 120 GeV

## Slide 4
Beam Physics Challenges

## Slide 5: Space charge
Large space charge tune shifts/spreads are expected
Crossing multiple resonances

## Slide 6: Resonances in Recycler
Current working point

## Slide 7: Resonance correction schemes being tested

## Slide 8: Resonance correction schemes
Currently implementing resonant correction schemes in the RR
3Qx correction has been demonstrated
  Unwanted side effect causes unexplained losses during operational cycle

## Slide 9: Impedances
Transverse impedance in RR and MI are dominated by resistive wall
Bunch by bunch dampers protect against coupled bunch instabilities
A different kind of damper is needed for slip-stacking
For slip-stacking, the growth rate for the sum mode (bunches performing the same motion) is much larger than the difference mode [Burov]
  A lower bandwidth damper looking at the envelope could be sufficient

## Slide 10: Slip stack damper
The current bandwidth of the damper is 2.5 MHz
  To what intensity will this be sufficient to damp?
  Can the bandwidth be increased further?
Damper
Landau

## Slide 11: Fast instability - electron cloud
A fast instability was observed in the Recycler but not in the Main Injector
Growth too fast to be stabilized by dampers
Eventually, attributed to electron trapping in the combined function magnets
Instability has been conditioned away for now
At what intensity will it reappear?
Observed on BPMs, growth rate 10-15turns
S. Antipov

## Slide 12: Transition crossing

## Slide 13: Gamma-t jump
Transverse loss

## Slide 14: Transition Crossing
For PIPII, a large dp/p is expected
  gamma-t jump is planned
So far simulations only include space charge
Need to add impedances
  Will try to measure longitudinal impedance on MI
  Compare with simulations

## Slide 15: Halo/Tails
As intensity is increased
  Tails and halo will become more and more important
Need to understand what generates halo/tails
Currently, only method of measuring tails in collimator scan
  Slow
  Destructive
Need better diagnostics capable of measuring transverse tails/halo

## Slide 16: Operational Challenges

## Slide 17: Collimation
For 700 kW operation, access to tunnels is already becoming problematic
High activity in leads to component damage
  Loss ion pumps making vacuum worse -> higher losses
MI8 line
  Design spec, 1% of 5E12 at 10 Hz
  Currently running, ~1% of 4.5 E12 at 15 Hz
  Need to add more collimators in MI8 line
MI30 collimators
  Inside Main Injector, most take care of longitudinal losses from slip-stacking
  Plan to add inserts

## Slide 18: Two machines in the same tunnel
Recycler
Main Injector

## Slide 19: Two machines in the same tunnel
Loss identification becomes more difficult

## Slide 20: RF
Power limits
  Current limit 54E12 (NuMI target limit). This corresponds to 777 KW with 1.33 sec cycle time.
  MI is limited by the available RF power to 62E12 which corresponds to 892 KW with 1.33 sec
  Dual PA upgrades will increase this to 1.24E13 (1.784 MW)
Beyond this
  New cavities
  New PAs
  Space requirements become an issue

## Slide 21: Aperture
Old
New
RR not designed to be a proton stacker and such apertures are a big problem
Limiting apertures are at lambertson locations
Efforts made to improve apertures in certain areas
Issues still exist particularly at RR to MI extraction

## Slide 22
Summary

## Slide 23: Beam Physics Challenges
Space charge
  Tune shifts crossing resonances
Impedances
  To what intensity will slip-stack damper work?
    Need more bandwidth?
    What’s the highest bandwidth before slipping causes a problem
Electron Cloud
  Instability may return, what intensity?
Transition crossing
  Gamma-t jump will help
Halo
  Controlling losses at high power

## Slide 24: Operational challenges
Collimation
  Tunnel access already difficult at 700 kW
Two machines in the same tunnel
  Identifying losses
  Space requirements
Apertures
  Major loss locations occur at Lambertsons (Transfers)
  RR pipe is small
Instrumentation
  How measure tails/halo?

## Slide 25: Backup

## Slide 26: Effect with other sextupole powered

## Slide 27: 222 bump scan

## Slide 28: Beta-wave comparison

## Slide 29: Effect on 6+6
SC222 off
SC222 on at -10A

## Slide 30: Effect with bump
SC222 on at -10A
SC222 on at -10A, with bump
Loss at 232C unaffected

## Slide 31: Slip-stacking
Slip-stacking allows us to double the intensity of the bunches in the Recycler

## Slide 32: Slip-stacking
Gap clearing kickers fire before every injection sending beam to abort

## Slide 33: Gamma-t jump
Effectively cross transition quicker using ramped quads
2 quads (0.85 T-m/m) in the arc
1 quad (1.7 T-m/m) in the straight section

## Slide 34: Gamma-t jump
The quad triplets perturb the lattice
  large beta-wave
May have potentially adverse effects on transverse phase space
At max of 0.5 unit jump