## Slide 1
Nikita Kuklev
IOTA/FAST 2019 Collaboration Meeting
10 June 2019
IOTA Instrumentation

## Slide 2: Motivation
Showcase of existing and potential instrumentation
We have a lot of things
But...if we don’t have it, you can BYOD (bring your own devices)
Most systems are modular and easy to work with - add-ons just slot in

## Slide 3: Outline
IOTA ring – geometry and design
Control and readout
Devices
  BPMs
  Sync-Light – cameras + PMTs
  WCM/DCCT/other
  BYOD

## Slide 4: IOTA design
SL
BPM
DCCT
WCM

## Slide 5: IOTA design
8 bending magnets – 4x30 + 4x60
Vacuum chambers with extra windows
Various drift regions (some have gate valves, easy in/out)
Individually powered magnets (all except main bend)
Variety of extra connections
No need for rad-hard components

## Slide 6: IOTA design
Mechanical design is centrally managed (TeamCenter/NX)
Can provide models for all necessary parts
Oftentimes spares available for testing (even main bends)

## Slide 7: IOTA design
Lattice files in standard MAD-X format (+other)
  Central, authoritative repository
  Consistent design base + history

## Slide 8: Outline
IOTA ring – geometry and design
Control and readout
Devices
  BPMs
  Sync-Light – cameras + PMTs
  WCM/DCCT/other

## Slide 9: Readout + control
Main control network – ACNET…bit old school
Has a library of devices/drivers (optical flippers, digitizers, etc.)

## Slide 10: Readout + control
Do not fear – there are Python and Java wrappers
Masks most ACNET things, and unifies data acquisition
Have been playing with internal EPICS deployments, and can set one up for your devices
Complimentary fire department late night support included

## Slide 11: Readout + control
Spare cables of all varieties
  Heliax/RG58 (coax)/HV/mystery
  Ethernet + PoE + fiber
  AC/DC power up to few kW
  (Most) are labeled!
Internal network w/ control room access
  Can provision devices internally instantly
  Or more permanently in a few hours, accessible from anywhere via VPN
Portable networked scopes and digitizers available

## Slide 12: Outline
IOTA ring – geometry and design
Control and readout
Devices
  BPMs
  Sync-Light – cameras + PMTs
  WCM/DCCT/other
  BYOD

## Slide 13: BPMs
21 electrostatic button BPMs
Turn-by-turn or orbit (averaging) modes

## Slide 14: BPMs
Modular design, analog front-end + 250MS/s digitizers
  Equivalent to modern commercial ones, like Libera Brilliance+
Can feed/fan out signals to your own readout

## Slide 15: BPMs
During run 1, it had a number of quirks
  Linearity
  Random reboots/hangs
Performance was current/drift dependent
  Sufficient for tune measurements, but not LOCO
Many lessons learned, expect major improvements in run 2
  Advantage in having experts on site for support

## Slide 16: BPMs
Key (upgraded) specs for users:
  GigE readout (<<1s)
  8k+ turns
  <100um TBT
  <10um ORM
  Good linearity (or high sensitivity)
  Fully integrated into control system
  ‘Just works’

## Slide 17: Sync-Light
Each main bend has a base station with optics + camera
A variety of addons are installed – PMTs, diodes, etc.
Many parts custom CNC/3D printed
But all optics and mounting standard
Dog is listed as mission critical
Multi-anode PMT as a turn-by-turn BPM
G. Stancari

## Slide 18: Sync-Light
Live control room readout through DAQ server cluster
  Direct to disk saving and remote access
Exquisite precision for orbit measurement, <100nm statistical
Strongest constraints on LOCO

## Slide 19: Sync-Light
Dynamic range from mA to single electron
G. Stancari
PMT
Camera
A. Romanov

## Slide 20: Sync-Light
Extensions to low-emittance beams (slits/polarizers)

## Slide 21: Sync-Light
Can focus on different sources (edge interference)
Can use for insert alignment (OSC)

## Slide 22: DCCT/WCM/other
DCCT for current measurements
  Noisy, improvements in progress
WCM
  Can be used for longitudinal profile measurements, finding bucket loading
Beam loss monitors
  Never tripped, no hotspots
  They silently judge bad injections
Main bucket
Hitchhiker
50uA current, with 3-5uA noise

## Slide 23: BYOD
Many things can be changed quickly for custom devices
Case studies: edge radiation and undulator fluctuations
Both experiments took over a single SL station
  Installed within a day, most prep work beforehand
  Easy access for alignment and fixes (~60 mins beam to beam)
“Perhaps we have stared too long at this abyss.”
Brendan O’Shea, SLAC, 2019
I. Lobach

## Slide 24: Summary
IOTA is a flexible research ring, with flexible instrumentation
All basic capabilities are there – X/Y/Z profile/TBT position, current, losses, etc.
For custom devices, there is info/models for remote design and simulations, to optimize on-site time for actual data collection
Have an idea? Ask!