## Slide 1: IOTA Nonlinear Integrable Optics Experiment: Landau Damping
Nathan Eddy
Fast/IOTA Collaboration Meeting
10 June 2019

## Slide 2: Motivation/Theory
Landau Damping provides damping mechanism via tune spread
Octupoles provide a means to increase tune spread and increase the stable region via Landau Damping
Octupoles introduce strong non-linearities at large amplitudes
  Reduce dynamic aperture and lifetime
  Landau damping sensitive to tails of beam
  Can change chromaticity via feed-down effects

## Slide 3: Feedback System Overview
Use horizontal button electrodes on E2L bpm with 32db RF pre-amplifier on each button
BPM analog module based upon RF envelope detector conditions fast doublet into longer pulse – provides 32db of programmable gain control
Implement 1 turn notch filter delay and phase delay with cable
Use one plate of the horizontal strip-line to kick beam
E2L Button
BPM
Horizontal
Kicker
BPM
Analog
Module
Diff
Amp
Diff
Amp
1 Turn
Delay
32db
55db
Phase
Delay
~800ps
~20ns
~20ns
~Position
20db
Att
A,B
A
B

## Slide 4: Relevant Parameters
Parameter | Value
RF Frequency | 30.034 MHz
Harmonic Number | 4
Revolution Frequency | 7.508MHz
Revolution Time | 133ns
Ring Circumference | 3997cm
Stored Beam Orbit Tune (nx) | 5.30
Synchrotron Tune | 50-60kHz
Kicker Cable | 370ns
BPM Cables | 180-270ns
Feedback System (cables, amps) | 125ns

## Slide 5: BPM Selection
Have fixed minimum delays from cables and electronics
Select BPM candidates based upon estimated delays and expected tune to achieve approximately 90 degree phase advance from pickup to kicker for optimal performance
  Our minimum delay is 5-6 turns depending on pickup
  Very sensitive to tune (nominal nx=5.3)
BPM E2L was selected as a candidate with correct phase advance which was not critical to other BPM studies

## Slide 6: Commissioning – Beam Transfer Function
Injection Tunes
Before
Pre-amp
After
Pre-amp

## Slide 7: Commissioning – BTF after Phasing for Positive Feedback
1st
Harm
2nd
Harm
Lower Sideband
Upper Sideband

## Slide 8: Inducing Instability – Positive Feedback
Instability triggered by changing gain in analog module
Ability to provide relatively controlled instabilities

## Slide 9: Instability Threshold Study
Study the gain threshold for fast instability as a function of beam current and octupole current
With nominal emittance (~160-170um), step the feedback gain until a fast instability occurs (>10% beam loss)
The analog module attenuators were stepped in 1-2db steps until a fast instability occurred
After each instability, wait for synchrotron radiation damping to restore beam to nominal emittance

## Slide 10: Instability Threshold vs Gain
See approximately factor of 2 increase in the instability threshold with octupoles at 2A as compared with 0A

## Slide 11: Instability Octupoles 0A
Sum Signal
Kick Signal
Kick Signal Zoom

## Slide 12: Instability Octupoles 0A – 1st Harmonic

## Slide 13: Instability Octupoles 0A – Growth Rate
Growth Rate 195 Turns

## Slide 14: Instability Octupoles 0A – Frequency Analysis

## Slide 15: Instability Octupoles 2A
Sum Signal
Kick Signal
Kick Signal Zoom

## Slide 16: Instability Octupoles 2A – 1st Harmonic
Kick Signal
Kick 1st Harm
All Harm
1st Harm

## Slide 17: Instability Octupoles 2A – Growth Rate
Growth Rate 64 Turns

## Slide 18: Instability Octupoles 2A – Frequency Analysis

## Slide 19: Summary
See the expected effect that the octupoles at 2A increase the stable region by a factor of 2
Analysis of the time domain data of the instabilities shows faster growth rate for 2A vs 0A – this is not currently understood
Plan to implement a digital system which will provide better mechanisms to control the gain and phase to study the instabilities
Can also use BTF measurements to further the study stability diagram and chromaticity