## Slide 1
Vladimir SHILTSEV , with input from Sergey Striganov
IOTA/FAST Collaboration Meeting and Workshop on High Intensity Beams in rings
June 12, 2019 - Fermilab
Opportunities for Crystal Acceleration Research at FAST

## Slide 2: Motivation: “Ultimate” Colliders
Post-100 TeV “Energy Frontier” assumes
  300-1000 TeV (20-100 × LHC)
  “decent luminosity” (TBD)
Surely we know:
For the same reason there
is no circular e+e- collider above
Higgs-F there will be no circular pp
colliders beyond 100 TeV  LINEAR
2. Electrons radiate 100% beam-strahlung (<3 TeV) and in focusing channel
(<10 TeV)  µ+µ- or pp

## Slide 3: “Phase-Space” is Further Limited
“Live within our means”: for 20-100×LHC
  < 10 B$
  < 10 km
  < 10 MW (beam power, ~100MW total)
New technology should provide >30 GeV/m @
total component cost <1M$/m ( ~NC magnets now)
SC magnets equiv. ~ 0.5 GeV per meter (LHC)
3. Only one option for >30 GeV/m known now: dense plasma that excludes protons only muons

## Slide 4
Idea- Tajima & Dawson, Phys. Rev. Lett. (1979)
Plasma wave: electron density perturbation
Laser/beam pulse ~ p/c
Option B:
Short intense laser pulse
~1018cm-3, 50 GV/m over 0.1m
Plasma Waves
Option A:
Short intense e-/e+/p bunch
Few 1016cm-3, 6 GV/m over 0.3m
First looks into “Plasma-Collider”: staging kills ! <E>~2 GV/m,ε

## Slide 5: Novelty of the Approach: Acceleration in Continuous Focusing Channel
1024 cm-3 100 TV/m, λp~0.03µm
Synchtrotron radiation losses balance energy gain:
0.3TeV for positrons
10 000 TeV for muons (+)
1000 000 TeV for protons
1022 cm-3 10 TV/m, λp~0.3µm

## Slide 6: Linear +- Crystal X-ray Collider
1 PeV = 1000 TeV
n ~1000
nB ~100
frep ~106
L ~1030-32
V.Shiltsev, Physics-Uspekhi 55 (10), 965 (2012)

## Slide 7: What Do We Know about Crystals?
Strong inter-planar electric fields ~10V/A=1GV/cm
Very stable, can be used for
  deflection/bending (works)
  focusing (works )
  acceleration (if excited)
T980 experiment at Tevatron, N.Mokhov et al JINST 6 T08005 (2011)
~92.5+-5% efficiency
Or l_d ~ 5mm/0.025 < 0.2m

## Slide 8: 4 mm Si in LHC
~2 mrad at 7 TeV
~99.5% efficiency
Or l_d ~ 4mm/0.005=0.8m
Bent Crystals in the 7 TeV LHC Beams

## Slide 9: Ways to excite the crystal (1)

## Slide 10: Crystal Excitation by X-Rays
Tajima,Cavenago, Phys. Rev. Lett. 59 (1987), 1440
Need 40keV high peak power x-rays
  now available from SASE FELs like LCLS
Gradients >1GV/cm
Muons preferred
  No bremstrahlung, no nucl.
+ rad length 10^9 cm
  total energy~10^9 GeV

## Slide 11: …several other ways were proposed (short bunches, ion clusters, dislocations, etc)… Excite Nanotubes/Crystals (5) by Self-Mod’n Instability in long(er) charge particle beams

## Slide 12: AWAKE

## Slide 14: TOPICS FOR STUDIES (WORKSHOP’19)
overview of the past and present theoretical developments toward crystal acceleration, ultimate possibilities of the concept
concepts and prospects of PeV colliders for HEP
effective crystal wave drivers : beams/SMI*, lasers , other
beam dynamics* in crystal acceleration
instabilities in crystal acceleration (filamentation*, etc)
acceleration in nanostructures (CNTs*, etc)
muon sources* for crystal acceleration
application of crystal accelerators (Xray sources, etc)
steps toward "proof-of-principle" : 1 GeV gain over 1 mm, open theory questions, modeling and simulations
possible experiments at FACET, FAST, AWAKE, AWA, or elsewhere
* can be studied at FAST

## Slide 15: Ultimate Testbed

## Slide 16: FACET-II Beams
Compression X Y Z 8x7x2 um , 2 nC 
  n_e~0.6e19 cm-3
Compression X Y Z 2x2x0.4 um , 2 nC 
  n_e~2e20 cm-3
Peak currents:
  70…100…300 kA !

## Slide 17: Weibel (Filamentation) Instability

## Slide 19: FACET-II
Proposal #43: Beam filamentation and bright gamma-ray
bursts
  Sébastien Corde(ÉcolePolytechnique/LOA)
  Ken Marsh (UCLA)
  Frederico Fiuza (SLAC)

## Slide 20: MUON PRODUCTION AND CHANNELING
Advanced schemes
Simplified schemes (for FAST/FACETII)
e-
Thick
target
Upto 2 r.l.
π-+
μ-+
e-
Thin
target
~0.1 r.l.
π-+
μ-+
e-
γ
crystals &
detectors
10 cm C
½ r.l.

## Slide 21: Secondary particle production 300 MeV electron on 2 radiation length of carbon target
Courtesy S.Striganov

## Slide 22: Positive pions has very big positron/proton escort, large angle & high momentum; negative pion could be focused and extracted
Courtesy S.Striganov

## Slide 23: More pion could be obtained for larger thickness & low Z. target material. Larger thickness – large radiation problem, low Z - longer target (more difficult to collect)
Courtesy S.Striganov

## Slide 24: Low radiation scenario
Two production targets – photon production and pion/muon production.
Photon production target should be thin (~10% radiation length). Primary electrons can be swept and miss pion/muon target – compact muon source design (Nagamine at al 2001).
They made analytical estimate for 10% tungsten photon and 10 cm carbon pion/muon production target. For pion produced at 45 degree with acceptance 1 steradian and momentum from 150 to 163 MeV/c they got 3.5 10-9 π/electron in 2001 (4.7 10-8 π/electron in 2016). Our simulation shows that at 45 degree pions have heavy electron/positron escort, but at 90 degree we could get 3.7 10-8 negative pion/electron in above angular & momentum range. With such two target design we could get about 3 times more pion then with one 10% radiation length carbon target.
Large Omega muon optics channel could capture pion beam with dE=10 MeV and dΩ=1 steradian and produce 0.4 muon/pion.
Courtesy S.Striganov

## Slide 25: 2015-2017 CRYSTAL CHANNELING EXPT @ FAST
P.Piot, T.Sen, A.Halavanau, D.Edstrom, J,Hyun, et al
helpful experience

## Slide 26: Summary
Acceleration of muons in crystals/CNTs has great promise
There are many issues related to muon production, channeling and acceleration
Some modes of the crystal/CNT excitations can be tested at FACET-II – eg by SMI
Beam filamentation is of serious concern and can be studied at, e.g., FAST
  Past experience and hardware very helpful
Also can be tried at FAST : i) muon production; ii) muon detection; iii) experiment integration; iv) calibration of models
“Workshop on Acceleration in Crystals & Nanostructures” will take place at Fermilab, June 24-25 – please, join!

## Slide 27: Thank You for Your Attention!

## Slide 28: High Energy μ+μ- Colliders
Input #120
JINST Special Issue (MUON)
μμ @ 14 TeV
=
pp @ 100 TeV
Advantages:
μ’s do not radiate / no beamstrahlung acce-leration in rings  low cost & great power efficiency
~ x7 energy reach vs pp
  US MAP feasibility studies were very successful  MCs can be built with present day SC magnets and RF; there is a well-defined path forward
  ZDRs exist for 1.5 TeV, 3 TeV, 6 TeV and 14 TeV * in the LHC tunnel
Key to success:
  Test facility to demonstrate performance implications - muon production and 6D cooling, study LEMMA e+-45 GeV + e- at rest +-- , design study of acceleration, detector background and neutrino radiation
Offer “moderately conservative - moderately innovative” path to cost affordable energy frontier colliders:
* more like “strawman” parameter table
MNewPhysics = sqrt(s)/2

## Slide 29: Ways to excite the crystal (2)
Ways to excite the crystal (2)

## Slide 30: Ways to excite the crystal (3)

## Slide 31: Ways to excite the crystal (4)
Controlled generation of dislocations

## Slide 32: Nanotubes(1)

## Slide 33: Nanotubes (2)

## Slide 34: Combine (funnel) Channels

## Slide 35: SMI: Self-Modulation Instability (in 400 GeV protons)

## Slide 36: Self-Modulation Instability in AWAKE p+ Bunch

## Slide 37: Collider considerations
i.e. irrelevant