## Slide 1: Measuring Nonlinear Decoherence in IOTA
C. Hall

## Slide 2: Acknowledgements
RadiaSoft: David Bruhwiler, Nathan Cook, Jonathan Edelen, Stephen Webb
Fermilab: FAST/IOTA Collaboration, Nikita Kuklev, Alexander Romanov, Sebastian Szustkowski, Alexander Valishev

## Slide 3: Introduction
Measurements of decoherence taken with/without nonlinear magnet in IOTA
Decoherence measurements in the base lattice provide interesting look at initial beam distribution
  Infer energy spread
  Evidence of strong IBS
Comparison of nonlinear decoherence data to simulations is ongoing

## Slide 4: Experiment Setup
Horizontal Kicker
Vertical Kicker
‘elliptical’ nonlinear magnet

## Slide 5: Baseline Results
Damping of the centroid motion after a kick from decoherence
Several different kick amplitudes shown
Bunch normally kicked in x and y to measure both tunes (ideally)

## Slide 6: Analyzing Decoherence Rate
Tune-dependence on amplitude
Chromaticity-induced
Octupole strength:
Initial kick strength:
Normalized centroid amplitude by turn:
R. E. Meller et al., SSC-N-360
C. X. Wang, “Measurement and Application of Betatron Modes with MIA”,
in Proc. 20th Particle Accelerator Conf. (PAC'03)
Angle:

## Slide 7: Nominal Energy Spread
Single-particle, equilibrium energy spread is not well matched to damping data
Current: 1.68 mA

## Slide 8: Adjusted Energy Spread
Increasing energy spread provides much better comparison to data
Higher energy spread from IBS
a = 8e-3 m-1 or < 0.005 maximum tune shift
Current: 1.68 mA

## Slide 9: Estimated IBS Energy Spread
σ𝛅 = 2.36
1.68 mA
J.D. Bjorken, S.K. Mtingwa, “Intrabeam Scattering,” Part. Acc. Vol. 13, 1983, 115-143.
Calculation in elegant of expected equilibrium energy spread including IBS at IOTA parameters

## Slide 10: Checking Intensity Dependence
Normalized centroid data with decoherence envelope
No strong indication of intensity dependence
BPM resolution insufficient?
Time to equilibrium too long compared to measurement interval?

## Slide 11: Using the Nonlinear Element
Comparison of centroid damping with nonlinear element on/off
Taken at similar kick amplitudes

## Slide 12: Measured Tune Shifts
- X. Huang, S. Y. Lee, E. Prebys, and R. Tomlin, Phys. Rev. ST Accel. Beams 8, 064001 (2005).
- Belouchrani, A., et al. IEEE Signal Processing Society, vol. 45, no. 2, Feb. 1997, pp. 434–44, doi:10.1109/78.554307.
- ICA used to find tunes for decoherence signal
- Cos/sin signals plotted
Measured tune shifts for two different t-vales of nonlinear element

## Slide 13: Simulations – Centroid Motion
- Comparison of measurement to Synergia simulations
- Kick strength in simulation scanned to find reasonable agreement
Simulation t = 0.431
Measurement t = 0.433

## Slide 14: Conclusions
Decoherence measurements provide strong evidence for increased energy spread
  Driven by IBS
  Comparison to calculations show the decoherence is strongly driven by chromaticity/energy-spread coupling
  Measurement of energy spread from this data is dependent on accurate knowledge of chromaticity
Initial measurements taken with the nonlinear element
  Show the nonlinear element is working well
  Comparison to Synergia simulations is excellent, both for centroid and tune comparisons

## Slide 15: End