## Slide 1: protoDUNE photon Detector MC
Leon Mualem
Caltech

## Slide 2: Some MC notes
Based on wiki for photon detector MC tutorial
  https://cdcvs.fnal.gov/redmine/projects/dunetpc/wiki/Photon_Simulation_Tutorial
Using dunetpc v08_14_00 (fixed a +-X swap mapping to OpChannels)
Instead of using “DUNE” version as in the tutorial, use protoDUNE version of fcl(s) found in the protoDUNE subdirectory
In /srcs/dunetpc/dune/PhotonPropagation/Tutorial/protoDUNE/
My example in:
  /dune/app/users/mualem/pdune_201903/srcs/dunetpc/dune/PhotonPropagation/Tutorial

## Slide 3: Some MC notes
root –l protodune_optical_tutorial_reco_hist.root
TBrowser mine;
Navigate to OpChannel

## Slide 4: Along Faces of APA 5,6,4 in sequence
100 10 GeV/c Mu+
Along Z axis
  ThetaXZ=0
  ThetaYZ=0
Near APA non-beam drift (X=300)
Centered Top to Bottom (Y=300)
Start at beam face (Z=0)
All (almost) Hits on non-Beam, some leakage out the side reduces APA 1

## Slide 5: Along Faces of APA 3,2,1 in sequence
100 10 GeV/c Mu+
Along Z axis
  ThetaXZ=0
  ThetaYZ=0
Near APA beam-side drift (X=-300)
Centered Top to Bottom (Y=300)
Start at beam face (Z=0)
All (almost) Hits on Beam-side
Equal APA distribution
Small leakage across CPA

## Slide 6: Mid-Drift in front of APA 3,2,1
100 – 10 GeV/c Mu+
Along Z axis
  ThetaXZ=0
  ThetaYZ=0
Centered in beam-side drift (X=-180)
Centered Top to Bottom (Y=300)
Start at beam face (Z=0)
Almost all hits on beam side, small leakage to non-beam, probably 1 of 100 muons had photon cross the CPA

## Slide 7: Down Face of APA3
100 10 GeV/c Mu+
Along Y axis
  ThetaXZ=0
  ThetaYZ=-90
Near APA beam-side drift (X=-350)
Start At Top (Y=600)
Mid-APA3 (Z=110)
Largest hits on APA3
  less on APA2
    Least on APA1

## Slide 8: Down Face of APA2
100 10 GeV/c Mu+
Along Y axis
  ThetaXZ=0
  ThetaYZ=-90
Near APA beam-side drift (X=-350)
Start At Top (Y=600)
Mid-APA3 (Z=330)
Largest hits on APA2
  less on APA3 = ~APA1

## Slide 9: Along Face of APA1
100 10 GeV/c Mu+
Along Y axis
  ThetaXZ=0
  ThetaYZ=-90
Near APA beam-side drift (X=-350)
Start At Top (Y=600)
Mid-APA3 (Z=550)
Largest hits on APA1
  Less on APA2
    Least on APA3

## Slide 10: Along Face of APA5
100 10 GeV/c Mu+
Along Y axis
  ThetaXZ=0
  ThetaYZ=-90
Near APA beam-side drift (X=350)
Start At Top (Y=600)
Mid-APA5 (Z=110)
Largest hits on APA5
  Less on APA6
    Least on APA4

## Slide 11: Along Face of APA6
100 10 GeV/c Mu+
Along Y axis
  ThetaXZ=0
  ThetaYZ=-90
Near APA beam-side drift (X=350)
Start At Top (Y=600)
Mid-APA5 (Z=330)
Largest hits on APA1
  Less on APA2
    Least on APA3

## Slide 12: Along Face of APA4
100 10 GeV/c Mu+
Along Y axis
  ThetaXZ=0
  ThetaYZ=-90
Near APA beam-side drift (X=350)
Start At Top (Y=600)
Mid-APA5 (Z=550)
Largest hits on APA4
  Less on APA5
    Least on APA6 (furthest away)

## Slide 13: Conclusions
Re-Checked the correspondence of channel map in MC to Data.
Versions now agree, in prior versions channels were swapped in X
  (any earlier MC needs re-digitizing)
Geometry of the MC looks consistent with reality
  +Y axis = up and origin ~ bottom of CPA/APA
  +X axis = toward beam left, Jura, origin at ~CPA plane
  +Z axis = along the CPA plane, origin ~upstream end of APAs
    Caveat: did not test to cm or mm precision

## Slide 14: BACKUP Details on how to run (possibly out of date)

## Slide 15: Some MC notes
Based on wiki for photon detector MC tutorial
  https://cdcvs.fnal.gov/redmine/projects/dunetpc/wiki/Photon_Simulation_Tutorial
Instead of using “DUNE” version as in the tutorial, use protoDUNE version of fcl
In /srcs/dunetpc/dune/PhotonPropagation/Tutorial
My example in:
  /dune/app/users/mualem/pdune_201809/srcs/dunetpc/dune/PhotonPropagation/Tutorial

## Slide 16: Some MC notes
testgen.sh in that directory runs each step sequentially
Successfully ran up to about 5000 events. (files get too big if I recall)
Sim – Particle production, interaction, energy deposits, …. (GEANT bascially)
Digi – Take particle tracks, energy deposits and make into waveforms
Reco – Take waveforms and make hits, flashes, energy deposits in OpChannels
Each stage above produces file “gen” (big, all info) and “hist” (small, summary info)

## Slide 17: Some MC notes
root –l protodune_optical_tutorial_reco_hist.root
TBrowser mine;
Navigate to OpChannel

## Slide 18: Some MC notes
root –l protodune_optical_tutorial_reco_hist.root
TBrowser mine;
Navigate to OpChannel

## Slide 19: Some MC notes
Particle hints:
  /dune/app/users/mualem/pdune_201809/srcs/dunetpc/dune/PhotonPropagation/Tutorial
  …protoDUNE/protodune_optical_tutorial_sim.fcl
  Particle type:
  Particle Momentum:
# In this example, which primary particle(s) we'll focus on in an event.
# PDG code 13 = mu-.pi+ = 211 proton = 2212 mu+ = -13
PDGcode: 211
physics.producers.generator.P0: [3.0]

## Slide 20: Some MC notes
Geometry hints:
  /dune/app/users/mualem/pdune_201809/srcs/dunetpc/dune/PhotonPropagation/Tutorial
  …protoDUNE/protodune_optical_tutorial_sim.fcl
  We believe origin at upstream (wrt beam) bottom edge of cathode plane (maybe lowest wires?)
# positive x axis
# physics.producers.generator.Theta0XZ: [ 90 ] # degrees angle in xz plane from z axis ?
# physics.producers.generator.Theta0YZ: [ 0 ] # degrees angle in yz plane from z axis ?
# positive z axis
# physics.producers.generator.Theta0XZ: [ 0 ] # degrees angle in xz plane from z axis ?
# physics.producers.generator.Theta0YZ: [ 0 ] # degrees angle in yz plane from z axis ?
# negative z axis
# physics.producers.generator.Theta0XZ: [ 0 ] # degrees angle in xz plane from z axis ?
# physics.producers.generator.Theta0YZ: [ 180.0 ] # degrees angle in yz plane from z axis ?
# vertically down
# physics.producers.generator.Theta0XZ: [ 0 ] # degrees angle in xz plane from z axis ?
# physics.producers.generator.Theta0YZ: [ -90.0 ] # degrees angle in yz plane from z axis ?

## Slide 21: Beam Plug position?
Possibly the beam plug location – Paola probably knows best
# This block defines starting parameters for beam window 3 ( with beam plug) in protodune_v4.gdml geometry
physics.producers.generator.PosDist: 0 # Position distribution (0=uniform, 1=gaussian)
physics.producers.generator.X0: [7.966] # Starting position (cm)
physics.producers.generator.Y0: [460.84]
physics.producers.generator.Z0: [-191.60]
physics.producers.generator.SigmaX: [0.0]
physics.producers.generator.SigmaY: [0.0]
physics.producers.generator.SigmaZ: [0.0]
physics.producers.generator.AngleDist: 0 # Angle distribution (0=uniform, 1=gaussian)
#physics.producers.generator.Theta0XZ: [-11.844] # Starting angles (degrees)
# Flip the angle for the photon detectors. UGH!
physics.producers.generator.Theta0XZ: [11.844] # Starting angles (degrees)
physics.producers.generator.Theta0YZ: [-11.107]
physics.producers.generator.SigmaThetaXZ: [0.]
physics.producers.generator.SigmaThetaYZ: [0.]