## Slide 1: High-efficient low voltage supply signal processing based on quantized amplification
Antonio Liscidini
antonio.liscidini@utoronto.ca

## Slide 2: Outline
Power efficiency of analog and digital signal processing (thermodynamic limit)
Quantized-Analog (QA) Amplification (liquid bits)
Characteristics of the QA (noise, distortion, design)
Example of QA RX front-end (low supply and key features of QA systems)

## Slide 3: CMOS amplifier power efficiency
[Vittoz ISSCC ‘94]
The analysis assumes a linear amplifier. In presence of distortions, SNDR achievable for a given power is even lower

## Slide 4: A Figure of Merit for all the seasons
The relationship between bandwidth, SNR and Power is very straightforward and superiorly limited* to 1/(0.033 aJ) (or 195dBJ-1).
This figure of merit is a thermodynamic FoM and it is a the base of several figure of merit present in literature (Filters, ADC, Amplifiers).
* This FoM upper bound is valid only if in a cyclo-stationary process all power is dissipated in a period.

## Slide 5: Digital gate power efficiency
[Vittoz ISSCC ‘94]
The digital power grows less with the SNR by making digital signal processing more attractive for large SNR

## Slide 6: Power efficiency – Analog vs. Digital
Digital (1984)
Digital (2018)
Analog Limit
[ E. Vittoz, ISSCC ’94]
The power consumed by a digital filter depends on the # of operations required per cycle and on the energy required for each operation
In digital Energy for each operation is reduced by scaling.
For small dynamic range analog is better than digital

## Slide 7: Dynamic range vs. power
Power
Signal-to-noise ratio
Bandwidth
Current efficiency
(signal amplitude / dc current)
Voltage efficiency
(signal amplitude / voltage supply)
[A-.J. Annema et al. JSSC 2005]
This equation has been found by several authors for several analog building blocks and it appears to be more general than its derivation could suggest
For analog signal processing, voltage and current efficiency are “typically” smaller than one

## Slide 8: Upper and lower bounds in the DR
In voltage analog signal processing the maximum signal amplitude is limited to the supply (i.e. ηV=1)
Dynamic range is increased lowering the noise, which is done bu reducing the impedance level (i.e. kT/C)
Analog
In digital the minimum signal amplitude is one bit (i.e. VDD)
The maximum signal amplitude rises exponentially with the number of lines (binary weighted)
The binary weight increases voltage and power efficiency
Digital

## Slide 9: Voltage supply and efficiency
Voltage supply is a key element in the power/area optimization:
  It defines the power dissipation in digital
  It defines the maximum signal that the analog section can handle
  For a given input signal the voltage supply defines the voltage efficiency and with it the minimum theoretical power dissipation
  It define the impedance levels and thus the area
GOAL: increase voltage efficiency of analog signal processing above one

## Slide 10: Dynamic Range limitation in an amplifier
If no inductors are used, in a amplifier the maximum swing at the output is limited by the adopted supply
The gain of the amplifier sets the maximum signal that can be handled at the input, and thus the dynamic range

## Slide 11: Quantized Analog Amplification Principle
Each unit is dedicated to amplify only a portion of the signal
The original amplifier is sliced in N identical units each consuming 1/N of the original current
Voltage efficiency increases by N and with is also the power efficiency
Recombination can be after filtering large signals or in digital domain
[J. Musayev et al., Electronic Letters 2018]

## Slide 12: Analog quantized amplification
Since the recombiantion is a linear process, QA signal processing is compatible with ay linear operation such as filtering up/downconversion

## Slide 13: Liquid digital decomposition
For any input, all together the lines form a sort of thermometric code similar to the one produced by a flash ADC
Liquid bits (unsaturated lines)

## Slide 14: Quantized analog amplification and noise
Ideally only unsaturated slices produce analog noise at the output
Assuming to slice the original amplifier by N with 1/N of the current the input referred power noise increase by N
The voltage input range increases by N so the maximum input signal power increases by N2
The DR improves by N for a given power consumption compared to a pure analog processing

## Slide 15: Simulation of QA inverter amplifier
For the same total size, N is swept from 1 to 8, by adding offsets equal to VDD/A.
Voltage efficiency (i.e. input range) and hence DR (i.e. maximum SNR) improve N-times.
For N = 8, DR expands by 9dB as expected.
9dB

## Slide 16: Simulation of QA inverter amplifier (2)
Average supply current reduces by 4.5-times (ηc improves by 6.5dB).
Overall FoM improvement becomes 15.5dB (due to ηv and ηc).
These results are obtained assuming no distortion (i.e. SNRmax = DR).
15.5dB

## Slide 17: Analog quantized amplification efficiency
Digital (1984)
Digital (2018)
Analog Limit
Quantized Analog Limit (e.g. 10 lines)
The Dynamic Range increases by N for the same power dissipation. This because the voltage efficiency increased by N
Since the liquid thermometric code generated by the QA amplifier is not binary weighted the improvement is not exponential as in digital

## Slide 18: Quantized Analog Amplification and Linearity
In a real amplifier the gain of an amplifier is not constant in the input range
A large voltage offset between the elements produces a gain variation that generates distortion
A smaller offset and a larger number of elements linearize the gain and extend the range
Linearity and input range can be controlled by acting on the number of elements and their offset

## Slide 19: Overlap and gain linearization
If f(x) saturate at the extremes, no matter the gain shape, the higher order derivatives tend to zero if N is increased and ∆V decreased.
Small signal gain
Higher order derivatives

## Slide 20: QA inverter amplifier linearity
Ripple down to 0.0001% is obtained by 128 elements (at this point mismatches dominate).
Better linearity for both small (by 8dB) and large (by 64dB) signals is obtained.
High IIP2 with single-ended structure is possible (symmetry around mid-point).
0.9% ripple
0.0001% ripple

## Slide 21: Quantized Analog Amplification Design
The design of a quantized structure starts from a unit element
The multiplicity (i.e. number in parallel) defines the noise of the quantized structure
The voltage offset and the number of elements in series define linearity and input range
The overall performance in terms of noise and linearity and power are defined ONLY by the number of elements and their configuration

## Slide 22: Most important feature QA signal processing
Improving current and voltage efficiency allows to lower the power dissipation for a given SNR and bandwidth
Voltage supply is not an upper bound for the voltage signal swing anymore.
Since the recombination is a linear operation, the QA signal processing can be applied to any linear circuit (e.g. filters ,up/down converters etc.)
Saturated lines do not add analog noise or distortion
Both small and large distortions are improved
QA amplification design allows a more flexible optimization of the design to reach the target specs.

## Slide 23: Quantized Radio
Prototype in CMOS 65nm
23
First quantized radio 0.9-2GHz (100 elements)
[Musayev et. ESSCIRC’18]

## Slide 24: Power and DR
19dB
13dB
Compression point increases by 19dB
Noise Figure increases by 13dB
DR increases by 6dB, at almost no expense on power.

## Slide 25: Distortion

## Slide 26: Measurement Results
 | This work | Murphy, JSSS’15 [8] | Fabiano, JSSC’13 [7] | Liempd, JSSC’ 14 [9]
Topology | QA Front-End | Noise cancelling | Transformer-LNA | Voltage-modea, HR
Gain [dB] | 20.8b-36.8 | NA | 44.5a-45.5 | 70
Frequency [GHz] | 0.7-1.4 | 0.6-3 | 1.8-2.4a | 0.4-3
NF [dB] | 1.9-2.8 | 1.8-3b | 3.8, 1.9a | 1.8-3.1
NFblk [dB] | 6.6-7.9 | 7-9 | 7.9 | 14 (10d)
IIP3 [dBm] | 1-20.5b | 10-11.5a | 18, 16a | 3, 8d
IIP2 [dBm] | 45-75b | 49.5-55a | 64, 66a | 55, 80e
B1dB [dBm] | -8.5 to 10.5b | -6 to -1 | -1.5 | -13
HR (3rd /5th) [dB] | 40-67 / 47-70 | 52/54 | 54/65 | 40 (70)
Supply [V] | 0.8, 1, 1.2 | 1 | 1.2, 1.8 | 40 (75)
Power LO path [mW] | 37.2/GHz* | 13/GHz | 3.2/GHz | 6.8/GHz +5.4
Power LNA+BB [mW] | 13.7b-14 | 30-46 | 23.4 | 14.3
Area [mm2] | 0.25 | 5 | 0.84 (0.74a) | 0.6
Technology | 65nm | 28nm | 40nm | 28nm
* Not optimized in this work. a Differential, b HL mode (Vlad = 1), c LN mode (Vlad = 0), d LNA optimized, e Calibrated |  |  |  | 
QA receiver achieves the highest compression and low NF at the lowest power in signal path (LNA+BB).

## Slide 27: Conclusion
Analog signal processing has a lower bound in the power consumption set by the thermal noise.
Power efficiency can be improved by increasing voltage and current efficiency
A new mixed-signal processing has been presented. This merge together digital and analog without a fixed interface
The proposed quantized-analog (QA) signal processing looks promising to develop a new generation of low power circuits.
A prototype of a QA RX validated the theory