## Slide 1: Bi-Weekly DUNE Near Detector Engineering Integration Meeting
10/03/2019

## Slide 2: Agenda
M. Leitner: DUNE ND Engineering Requirements Update And Next Steps
All: Discussion
Upcoming Meetings:
  DESY Near Detector Meeting October
  DOE IPR End October
  Installation Review January
  Collaboration Meeting CERN January
  DOE Baseline Review April/May

## Slide 3: LAr Detector Main Structure Parameters
Width = 11.34 m
Depth = 8.34 m
Height = 7.04 m

## Slide 4: LAr Detector Simplified Flow Diagram:
Graphic: Min Jeong Kim
Below Ground
Cryogenics Moves
With Detector
Above Ground
3” pipe
6” jacket
24” pipe
6” pipe
12” jacket
3” pipe
6” jacket
2” pipe
Large Diameter Cryogenic Piping Needs To Move With Detector

## Slide 5: Cryogenic Line Guides Require Novel Design Solution
Metal Guide Option
Plastic Guide Option
Vacuum Jacketed Lines
Commercially Available
Guide Designs Needs To Resist “Coil-Up” Under Vacuum Load

## Slide 6: KLOE-3DST Detector Main Structure Parameters
See Sergio Bertolucci Talk
Yoke:
Length = 6 m
Diameter = 7 m
Full Detector Size:
Length ≈ 10 m
Height ≈ 11 m

## Slide 7: KLOE Magnet Incl. Cryostat Will Be The Heaviest Single Component To Be Lifted Into The DUNE ND Cavern
KLOE magnet: 42 tonne
Yoke: 510 tonne (separable into individual units weighing less than 30 tonne)
See Sergio Bertolucci Talk

## Slide 8: KLOE-3DST Detector Will Be Stationary And Can Be Assembled And Serviced Inside Cavern Below Ground
Coil Cryostat
Yoke
“Low Density Detector”
TPC or Straw Tubes
Calorimeter
11 Million 3DST Cubes
KLOE-3DST
Stationary Detector
Inside Alcove
Floor Guides
To Assembly
And Servicing
Station

## Slide 9: MPD Main Structure Parameters
Detector Size:
Length = 12.8 m
Height = ~10 m
Width = 8.5 m
See MPD Session

## Slide 10: MPD Design Maturation: Achieved Fully Integrated Design
Detector Size:
Length = 12.8 m
Height = ~10 m
Width = 8.5 m
See MPD Session
Calorimeter
Coil and Cryostat Structure
Pressure Vessel
TPC

## Slide 11: Open MPD Superconducting Coils Expose Adjacent Structures To Significant Magnetic Stray Field
Simulations by Vladimir Kashikhin
20 tonne-force between MPD and KLOE Plus Added Interaction Between Both Detector Coils
1000 G Contour
200 G Contour
MPD field will require LAr cryostat room-temperature structure to be fabricated out of stainless steel or aluminum
More effort will be required to ensure magnetic interactions are fully understood

## Slide 12: DUNE ND Prism Design Concept Utilizes Commercially Proven Roller Drives Which Distribute Detector Weights
Positive side capture required due to large magnetic forces
30.5 m movement range
9 stops, 2 weeks at each stop

## Slide 13: PRISM System Will Distribute Significant Detector Weights
Control system can synchronize several rows of rollers to distribute weight
Guide rail design optimized together with cavern structural design
System Permits Smooth Movement
Magnet Forces Could Complicate Design
  Prevent tipping
  Prevent unanticipated movement

## Slide 14: ND Requirements Document Collects Information About Facilities Interfaces
EDMS# 2230933
EDMS# 2222899

## Slide 15: Next Steps
Climate Control Discussion
Electrical Engineering
  1-2 MW Maximum Power
  Power Spreadsheet
  Grounding Details
  Power Distribution and 1-Liner Drawing
  Controls Layout
  Cable Trays (Designer)
Surface Building Requirements
  Incorporating Info From Terry and Don
  Cable Trays and General Utilities For Experiments
Integration and Installation (I&I) Will Detail-Design PRISM System
  Movement System
  Cable Chain
  Prototypes