## Slide 1: Magnet Fabrication Travelers, Non-Conformities and Resolution
Katherine Ray – LBNL (QA)
Mike Solis – LBNL (Procurement Technical Contact)
May 22, 2019 – MQXFA03 Structure and Loading Review

## Slide 2: Overview
State of the Magnet Fabrication Travelers
Non-Conformances on MQXFA03
Change Tracking Process
Shell Receiving process

## Slide 3: Magnet Fabrication Travelers Overview
# | Title | Revision | ID
1 | Yoke Pre-Stack WI | B | SU-1008-8072
2 | Yoke Half Stack WI | B | SU-1009-7829
3 | Shell Instrumentation WI | B | SU-1009-3745
4 | Shell-Yoke Assy WI | A | SU-1008-2169
5 | Loadpad Pre-Stack WI | B | SU-1008-8075
6 | Dressed Coil WI | B | SU-1008-8073
7 | Pad-Collar Assy WI | Not released | SU-1010-1610
8 | Coil Pack Subassy WI | A | SU-1008-8074
9 | Magnet Electrical QA at LBNL | B | SU-1010-1903
10 | Magnetic Measurements | Not released | SU-1010-2018
11 | Magnet Fiducial Structure WI | A | SU-1008-8070
12 | Axial Rods Instrumented WI | B | SU-1008-8069
13 | Axial End Load Structure WI | B | SU-1008-8068
14 | Splice Box WI | A | SU-1008-8067

## Slide 4: Magnet Fabrication Travelers Overview
# | Title | Revision | ID
1 | Yoke Pre-Stack WI | B | SU-1008-8072
2 | Yoke Half Stack WI | B | SU-1009-7829
3 | Shell Instrumentation WI | B | SU-1009-3745
4 | Shell-Yoke Assy WI | A | SU-1008-2169
5 | Loadpad Pre-Stack WI | B | SU-1008-8075
6 | Dressed Coil WI | B | SU-1008-8073
7 | Pad-Collar Assy WI | Not released | SU-1010-1610
8 | Coil Pack Subassy WI | A | SU-1008-8074
9 | Magnet Electrical QA at LBNL | B | SU-1010-1903
10 | Magnetic Measurements | Not released | SU-1010-2018
11 | Magnet Fiducial Structure WI | A | SU-1008-8070
12 | Axial Rods Instrumented WI | B | SU-1008-8069
13 | Axial End Load Structure WI | B | SU-1008-8068
14 | Splice Box WI | A | SU-1008-8067
The majority of the 14 travelers that describe the magnet fabrication process have been released.
However, revisions based on Lessons Learned have been and will continue to be made.

## Slide 5: Magnet Fabrication Traveler Changes Made to Address Pinched Wire in MQXFAP1b
Added verification point

## Slide 6: Change Records
We are tracking Non-Conformances, Deviations and Engineering Changes in one spreadsheet
These are currently communicated to Fermilab on a monthly basis

## Slide 7: MQXFA03 Change Records
Thus far we have only minor non-conformances, which we are tracking
  Pion mounting, non-certified washers, minor out of tolerances on parts

## Slide 8: Example Change Records Process: Coil Alignment Keys
MQXFA03 alignment keys were made full-length as well
Project subsequently decided not to have full-length alignment keys. Request to deviate from the released drawings for MQXFA03 documented.
Engineering Change Note used to request drawing changes and work instruction changes for future magnets
MQXFAP2 coil alignment keys were full length

## Slide 9: Overview
State of the Magnet Fabrication Travelers
Non-Conformances on MQXFA03
Change Tracking Process
Shell Receiving process

## Slide 10: MQXFA03 Shells Built to Drawing Revision C
Shell Material updated to Aluminum 7075-T6, from T652
Added larger radii to cutouts

## Slide 11: Shell Material Certifications and Inspections
Fluourescent (Dye) Penetrant Inspection (FPI) now required
Ultrasonic inspection
Aluminum 7075-T6

## Slide 12: Shell Dimensional Inspections at the Vendors
Vendors measure inner and outer diameter in 5 locations
Tolerances are for restrained condition. Above measurements made in unconstrained condition.
Measurements averaged when evaluating.
Other vendor’s report in restrained position looks good

## Slide 13: Shell Dimensional Inspections at LBNL
Shells started arriving at LBNL this week
They will be sent to our CMM facility to verify the vendors’ data

## Slide 14: Summary
The procedures and drawings are mostly released
We are tracking changes from lessons learned
  Drawing & procedure updates
  Documented with various change records
Reporting monthly to L2
Shell QC recommendations have been implemented
Certs and inspection data are retained for records
No critical deviations noted to date