## Slide 1: Loading Sequence for MQXFA03 (Proposed)
Soren Prestemon – LBNL (L3/CAM)
Dan Cheng– LBNL (Deputy L3/CAM)
Heng Pan
May 22, 2019

## Slide 2: Loading considerations
Azimuthal (radial) preload is applied via a bladder-and-key approach
  Target strain values for Aluminum shells and coil poles are determined in advance
  Strain gauges on shells and coil poles are monitored during loading
  Keys are shimmed to lock in the load
Axial preload is achieved via a hydraulic loading rig
  Target strain values for the rods are determined in advance
  Strain gauges on rods are monitored during loading
  Once target strain achieved, nuts lock the preload in place

## Slide 3: Order of operations
The order of these operations has evolved through LARP and into HL-LHC AUP
  In the TQ era, partial radial preload was followed by partial axial, then full radial and then full axial
  In the HQ era and into HL-LHC AUP (through MQXFAP2), the full radial preload was performed, then the axial rods installed and full axial preload applied
  Note that CERN has used the following process (similar to TQ):
    Snug the rods; 50% radial loading, 50% axial loading, then 100% radial, 100% axial
In the absence of friction, the order will not affect the end state
With friction, there is the potential for difference in end state stress distribution
  Influences primarily the coil ends

## Slide 4: Proposed order of operation for MQXFA03
MQXFAP1b test results hint at issue with coil end preload
We intend to perform the following loading sequence with MQXFA03:
  Install and snug the axial rods
  Perform azimuthal (radial) preload to 50% of target value
  Perform axial load to 50% of target value
  Perform azimuthal (radial) preload to 100% of target value
  Perform axial load to 100% of target value
The magnet assembly plan will be modified accordingly
  Implies updates to travelers and drawings
  Will be captured in the updated FDR