## Slide 1: CAD MARS: DAGMC-MARS Meeting Summary
Nikolai Mokhov (Fermilab)
TSD Topical Meeting, Fermilab
May 16, 2019

## Slide 2: CAD MARS Possibilities
Despite of worldwide efforts - with hundreds and hundreds of person-years invested over last 30 years - reliable user-friendly error-free implementation of CAD models into Monte-Carlo particle interaction and transport codes is still a dream.
There are several bi-directional packages which pretend to do this job:
MCAM* (China, commercial) http://www.fds.org.cn/en/software/mcam_1.asp
McCad* (Germany) https://inis.iaea.org/search/search.aspx?orig_q=RN:39015646
FASTRAD* (France, commercial, not for China, Russia and USA) https://www.fastrad.net/
DAGMC** (UW-Madison) https://svalinn.github.io/DAGMC/ - this meeting
*) Translation, **) Direct modelling on CAD models
We at Fermilab use manual conversion from the CAD STEP files to MARS input
CAD STEP AP209 standard http://www.ap209.org promises CAD+FEA+CFD and – most important - assigned material properties and materials database

## Slide 3: DAGMC and its Possible Integration into MARS15
Working Meeting with Paul Wilson, Prof. of Nuclear Engineering of University of Wisconsin-Madison and Dr. Patrick Shriwise (ANL) https://svalinn.github.io/DAGMC/
Fermilab, BTW, Penthouse, Thursday, May 9, 9:30 AM – 4:00 PM
Direct Accelerated Geometry Monte Carlo (DAGMC) is a software package that allows users to perform Monte Carlo radiation transport directly on CAD models – P. Wilson
MARS15 is a default Monte-Carlo code system at Fermilab for accurate simulation of particle transport and interactions in accelerator, beamline and detector components, radiation shielding and environment. Geometry models are built either from predefined shapes described in user-friendly input files, or via using the power of the ROOT system for complex real-life applications. CAD models - saved in the STEP format - are currently implemented manually into MARS – N. Mokhov, D. Reitzner, I. Tropin
A possible integration of DAGMC into MARS15 would allow users to perform MARS15 simulations directly on CAD models and, as a result, reduce human effort and minimize human errors - All

## Slide 4: M

## Slide 5: M

## Slide 6: M

## Slide 7: M

## Slide 8: M

## Slide 9: M

## Slide 10: M

## Slide 11: M

## Slide 12: M

## Slide 13: M

## Slide 14: M

## Slide 15: M

## Slide 16: M

## Slide 17: Steps Towards Implementation
1. FNAL
a. Define a pathological problem to test geometry tessellation at necessary
tolerances & provide those to UW
b. Acquire Cubit or Trelis
c. Install dependencies
i. HDF5
ii. MOAB
iii. (PyNE)
iv. DAGMC (a la OpenMC)
v. Svalinn plugin
d. Join dagmc-users mailing list
e. Join community call - every 2nd Thursday (next, 5/16), 9AM CT,
cnerg.engr.wisc.edu/meet.html
f. Review FLUKA and/or Geant implementations of DAGMC for guidance
g. Develop list of additional metadata of interest
2. UW
a. Acquire Cubit for testing of plugin

## Slide 18: DAGMC Implementation to MARS15 ?
Issues
Auxiliary software (some are commercial)
Spatial resolution: 10-4 cm in DAQMC, 10-10 cm in MARS
CPU performance
Always tessellated volumes and surfaces (facets)
Magnetic/electric fields: No in DAQMC, Yes in MARS
Quasi continuous processes like multiple Coulomb scattering:
No in DAQMC, Yes in MARS
7. Lost ROOT system features: geometry, histograming and
other ROOT capabilities
Investigate the alternative
Use just translation capability of DAGMC and its finding algorithms to answer two fundamental questions: “Where am I?” and “How far?”, not a particle transport algorithm