## Slide 1: DUNE Far Detector Calibration with Cosmic Rays
Tom Junk
DUNE Far Detector Calibration Workshop
June 18, 2019
Many thanks for materials stolen without permission: David Adams, Jonathan Asaadi, Bruce Baller, Sowjanya Gollapinni, Kevin Ingles, Vitaly Kudryavtsev, Kendall Mahn, Mike Mooney, Ajib Paudel, Jen Raaf, Aidan Reynolds, Hannah Rogers,
Michelle Stancari, Matt Thiesse, Filippo Varanini, Erik Voirin, Mike Wallbank, Karl Warburton, Leigh Whitehead, Tingjun Yang

## Slide 2: Early Years of DUNE
Most data from most interactions will be from cosmic rays.
~1.3 million useful interactions per year per module
Schedules shown so far have at least one FD module up and running at least one year before there is beam
Commissioning, calibrating, atmospherics, exotics, possibly a SNB during that early period

## Slide 3: Uses of Cosmic Rays
Check the channel map
Identify disconnected channels. The pulser only tests up to preamp input. Need to see physics signals. 39Ar serves this role too.
Calibrate pulse shapes – field response of the detector
Measure electron lifetime (maybe 39Ar can do this too)
Measure dQ/dx uniformity across APA faces (channel calib). (39Ar too)
Calibrate dQ/dx --> dE/dx using known MIPs (39Ar too)
Measure drift velocity using Cathode-Anode Piercing Tracks
Align the APAs and CPAs
Calibrate charge and drift response in inter-APA gaps

## Slide 4: Uses of Cosmic Rays
Characterize electric field nonuniformity
  space charge (not expected for FD-SP but FD-DP will need to check)
  field cage nonuniformities
Test relative timing of TPC and photon detectors
Explore saturation characteristics of front-end and ADC
Measure long-range induction effects in the APAs (and FEMB effects)
Michel electrons test the low-energy EM response

## Slide 5: Muon Flux at the 4850' Level
See DocDB 5505 for an approximate calculation based on Vitaly Kudryavtsev, Martin Richardson, J. Klinger, and Karl Warburton LBNE DocDB 9673-v1, and the calibration concept study document, DUNE DocDB 4769-v2
Estimate 4 cosmic rays
per day per square
meter at the 4850'
level (DocDB 4769)
Syst. Uncertainty
is ±20% in total rate.
Shapes are uncertain
too!

## Slide 6: Fraction of Showering Muons
No-shower cut: Critical Energy (energy at which radiative effects are more important than ionization) is 485 GeV in LAr. log10(485) = 2.7
Vitaly's plot was
in muons per GeV (linear)
on a log scale (!)
Estimate that 60% of muons
don't shower significantly.
MUSUN Generator-Level Run: prodMUSUN_DUNE10kt.fcl with 100000 events

## Slide 7: Rates For One DUNE Far Detector Module (SP)
Some studies like checking for dead channels can use looser selections.
Collection-plane channels get hit 10x per day. Induction-plane channels are hit more.

## Slide 8: Validating/Fixing the Channel Map
Some flaws in the channel map are obvious once you have straight tracks.
Example from 35-ton running: even and odd collection-plane channels were swapped (ribbon cable?)
Not the only possible flaw. If we get all the channels backwards, straight tracks may still look straight.
Swap U and V views – can test with timing.
Channel Number
Tick
ProtoDUNE-SP channel map was correct on Day 1 of operations due to good communication
and hard work.
DUNE FD-SP map is likely just a scale-up. Cable swaps like this may be unlikely (all boards)
Two days of cosmic ray data should suffice for this and also spot dead channels that stay dead. Intermittent channels are more difficult.

## Slide 9: Staging Cosmic-Ray Measurements
Cosmic ray rates are low at the 4850' level. 10x per collection-plane wire per day.
For rapid measurements and stability checks, we will have to loosen up cuts. E.g. use photon detector timing to locate an event in x and not rely on anode-cathode piercing tracks
Some measurements can be done inclusively by assuming uniformity of the detector.
  e.g. assume lifetime is the same everywhere – get a number within an hour.
  Relax the assumption to get a more differential measurement takes more data.
Looking at average hit response on a channel takes a few days' data. Looking along length for shadows of other wires takes thousands of times more data.

## Slide 10: Lifetime Measurement
Tracks that leave hits at different distances from the APA provide a calibration sample for the lifetime.
ICARUS: https://arxiv.org/abs/1409.5592 (JINST 9 (2014) no.12, P12006)
MicroBooNE: https://arxiv.org/abs/1710.00396 (Varuna Meddage conf. proceedings, DPF 2017)
  DUNE lifetime analysis module implemented for ProtoDUNE-SP for running in the nearline monitor
  Uses APA-CPA piercers
LArIAT: Single-track and multi-track methods – see Jen's talk at the January 2018 collab meeting.
35-ton prototype: Matt Thiesse's Ph.D. Thesis: very difficult due to low signal/noise). Multi-track method.

## Slide 11: ICARUS Lifetime Measurement
Truncated means get more
information out of
Landau (convoluted with Gaussian)
hit charges

## Slide 12: Precision of Lifetime Measurement
𝜆=1/𝜏 is a more
natural variable as
the uncertainties
don't depend on 𝜏
For a 3 ms lifetime, one gets about a ±30%
measurement of the lifetime for each track
Five muons per day per APA, 1/day if you want
the muon to go in the opposite CPA panels.

## Slide 13: Impurity Contour and Velocity @ Z=0
124 discharge ports
Erik Voirin
Max. variation
~2%
FD-SP
Near Mid-Plane

## Slide 14: Velocity Streamlines
124 discharge ports
(high res image – zoom for detail)
Erik Voirin,
DUNE DocDB 1046-v2

## Slide 15: Pulse Shape Measurement
Undershoot correction for AC-coupled electronics
  can do with a pulser but better with cosmic-ray data
  needs very little data to check – just need a few big signals
  Electronics model is reliable, just need to check each channel
  Imperfect pole-zero cancellation seen in MicroBooNE's preamp causing under- and overshoot.
MIP response needs tracks perpendicular to wires. Easy for induction-plane wires, harder for collection-plane wires.

## Slide 16: MicroBooNE Example – Calibrating Pulse Shapes
C. Adams et al., JINST 13 (2018) no.07, P07007
MicroBooNE has no grid plane, so U is
special.

## Slide 17: An Event in ProtoDUNE-SP
APA 3
APA 2
Time (tick)
Collection Plane Wire Index
DUNE DocDB 10842
T. Yang

## Slide 18: ProtoDUNE-SP Electron Diverter Field Predictions
Biased as designed
Grounded outer electrode

## Slide 19: Passive Diverters or No Diverters
Options under consideration

## Slide 20: Calibrating Response in Gaps
Isochronous tracks – measure time delays
Tilted tracks – measure spatial distortions
Electron Diverters
grounded in this
event.

## Slide 21: dQ/dx uniformity near gaps
Diverter at nominal voltage.
note: APA 3's grid plane is charging up
Grounded Diverter
Note: One ASIC is a little different
from the others.

## Slide 22: Ajib's Median dQ/dx Z plane (y,z)
APA 1
APA 2
APA 3
Beam Right
Calculated using Anode-Cathode Piercing Tracks
80,000 events used to fill histograms with
this granularity in ProtoDUNE-SP

## Slide 23
Ajib Paudel, June 12, 2019
dE/dx in data scaled to MC
~a few thousand events should suffice if we assume detector is uniform

## Slide 24
  Ionization density distributions from different physical samples in CNGS data are compared with MC expectations:
    Low energy showers from isolated secondary p0 show good agreement
    Stopping muons from nmCC interactions of CNGS neutrinos show a small (~2.5%) underestimation
dE/dx comparison
M. Antonello et al., Eur. Phys. J. C (2013) 73:2345
p0
m
Beam neutrino data, not cosmic rays!
Trying to do this
with cosmic rays
is harder – energy spectrum
is less well known
F. Varanini

## Slide 25
Electric Field Nonuniformities – Apparent in Individual Events

## Slide 26: Average dQ/dx vs Y
Three
Field
Cage
box-beam
Pairs
Four
Wire
Support
Combs

## Slide 27: Ajib Paudel found the CPA pattern in his dQ/dx analysis
Shows expected pincushion distortion

## Slide 28: Need for Faster Monitoring
ProtoDUNE-SP had an issue with APA 3's grid plane not being connected
Charge-up time of several days in ProtoDUNE-SP. Grid not perfectly transparent while charging up.
Affects dQ/dx means in a time-dependent way.
Underground: fewer cosmic rays, and more capacitance on the grid plane (to reduce an induction effect seen in ProtoDUNE-SP)

## Slide 29
David Adams, March 2019

## Slide 30: Alignment
Nearly every detector in HEP is aligned with cosmic rays
Elaborate examples:
  CMS: http://arxiv.org/abs/0911.4022
  ALICE: http://arxiv.org/abs/1001.0502
  An ATLAS Ph.D. Thesis: Vincente Lacuesta Miquel http://inspirehep.net/record/1429422/ And another: Regina Moles-Valls http://inspirehep.net/record/1339828/ No specific mention of cosmic rays in either of these, but the idea's the same. Tracks from the collision point are copious at the LHC, but there are "weak directions"

## Slide 31: "Strong" Directions in DUNE
Local deviations from nominal for inter-APA gaps
APA's seen from above, looking down a vertical gap
Need positive 𝛥x or positive 𝛥z
to fix this track (really a combination)
Need positive 𝛥x or negative 𝛥z
to fix this track (really a combination)
M. Wallbank

## Slide 32: Alignment results – ProtoDUNE-SP
No Diverter
No Diverter
Shorted
Diverter
100% Biased
Diverter

## Slide 33: Vertical Gap Measurement Precision: 35-ton experience
From Mike Wallbank's work on 35-ton measurements.
Some gaps had more crossing tracks than others and are thus better measured.
Assumes: 𝛥x and 𝛥z are constant along the length of the gap
Error bars
on these points
are arbitrary
cm
Stat errors of order 10-50 microns

## Slide 34: Measuring Angles
What if the gaps between the APA's aren't of uniform width?
What if the offsets along the drift field direction (x) vary with height (y)?
Repeat analysis in bins along y for each gap. Approximate analysis with two bins with centers 3 m apart and uncertainties for half as many tracks in each:

## Slide 35: Examples of "Weak" Directions (ATLAS alignment)
From Moles-Valls'
thesis.

## Slide 36: Difficult Distortions to Constrain
Bending of APA's:
More difficult with cosmics than steps at the gaps
Does not violate alignment pin constraints (others do, but manufacturing imperfections can result in systematic offsets)
Multiple scattering means that single tracks cannot be relied on to extract bending information. A large ensemble of them might be able to tease something out. But more z coverage per track helps.
Bent APA's: Will a "flat" APA stay flat when cold?
What is the magnitude of this that would escape our notice?
Cosmic rays are good at measuring local relative changes in positions (local in X, Z)
and not good at absolute positioning

## Slide 38: Estimate of Uncertainty on t0
Width of core of data distribution in 35-ton: 2 𝜇s. Half of the tracks are in the core, other half in the tails.
Here, Ntracks is the number of APA-crossing tracks.
You can average over the entire module or perform this APA-by-APA.
But only inner APA's.

## Slide 39: Outer APA's Contribution (ProtoDUNE-SP) and FD
With a mesh, you get a couple of hits on the far side
These hits will be gone
We will see only these on the outer APA's

## Slide 40
  Cathode non-planarity can also be measured from data: cosmic ms crossing the cathode plane
  Measurement can be performed during run but takes a long time underground (results shown here refer to ~6 months)
  This measurement refers to a full and cold TPC
  The apparent drift coordinate of the point where the muon crosses the cathode plane in both TPC is considered
  The difference Dtd=tdR-tdL is approximately proportional to the cathode distortion Dy in that point:
Measurement of cathode distortions in ICARUS
tdR ,tdL
Dy ≈ 1/3 vdDtd
tdR
tdL
Yellow line marks nominal cathode
position(Dy=0)
sDy ~ 2mm
Filippo Varanini
Jan 2017 DUNE
Collab meeting

## Slide 41
J.Raaf, J. Asaadi, LArIAT
Once you know how far the cathode is from the anode, you get:

## Slide 42: A Track in ProtoDUNE-SP that runs along U Wires
Unipolar induced charge over a span of hundreds of wires.
Can be used to calibrate 2D field response.

## Slide 43: We can learn from big showers
Front-end saturation, induction on back-side collection-plane wires due to wrapping
of induction-plane wires, FEMB-localized effects.

## Slide 44: Space Charge
Space charge from cosmogenic sources not expected to be significant in FD-SP
Space-charge effects in ProtoDUNE-SP and ProtoDUNE-DP are large – proportional to the cosmic-ray rate and the cube of the drift time
More than 20 cm of lateral distortion in hits in ProtoDUNE-SP
Beam-induced space charge not yet estimated.
Calibration of space charge in ProtoDUNEs needed to be able to extrapolate measurements to the FD (e-field distortions affect recombination for example, and thus the EM energy scale). Mike Mooney and Hannah Rogers have done a great job calibrating this with cosmics.
Broken Field Cage resistor has an effect on the field that can be measured in a similar way to space charge

## Slide 45: More Speculative: EM Showers
K. Ingles: 10 TeV horizontal muon simulated in the FD

## Slide 46: EM Showers
Cosmic rays will be the most abundant source of EM showers in the DUNE FD – mostly bremsstrahlung
Some 𝜋0's: 1300/module/year
Spectrum of EM energy loss is model dependent.
  energy spectrum of cosmic rays entering detector not perfectly known
  interactions of high-energy muons with argon atoms
Michels from stopping muons (11000 stopping muons per module per year) can help constrain EM energy reco
Delta rays

## Slide 47: ICARUS 𝜋0 Invariant Mass Reco
ICARUS Collab.
arXiv:0812:2373
212 Candidate
Events, Pavia
Surface Run

## Slide 48
Extras

## Slide 49: Muon Momentum from Multiple Scattering
Recent examples:
  ICARUS: https://arxiv.org/abs/1612.07715 (JINST 12 (2017) no.04, P04010)
  MicroBooNE: https://arxiv.org/abs/1703.06187 (JINST 12 (2017) no.10, P10010)
A DUNE FD module is 12 meters top to bottom, taller than MicroBooNE is long. 2.5 GeV muon or less will stop in DUNE.
Selected
beam neutrino-
induced muon
candidate tracks

## Slide 50: Recombination vs Angle
Same analysis as the MIP scale analysis, except binned in the angle with respect to the electric field.
Cosmic rays are depleted at horizontal angles
Even rock muons from the beam are depleted at angles that point along the electric field.
Energy spectrum of cosmic rays will depend on angle though!
Need stopping muons if you want precise, absolute scale.
Michels provide electron information, but are tricky – a fraction the energy is scattered about in little deposits not connected to the track. Should be do-able.

## Slide 51: dE/dx Calibration with MIPs
MicroBooNE has an analysis of the uniformity of detector response using tracks
Need t0-tagged tracks
  shouldn't be a problem in the FD. Tricky in ProtoDUNE-SP; even harder in ProtoDUNE-DP
Absolute precision calibration of MIP scale complicated by the energy dependence and need to model the energy spectrum.
Better measurement from stopping muons 30/day/10 kt (Sowjanya) Michels -> stopping electron dE/dx
K. Ingles

## Slide 52: Example: Radial Expansion is a Weak Direction
Tracks from the center of
the detector don't constrain
the radial size of
the detector.
Expand the detector, and all
the hits still fit!
Moles-Valls

## Slide 53: Extra Constraint from Cosmics
These tracks are no longer
straight when you expand
the detector.
Moles-Valls

## Slide 54: An Elaborate Example: CMS muon tracker
http://arxiv.org/abs/0911.4022
Essentially a sum of track-fit chisquareds as a function of alignment parameters
(offsets and angles). Add to that survey constraints which keep the fit from
wandering off in "loose" directions.
The total chisquared is quadratic in its parameters and minimizing it is a matrix inversion.
Another method in the paper uses non-Gaussian constraints and runs MINUIT.
Some hints at selecting well-formed track segments may be clues of things we have to
do too.
This example has only two displacements and two angles per rigid detector piece due to the strip geometry. We'll probably do ours in 3D.

## Slide 55: Local vs. Global Alignment
We measure gap offsets in x and z easily.
But muons only sample a small amount of x and z at a time – mostly travel in the y direction.
How to tell these kinds of distortions apart with cosmics? Cosmic rays sample local patches of (x,z) and are best at seeing step discontinuities
APA's viewed from top – distortions exaggerated
x
z
A

## Slide 56
APA Alignment Pin and Slot
  From the ProtoDUNE-SP TDR
Provides a One-Dimensional Position Constraint (X but not Y or Z, unless they are locking).
Provides a One-Dimensional Angular constraint if the slot is tight (roll in the above picture)
A series of pins provides an additional angular constraint (pitch)
On the figure above, roll and pitch are constrained but not yaw.
Manufacturing tolerances: With the pins engaged, wires can still be offset in ways we can measure.
35-ton Prototype was assembled without Alignment pins and slots
x
z
Hopefully constrain this sort
of distortion

## Slide 57: Hits on the Outer Side
Electric field drifts electrons away from the APA, towards the cryostat wall
Hits made inside the wire planes will still be there, but they will have different pulse shapes (asymmetric induction-plane signals)
Samples of these hits can be selected for study

## Slide 58: Wire Support Combs
Support combs placed so that the maximum unsupported run is 1.6 m.
ProtoDUNE-SP
TDR
Ed. comment: Thermal expansion of comb vs. APA frame could cause deviations larger than
150 microns

## Slide 59: Field Cage Beams and Wire Support Combs
From Kevin
Wood's
Collab
Meeting
Talk
Sep 2018