## Slide 1
George Lolov
NBI 2019
10/23/2019
NuMI Target Construction & Megawatt Modifications

## Slide 2: Outline
10/23/19
NBI 2019 / NuMI Target Construction and Megawatt Modifications
  NuMI Overview
  Target Assembly Overview
  Target Fins
    Overview
    1 MW Modifications
    FEA Results
  Downstream Beryllium Window
    Overview
    Preliminary FEA
    1 MW Modifications
    Final FEA
  Baffle
    Overview
    1 MW Modification
    FEA
    Manufacturing

## Slide 3: NuMI Overview and Challenges of 1 MW Upgrade
Current Experiment Metrics
Beam Power: 700-750 kW
Beam Energy: 120 GeV
Beam Intensity: 5e13 Protons/Pulse
Beam Bunches: 588 Bunches/Pulse
Pulse Length: 11 µs
Duty cycle: 1.33 seconds
2020/2021 Beam Upgrades
Beam Power: 1 MW
Beam Intensity: 6.5e13 Protons/Pulse
Duty cycle: 1.2 seconds
MET-05 designed for 1 MW use
TA-02 | TA-03 | TA-05 | TA-06, 07, 08, 09
7/15/19: Transferred to C0 hot cell | 8/9/19: Transferred to MI-65 Morgue for cooldown | 8/12/19: Fabrication + Assembly 100% complete | Part procurement has begun
1 MW Upgrade Challenges |  | 
Temp. and Stress Increase from Beam Heating | Increased Radioactivation | Aging Infrastructure
Pre-target beam window Target core and baffle Target DS window Horn stripline cooling Radioactive water (RAW) systems, target chase air handling, chiller Hadron absorber temperature monitoring | Additional shielding to the RAW room and target chase Review NuMI shielding and tritium production assessment for 1MW Retrofit or expand existing tritium mitigation systems New radiation-hard hadron monitors | Decay pipe window repair plan​ Target/horn module positioning drives Chase cooling retrofits and expansion
10/23/19
NBI 2019 / NuMI Target Construction and Megawatt Modifications

## Slide 4: Target Assembly Overview
Target Assembly 05
Baffle
Target Rail Assembly
Target Canister
Target Carrier
Upstream (Beam Enters)
Downstream (Beam Exits)
Graphite Slug Shield
Beam Heat Dissipation
Graphite Target Fins
Cooling Rail
Fin Enclosure
Helium Environment
Frame
10/23/19
NBI 2019 / NuMI Target Construction and Megawatt Modifications
Hylen Device

## Slide 5: Target Fins
10/23/19
NBI 2019 / NuMI Target Construction and Megawatt Modifications
Graphite Grade: POCO ZXF-5Q

## Slide 6: Location of Target Fins
TA-05 Target Carrier
MET-05 Graphite Fins
MET-05 Target Canister
10/23/19
NBI 2019 / NuMI Target Construction and Megawatt Modifications

## Slide 7: Target Canister Overview
Enclosure for target fins
Helium environment
Water cooled walls
10/23/19
NBI 2019 / NuMI Target Construction and Megawatt Modifications

## Slide 8: Target Rail Overview
Back View
Front View
48 target fins + 2 budal fins
Graphite Grade: POCO ZXF-5Q
Water cooled channel within the rail
Target fins
Water Supply/Return
Cooling Rail
Budal Fins
10/23/19
NBI 2019 / NuMI Target Construction and Megawatt Modifications

## Slide 9
Steady-state thermal analysis
Fins width updated to 9 mm
Peak graphite fin temperature: 913 °C
Budal brackets peak temperature ~316 °C
10/23/19
NBI 2019 / NuMI Target Construction and Megawatt Modifications
1MW Design Modification 1: Increased Fin Thickness

## Slide 10
Reduce conduction path length in Aluminum
  Shorten and keep Al brackets closer to cooling rail
  Longer graphite fins extending towards cooling rail
Original Budal fins/brackets design
Aluminum bracket
US Budal fin
DS Budal fin
10/23/19
NBI 2019 / NuMI Target Construction and Megawatt Modifications
1MW Design Modification 2: Budal Bracket/Fin Redesign

## Slide 11
Addition of four graphite winged fins currently at downstream end of target
Provides protection for decay pipe window as well as Horn 1 neck in the event of completely mis-steered beam
Winged fins
Updated Budal fins/brackets
10/23/19
NBI 2019 / NuMI Target Construction and Megawatt Modifications
1MW Design Modification 2: Addition of Winged Fins

## Slide 12
(I. Rakhno)
NuMI AIP 1 MW beam parameters
Energy: 120 GeV
Power: 1 MW
σ = 1.5 mm
Repetition rate: 1.2 s
Pulse length: 10 µs
Protons/pulse = 6.25e13
Protons/s = 5.21e13
MARS geometry and binning
48 fins: 24 mm x 9 mm x 150 mm
x-y direction:
18 x 18 bins: x from 4.25 mm to -4.25 mm, y from -4.25 mm to 4.25 mm (0.5 mm x 0.5 mm bins)
6 x 6 bins: x from 3.75 mm to -3.75 mm, y from -51.7083 mm to -8.79167 mm (1.5 mm x 8.6 mm bins)
6 x 6 bins: x from 3.75 mm to -3.75 mm, y from -138.042 mm to -63.4583 mm (1.5 mm x 14.9 mm bins)
z-direction:
4 x-y data sets per fin for 48 fins
[(18 x 18 x 4) + (6 x 6 x 4) + (6 x 6 x 4)] x 48 = 76032 data points
10/23/19
NBI 2019 / NuMI Target Construction and Megawatt Modifications
MARS Energy Deposition Data

## Slide 13
Tgraphite, max: 997 °C
ΔT ~ 107 °C from SS temperature
TARGET RAIL ASSEMBLY
Al COOLING RAIL & PRESSING PLATES
Negligible change in temperature of Al cooling rail and pressing plate from beam pulse
Cooling Water
10/23/19
NBI 2019 / NuMI Target Construction and Megawatt Modifications
Thermal Analysis: Steady State + Beam Pulse

## Slide 14
Downstream Beryllium Window
Target Rail Assembly
PF-60 Be disk e-beam welded to Al ring
Be disk and Al ring weldment then e-beam welded to Al flange
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 15: Thermal Analysis Results
Tmax: 91.5 °C
Tmax: 106 °C
Steady-state temperature distribution
Temperature immediately after beam spill
Initial temperature: 25 °C
Temperature after first beam pulse: 41 °C
K. Ammigan
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 16: Structural analysis
5 psig Helium internal pressure (worst-case condition)
At steady-state, Tmax: 91 °C
At steady-state immediately after pulse, Tmax: 106 °C
Internal surface
Peak σequiv = 200 MPa (center)
External surface
Peak σequiv = 182 MPa (edge)
External surface
Internal surface
Peak σequiv = 226 MPa (center)
Peak σequiv = 185 MPa (edge)
K. Ammigan
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 17: Peak Equivalent Stresses Exceed Be Yield Strength
Internal pressure (5 psig) | Tmax (°C) | Internal surf. σequiv, max (MPa) | External surf. σequiv, max (MPa)
Steady-state | 91 | 200 (center) | 182 (edge)
Steady-state + beam | 106 | 226 (center) | 185 (edge)
Beryllium strength properties at room temperature
Lower YS at elevated temperatures
Chemical composition closer to S-65 grade (VHP)
Expect anisotropy in properties due to rolled and textured material
Uncertain long-term effects of radiation damage
K. Ammigan
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 18: Proposed Cooling Loop
C. Crowley
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 19: 1 MW Modification: Active Cooling Loop
Custom Bent Tubing
0.5 GPM Water Diverted from Cannister Supply
Thermocouple
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 20: Thermal Analysis – Active Cooling
Steady-state temperature distribution
Temperature immediately after beam spill
Peak temperature reduction of about 16 °C
K. Ammigan
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 21: Peak Equivalent Stresses in Be Disk With Active Cooling
Beryllium strength properties (at RT)
Stresses now below YS of other Be grades
K. Ammigan
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 22: Baffle Overview
Al Casing
Graphite Slug
0.010” thick beryllium windows at US and DS ends
Graphite core press fit at 150 °C - 160 °C with 0.005” – 0.006” interference fit at RT
13mm Hole
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 23: 1 MW Modification: Increased Hole Diameter
Baffle hole diameter enlarged from 13 mm to 15 mm for NuMI Target Systems AIP
Since beam spot size increased, baffle hole diameter must also increase proportionally to prevent scraping
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 24
ANSYS Steady-State Thermal Results
Peak Graphite and Aluminum temperatures: ~50 °C
Peak Beryllium temperature: 53 °C
beam
K. Ammigan
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 25
Direct beam interaction - thermal and structural FEA results*
NOvA beam parameters: 120 GeV, 0.7 MW, σ: 1.3 mm, 4.9e13 ppp, 1.33 s rep. rate
Temperature
Equivalent stress
Peak ΔT in graphite: 339 °C
σequiv, max in graphite: 14 MPa
σequiv, max in Al: 13.6 MPa
K. Ammigan
Baffle expected to survive direct beam interaction
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 26: Baffle Press Fit Fixture
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 27: When Things Go Wrong…
Improper shrink fit
Poor temperature monitoring
Improper tooling (tried to use 13mm stacking rod on new 15mm bore 1MW baffle).
NBI 2019 / NuMI Target Construction and Megawatt Modifications
10/23/19

## Slide 28: Summary
Temperature, Stress, and Beam Sigma increases due to increased beam power warranted redesigns of:
  Target Fins
  Downstream Beryllium Window
  Baffle
TA-05 ready for 1 MW operation