## Slide 1: LBNF Target Exchange System - Design Progress
Eric Harvey-Fishenden, Chris Densham, Mike Fitton, Joe O’Dell, Peter Loveridge (High Power Targets STFC RAL)
In conjunction with FNAL Target Systems Department
NBI Fermilab 2019

## Slide 2: LBNF Neutrino Beamline
Horn A & Module: most of the important interfaces between RAL and FNAL
Horn A & Module
LBNF/DUNE Experiment
LBNF Target Hall

## Slide 3: Why Do We Need To Exchange Targets?
Horn & Target configuration for LBNF/DUNE optimised using genetic algorithm (Laura Fields)
Optimum geometry for physics tends towards 4λ length target (≈2m)
Achieving a long target pushes fundamental limits (deflection, natural frequency, manufacturing etc.)
  Must be prepared for targets to fail
Horns are inherently complex, costly and take a long time to produce
Target cost ≈1/10th horn cost, and spares can be produced more readily
  Hence the need for an independently exchangeable target

## Slide 4: Current Experience – T2K
LBNF target exchange is a similar concept but under different constraints
  Longer target, different exchanger interfaces, more horn bore clearance
  Experience from T2K will feed into LBNF exchanger design

## Slide 5: Conceptual Procedures for Target Exchange
1
2
3
4
5
6
7
8
12…
11
10
9

## Slide 6: Target Concept Selection
Target exchange impacts were a key consideration in the LBNF target concept selection:
Target exchange was considered for each concept including:
  Procedures required
  Risk associated with target exchange
  Time taken to exchange target system
  Impacts on the work cell requirements
Double target
2.2m supported target
Single cantilever target

## Slide 7: Target Concept Selection
Double target
2.2m supported target
Single cantilever target
Option | No. Operations | Target Handling Time (Days)
1) 2.2m Supported Target | 41 | 22
2) Double Target | 35 | 14
3) Cantilever Target | 18 | 5
John Back’s assessment calculates an extra 13-19 days running per year with a single cantilever target to achieve same theoretical physics performance as a 2.2m supported target
A single cantilever target was selected as providing the optimum performance:
Small hit in instantaneous physics versus a longer, downstream supported target, but;
Instantaneous physics hit likely to be made up in integrated performance due to a more robust design
  Simpler target is less likely to fail in operation
  Takes less time to replace outside of a planned maintenance schedule

## Slide 8: LBNF Work Cell During Target Exchange
Horn module supported from the top of the work cell
Target exchanger located on lift table on work cell floor
Persons using through-wall manipulators are approximately 4m away from the front face of the horn

## Slide 9: T2K Target Exchange System
Target exchange set-up in remote maintenance area (RMA)
Target exchanger and through-wall manipulators
View through from human side of RMA

## Slide 10: T2K Target Exchanger
Lift table
Screw jacks
Load cells
Limited movement gimbal
Spring overload protection
Air motors
Passive linear rails
Docking interface
Catch tray
Target carriers
Floating table

## Slide 11: Some Differences for LBNF
Length of target exchanger
  T2K Target 0.9m (1.7m exchanger)
  LBNF Target 1.5m+ (2.8m exchanger)
Docking interface
  T2K relies on perpendicularity of several interfaces
  Limited “real estate” on LBNF
  LBNF supports are not a robust datum for alignment
  Potential for large moments to be applied to horn A
→ “Hard” mechanical docking/alignment likely not possible for LBNF
Docking interfaces on horn front end
Cross rail system
  Moving target from “x” rail to “z” rail is fiddly and time consuming
Passive rails
  Range of motion required to push or pull target carriers along rails would be excessive for LBNF
T2K
LBNF
T2K
LBNF
→ Use motorised linear rails for LBNF target exchanger

## Slide 12: LBNF Target Exchange System Concept
Dock exchanger @ target supports to accurately fix position at front end of exchanger
Allow some rotation about that position to align the exchanger axis to the horn bore axis
  Alignment diagnostics may be challenging – investigating triple beam interferometers/autocollimators for laser alignment
  Sensitivity/accuracy of these systems may be no better than a “hard” mechanical alignment but the risk of damaging other systems is reduced
Horn
Target supports
Target
Docking
interface
Exchanger support and adjustment
Exchanger
Target Carrier
Linear rail

## Slide 13: LBNF Target Exchange System Requirements
Horn module suspended from the top of the work cell
Exchanger located on lift table on work cell floor
  Relative positions not well defined
Horn tilted at approximately 6° from horizontal
Exchanger must have sufficient compliance to allow location pins at front end to align
  Compliance must be well controlled such that the exchanger is not unstable
Driven jacks/linear stages must allow fine adjustment to align the exchanger slides to the horn bore
Target carrier must have some small in-plane compliance to allow target to locate on its alignment pins, but must not allow angular rotation
  Target must clear horn bore without touching

## Slide 14: Potential Layout
Screw jacks
Load cells
Spring overload protection
Actuated linear rails
Docking interface
Catch tray
Target carriers
Floating table
Challenges:
Stiffness/mass trade-off
Minimising complexity

## Slide 15: Docking Interface Ideas
Spring centred location pin on spherical bush
Tapered hole/slot in target supports
Spherical stop to fix separation between exchanger and target supports but also permit small rotational adjustments after docking
Still need a method of securing the exchanger to the target supports
Layout of pins/holes may change
- Prototyping of interface will be necessary
Target support
Exchanger

## Slide 16
Summary
The LBNF secondary beamline will use a remotely exchangeable target
The procedures for exchanging targets have been developed and documented
The concept for an LBNF target exchanger is being developed into preliminary design ideas
  Plenty of R&D still to be done
Lessons learnt from the target exchange system for T2K are being implemented in to the LBNF design
Based on T2K experience we expect to go through a few iterations before we have an exchanger suitable for “on-line” target exchange
  Current schedules show that this will be possible

## Slide 18: Backup - Schedule
RAL Schedule currently has exchanger testing during summer 2024
Approx. 6 months allocated to redesign prior to delivery to FNAL
Feb 2025 earliest possible date for actual integration and exchange testing with Horn A on test stand at FNAL
  Assuming this schedule is correct, there are several years available to iterate and potentially improve exchanger prior to an “on-line” target exchange
  This will also allow scope for FNAL RH technicians to develop and become familiar with procedures

## Slide 19: Backup - Exchanger Table Supports
Spring support (lockable)
Rose joint
X-adjustment stage
Spring centered floating stage (ball transfer units)
Rose joint
Load cell
Load cell
Screw jack
Screw jack
Thrust tapered roller bearing
Challenges:
Flexibility/stability compromise
Maintaining simplicity