## Slide 1
C-Zero Radioactive Component Storage Facility
By: Mike Campbell
October 25, 2019
Managed by Fermi Research Alliance, LLC for the U.S. Department of Energy Office of Science
NBI2019: 11th International Workshop on Neutrino Beams and Instrumentation

## Slide 2
Contents:
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019
Brief History of Czero and the Project Team
The Design and Build
  Civil Construction
  Bridge Crane w/ Vertical Sliding Shield Wall
  Sliding Shield Door w/ Railcar Pass-Thru
    Cameras & Remote Viewing Station
Moving In Our First Hot Component

## Slide 3
Brief History of Czero
Czero building originally completed in 2004 for the BTEV Project (was cancelled)
Had Tevatron magnet ring passing thru otherwise empty 30’ x 80’ detector hall
Had 3 hot-storage bays and a hot cell w/ telemanipulators added 2012 (Czero RHF)
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 4
Brief History of Czero
Summer, 2013: Long-Term Radioactive Storage Facility Task Force Report
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 5
Brief History of Czero
Design concept later modified to:
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 6
Brief History of Czero
Design concept later modified to:
New wall being added
New sliding shield door
New rail car and track
New radioactive storage area
New crane inside w/ vertical sliding shield wall
No crane coverage in this area
Access/Service area
Lead-glass window
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 7
Brief History of Czero
Project began 2014
Project Team:
Pat Hurh, Ryan Schultz, Cory Crowley – Engineers AD/TSD – Project oversight
Jonathan Hunt – Engineer, FESS – Civil construction
Cory Crowley – Engineer AD/TSD – Bridge-crane w/ vertical sliding shield wall
Mike Campbell – Engineer AD/TSD – Sliding shield door w/ railcar pass-thru
Keith Anderson – ME Build Tech AD/TSD – Cameras and remote viewing Station
Cervando Castro – ME Build Tech AD/TSD – Lead builder (also Bob A., others)
Budget: $ 3M
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 8
Civil Construction
Civil construction included:
Demolition of existing concrete shield plug and other structures
Two new concrete walls – one w/ large opening, other w/ lead glass window
Install structural steel for crane (columns & rails)
Install hot-side bridge crane w/ redundant / relocated motion controls
Electrical infrastructure build-out (lighting, crane & door control panels, etc)
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 9
Civil Construction
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 10
Civil Construction
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 11
Civil Construction
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 12
Bridge Crane w/ Vertical Sliding Shield Wall
4X hydraulic lifting cylinders
Lead-glass window
Crane rail
Crane rail
Horizontal actuating panel
Horizontal actuating panel
Rising shield wall
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 13
Bridge Crane w/ Vertical Sliding Shield Wall
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 14
Bridge Crane w/ Vertical Sliding Shield Wall
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 15
Bridge Crane w/ Vertical Sliding Shield Wall
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 16
Sliding Shield Door with Railcar Pass-Thru
Camera access holes w/ sliding covers (Keith A)
Upper guide
track and drive
Sliding shield door
Lower guide track
New rail car and tracks
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 17
Sliding Shield Door with Railcar Pass-Thru
2X long standard Hilman rollers
Small shield blocks fill in the gaps at both ends and in between the rollers
2X gaps for rail car tracks plus center gap for motor power cable
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 18
Sliding Shield Door with Railcar Pass-Thru
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 19
Sliding Shield Door with Railcar Pass-Thru
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 20
Sliding Shield Door with Railcar Pass-Thru
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 21
Cameras and Remote Viewing Station
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 22
Cameras and Remote Viewing Station
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 23
Cameras and Remote Viewing Station
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 24
1
2
3
4
7
5
6
8
9
Mu2e Components
NuMI / Nova Components
Moving In Our First Hot Component – The Planned Layout
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 25
Moving In Our First Hot Component
June 27, 2019
NuMI Horn #PH1-02
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 26
Moving In Our First Hot Component
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 27
Moving In Our First Hot Component
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 28
Moving In Our First Hot Component
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 29
Moving In Our First Hot Component
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019

## Slide 30
Moving In Our First Hot Component
Questions ?
C-zero Radioactive Component Storage Facility – Mike Campbell 10-25-2019