## Slide 1
George Lolov
NBI 2019
10/24/2019
Air Diverter for Cooling 1MW Horn Stripline

## Slide 2: Outline
10/24/19
Air Diverter for Cooling 1MW Horn Stripline
Horn 1 Overview
  Environment
  Stripline Design
Motivation for Testing and Requirements
Testing and Design Goals
T-Block Air Diverter
Testing
  Pressure
  Convection Coefficient
Air Diverter Redesign
Test Results

## Slide 3: Horn 1 Layout and Environment
Airflow
Air Diverter
Horn Stripline
Chase is kept cool with a large fan delivering ~ 25,000 CFM
Will be increased to ~ 28,000 for 1MW operation
Chase
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 4: Horn 1 Stripline Overview
Upper Flags
Lower Flags
Inner Flags
Outer Flags
2 Main Stripline Areas
  8 flags where majority of testing/analysis focused on
  Inner stripline
Stripline Span
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 5: 1MW Stripline Motivation & Requirements
Existing 700kW stripline & air diverter system is not a viable solution at 1MW.
Max stripline temperature desired to be less than 100C at any point.
Must maintain 100,000,000 pulse lifetime requirement. Temperature & resultant material creep makes pulse life determination impossible.
Analysis Credit: Zhijing Tang
Improve air cooling to stripline structure and reduce stripline temperature < 100C
Goal:
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 6: Testing & Design Goals
Understand existing air flow characteristics & heat transfer.
Identify improvements to existing structures & verify through iterative theoretical & experimental testing.
Verify conclusions and final production design with repeat wind tunnel & heat transfer test.
Analysis Credit: Lionel Pittman
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 7: CFD Conclusions of Existing Diverter
Provides good flow for inner lower flags; moderate flow for inner upper flags.
Sharp edges and pinch points appear to impeded air velocity.
Initial thoughts were that they created eddy currents to improve flow.
Theoretical simulations show these can be improved.
Sharp Edges
Middle Duct
Outlet Duct
Inlet Duct
Divider
Mounting Bracket
Low Airflow
Low Airflow
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 8: T-Block Air Diverter
Solution needed to address stripline upper flags and vertical side spans.
Solution:
  Dedicate T-block with internal duct (direct access to upper flags)
Air deflection from T-block appears to greatly help vertical side spans as well.
Multiple diverter angles tested; winner is 45 degrees at ~600 CFM.
Upper Flags
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 9: T-Block Air Diverter Location
T-Block to be Redesigned
Stripline Route
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 10: T-Block Air Diverter
Drop in replacement T-block.
Channel dimensions minimized (8” wide X 4” deep).
Supply will employ quick disconnect coupling.
Outlet
10/24/19
Air Diverter for Cooling 1MW Horn Stripline
C. Crowley

## Slide 11: Test Setup - Pressure Testing Trials
Fixed on each of the 8 flag faces and measured airflow pressure at 9 locations on the flag surfaces
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 12: Pressure Testing
Ran pressure tests for each iteration of the top and bottom diverters.
Results mostly inconclusive. Pressure drop not large enough to provide reliable data.
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 13: Convection Coefficient Testing
Al coupon with heating pad and thermocouple inside.
  Set on each of the flag faces
  Set heater to 80W
  Turned on the airflow
  Observed cooling curve until SS temperature was reached
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 14: Old / New Diverter Comparison
Sharp Edges
Middle Duct
Outlet Duct
Inlet Duct
Divider
Mounting Bracket
Low Airflow
Low Airflow
Smooth Edges
Middle Duct
Outlet Duct
Inlet Duct
Divider
Mounting Bracket
Balanced Airflow
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 15: New Diverter Design: Inlet
New Inlet features 4 sheets curved into elliptical geometry.
Initially tried creating from cardboard- didn’t turn out so well.
Split into 4 sections and 3D printed (K. Anderson)
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 16: New Diverter Design: Inlet
DEVELOPMENT OF BELL MOUTH FOR LOW SPEED AXIAL FLOW
COMPRESSOR TESTING FACILITY
Apurva Tiwari Et al.
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 17: New Diverter Design: Outlet
Because we doubled the inlet area, we also doubled the outlet area – airflow covers more flag surface area.
Didn’t bother with cardboard, split up into 4 pieces and 3D printed.
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 18: Diverter Prototype
3D Printed Inlet
3D Printed Outlet
Cardboard Middle Section with Cardboard Divider
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 19: Stripline Problematic Areas: Between Striplines
Segment # | External (W/m2∙K) | Internal (W/m2∙K)
1 | 5 | 2
2 | 15 | 5
3 | 36 | 5
4 | 36 | 5
5 | 36 | 5
6 | 36 | 5
7 | 36 | 5
8 | 15 | 5
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 20: Convection Coefficient Testing
Heating Pad
Adjacent Coupon
T
T
J-Type Thermocouple
3/8”
3/8”
3/8”
3/8”
3/8”
4.25”
4.25”
Assumed stagnant air convection coefficient between the striplines unless proven otherwise.
Simulations showed inner stripline temps to be too high.
Experimentally determined convection coefficient for most problematic areas.
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 21: Convection Coefficient Test Results
6 Total Tests – changed top/bottom diverter designs, added insulation.
Not all flags showed cooling at 80W, Wattage had to be adjusted to equilibrium.
10/24/19
Air Diverter for Cooling 1MW Horn Stripline
Final Top/Bottom Diverter Designs

## Slide 22: Updated Analysis Results
Steady state temperatures @ 1MW appear to meet requirements of <100C.
Hot spots are result of remaining conservative cooling coefficients. Further testing could reduce further but design goals are met.
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 23: Final Diverter Design
Mounting Bracket
6061 Aluminum Sheets
Welded at seams
10/24/19
Air Diverter for Cooling 1MW Horn Stripline

## Slide 24: Summary
Updated air diverter design(s) needed to maintain acceptable Horn 1 stripline temperatures during 1 MW operation
Convection coefficient testing was conducted to identify problematic areas and areas for improvement
Testing led to design revisions until final designs for the top/bottom diverters were selected
Stripline temperatures were verified with final FEA and experimental test
10/24/19
Air Diverter for Cooling 1MW Horn Stripline