## Slide 1: LBNF Target Hall Remote Handling Facilities and Horns exchange procedure
Vladimir Sidorov
NBI 2019
25 October 2019

## Slide 2: Remote Handling Equipment Requirements
  Remote Handling Facilities and Equipment must provide methods to support radioactive component replacement and short-term storage
  The remote handling shall be integrated into the infrastructure of the complex both underground and above ground. (This indicates that Remote Handling Facilities shall be designed for 2.4 MW operations since it is not upgradeable)
  The remote handling shall incorporate ALARA (As Low As Reasonably Achievable) principles into facilities, equipment and procedures

## Slide 3
Target Chase
Baffle
Target/Horn-A
Horn-B
Horn-C
Decay pipe
The Target Hall enclosure contains the components, Baffle , Target and Horns, for generating neutrinos and focusing them toward the near and far detectors.
All components have the life limits and have to be replaced with new ones.

## Slide 4
LBNF Target Hall Remote-Handling Facilities
All components are replaced remotely in the Work Cell and stored in the morgue located inside the target hall. The morgue location inside the Target Hall simplifies the remote handling operation. The radioactive components are transported to the permanent storage place after the cool down in the Target Hall morgue.
All Remote-Handling operations are provided by using the bridge
crane 60 ton capacity with redundant motions in the Target Hall and 60 ton crane in the service building.
Work
Cell
Morgue
T-blocks pit
Rails
Service
building
Target Chase
Beam line
Truck
bay
Horns
Assembly
stands
Transfer
Cart
Shielding door
Crane

## Slide 5
      Target Complex Remote-Handling Facilities, Old design
60
Work Cell
T-blocks storage pit
Morgue
Casks
Door
Rails
Target Pile
Maintenance
area

## Slide 6
Real life examples from NUMI Target Hall
T-block
storage
Work
Cell
Target Chase
T-block
Horn with module

## Slide 7
Video Center
Video cameras
Target Hall
Crane
Work cell
PELCO SD4-W0 SPECTRA SD4-W0
Operations remote viewing system
The video system is integral to all remote handling steps.

## Slide 8
The Work Cell and Operation Center are located in the right corner of the downstream end of the Target Hall. The top shielding covers ( 14” thick steel blocks) are installed and removed by crane remotely.
Work Cell and Operation Center
Work Cell
door
Carts rails
Top covers
Operation
Center door

## Slide 9
Transfer cart
with lifting tables
Shielding plate
Chain drive
mechanism
Tele-manipulator
Work Cell and Operation Center
Operation Center
Work Cell
Guide rails
300”
256”
The Work Cell is equipped with remotely operated transfer cart with lifting tables, remotely operated door, Lead-Glass windows and video cameras.
Led-Glass window
Door

## Slide 10
Two doors 12” thick and 20’ tall are installed on the base plate in the front
of the Work cell. Both doors are guided at the bottom and top. Doors are moved with
independent motorized screw jacks. Doors weight 44,000lb –right; 47,000lb left.
One door opened
Both doors opened
Both door closed
Screw jack
90”
240”
Work Cell Door

## Slide 11: Target Hall Work Cell Horns replacing system
Work cell
Module
Horn-B
Transfer cart
Lifting tables
Rails inside WC
Rails
Chain
Drive
Operation
Center
The module with horn is delivered into the Work cell from the Target chase by crane.

## Slide 12
The lifting tables are raised up and touching the horn support legs.
The horn is disconnected from module and lowered down by lifting tables.
The work cell door is opened.
The cart with Horn is moved out from the Work cell.
Chain type: CH60PS2000; Stroke 10meters ( 397in);Push-pull force 2,810 lbf; Speed 7 fpm

## Slide 13
The Horn is picked up by crane using horns lifting fixture and dropped into the morgue through the opened concrete shielding hole . The concrete shielding blocks are installed. New Horn is arrived , delivered to the Work Cell and attached to the module.

## Slide 14
Target Hall morgue and T-blocks pit design
Morgue
T-blocks pit
Work Cell
Storage
box
The shielding between morgue and T-blocks pit is removed. Concrete blocks and T-blocks
support lips are modified. The storage box is redesigned.

## Slide 15
The platform support I-beams are mounted into the wall.
The same size platforms can be installed on middle and upper levels.
The corbel is made from 8” I-beam.
Platform
Morgue design
Platform weight-1,757lb.
80”
155”

## Slide 16
Horn A and Horn C Platform FEA calculation
Deformation and stress are low

## Slide 17
Corbel FEA calculation
Deformation and stress are low

## Slide 18
T-Blocks pit
Storage box
Shielding plate
Stripline block
T-Blocks
120”
174”
There is no shielding between the morgue and T-blocks pit.
Shielding wall
Concrete blocks

## Slide 19
Work cell hatch
180”
48”
Work Cell
hatch
WC Hatch
Shielding
plates
The hatch is located in the middle of the work cell between two transfer cart rails.
The hatch is covered by two shielding plates, 12” thick.
48”
Cooling
panel
TH Cooling panels can be stored under the Work Cell. The panel is delivered into the storage place through the hatch. The special lifting fixture and the panel support stand are required for the cooling panel storage.

## Slide 20
Morgue usage LBNF
P.Hurh

## Slide 21
Two halves of the sliding target hall main door are made of 6 inches of poly and 10 inches of steel. Both doors are running on the base plate by push-pull electrical cylinders. Doors are guided by the guide rail and rollers on the top and rollers on the bottom. Limit switches are controlled the doors position. The door has double air sealing.
Target hall main entrance door
Steel
door
Borated
Polyethylene
Base plate
Door frame
Electrical
cylinder
Guide rail
Limit switch
Seal
clamp

## Slide 22
The door is mounted on the outside 5 ft long wall the polyethylene facing to the Target Hall and the steel facing to the Rail Corridor.
The door must be providing the shielding of the service areas from the Target Hall.
Steel
Poly
Air sealed
roll door
Air sealed
roll door
Shielding
Door
Rails Corridor
Service building
Target
Hall

## Slide 23
Roll door
Shielding Door
Air sealed door
The shield door will incorporate an air seal to separate the radioactive
air volume of the Target Hall enclosure from the air volume of the neighboring
service areas.
Rails Corridor
Target Hall
Service
Building

## Slide 24
The cask with closed door is placed on the transfer cart by crane and moved from the target hall to the Service building through the Rails Corridor, where the horn is uploaded on the truck and moved to the permanent storage place.
NUMI Target Hall
Rails Corridor
Horn transportation

## Slide 25
Summary
The Remote Handling Facilities and equipment are designed for 2.4 MW operations and providing the support of the radioactive components replacement and short-term storage.

## Slide 26
Back up slides

## Slide 27
Top guide rail
Top linear bearing
Screw jack
Nut
Left door
drive
Right door
drive
Hilman rollers
Bottom guide rollers
Work cell doors details

## Slide 28
Shielding door air seal
Air seal
Door closed
Door open
Air seal
Gap
Gap
Seal

## Slide 29
Shielding door double seal
Seal clamps
Middle seal
Clamp
Door seal
Seal
angle
Clamp
Seal
angle
Top seal

## Slide 30: Horns Casks
172”
27.3”
75 5/8”
90”
57”
108.75”
127.75”
84”
225”
27.3”
4”
3”
1.5”
4”
NUMI Horn Cask
LBNF Horn B Cask
The LBNF Horn cask is 53” longer,27” wider and 34.75” taller then NUMI Horn cask. The NUMI cask with horn weight is 30 ton, the LBNF cask with horn weight is about 52 ton.
4”
4”

## Slide 31
Horn exchange , old version
The horn is disconnected from the module ,lowered down by the structure and placed on the cart.
The cart with the horn is pulled into the cask by a chain drive mechanism. The small door of the work cell is open. The cask door open.
Chain Drive

## Slide 32
Horn-A Module in Work Cell
Horn-A

## Slide 33
Horn-C Module in Work cell
Horn-C