## Slide 1: BNB Target Beam Scans
Alyssa R Miller
Fermilab Accelerator Division, External Beams Department
NBI 2019

## Slide 2: Purpose
9.5mm
1.6mm
8.8mm
Maximize target lifetime
  Ensure symmetric energy deposition of beam on target
Autotune calibration check
  BPM electrical center can drift
  Multiwires give mechanical center wrt target alignment
How can we improve beam quality?
How can we learn more about BNB beam dynamics with instrumentation?

## Slide 3: Pre-target Instrumentation

## Slide 4: Functional Pre-target Instrumentation

## Slide 5: Target Scan Procedure
Autotune program
  BPM feedback tells trims how to move beam to center
    Determined by previous target scans
  Turn off for target scan
Change downstream trim settings to move beam across target
  2-bump to move position horizontally and vertically
  2-bump to move angle horizontally and vertically

## Slide 7
Chart: Positions Over Time
1
2
Vertical scan over target face, horizontal beam position isn’t moved from zero
Horizontal scan over lower target fin, vertical position isn’t moved from fin (~ -8mm)

## Slide 8
Chart: Vertical Target Diameter Scan
Rise | 0.010195 | 0.01196
Flattop | 0.014005 | 0.014019
Fall | 0.0078539 | 0.0040765
Tolerance | 0.014 | 0.014
Fin flat | 0.0084003 | 0.008406
Off target flat | 0.00054146 | 0.00054064
Nominal | 1
Tolerance | 1
Center | 1
1
2
3
4
5
Beam on lower fin
Beam between lower fin and target face
Beam on target face
Beam moving off target face into air cooling gap
Beam in air cooling gap

## Slide 9
Chart: Vertical Target Diameter Scan
Rise | 0.010195 | 0.01196
Flattop | 0.014005 | 0.014019
Fall | 0.0078539 | 0.0040765
Nominal | 0.014
Tolerance | 0.014 | 0.014
Center | 0.014
Fin flat | 0.0084003 | 0.008406
Off target flat | 0.00054146 | 0.00054064
Nominal | 1
Beam center determined by BPM linear estimates in target scan data -0.19mm
Autotune center and tolerance from previous scan 0.39 +/- 0.5mm Off by 0.53mm
Notes: When beam is actually on the center of the target, the BPM is -0.19. This is the instrument’s offset.
BPMs will drift

## Slide 10
Chart: Horizontal Target Fin Scan
Rise | 0.004302 | 0.0070363
Fall | 0.0058609 | 0.002082
Flattop | 0.0083487 | 0.008281
Tolerance | 0.0084 | 0.0084
Nominal | 1
Tolerance | 1
Center | 1
Linear Fits | 1
1
2
3
4
Beam moving off lower target fin into air cooling gap
Beam on target fin
Beam moving off lower target fin into air cooling gap
Beam in air cooling gap

## Slide 11
Chart: Horizontal Target Fin Scan
Rise | 0.004302 | 0.0070363
Fall | 0.0058609 | 0.002082
Flattop | 0.0083487 | 0.008281
Nominal | 0.0084
Tolerance | 0.0084 | 0.0084
Center | 0.0084
Nominal | 1
Tolerance | 1
Center | 1
Beam center determined by BPM linear estimates in target scan data -0.31
Autotune center and tolerance from previous scan 0.46 +/- 0.5mm Off by 0.31mm
1
2

## Slide 12
Chart: Mean Beam Distribution Over Time

## Slide 13
Chart: Loss Over Mean Beam Distribution From Multiwires, Center Pivot
Losses lowering = POT lowering? Scraping upstream of loss monitor
Scraping closer to loss monitor
1
2
Expect to see symmetric losses

## Slide 14
Chart: Loss Over Mean Beam Distribution From Multiwires, +2mm Pivot
1
2
Losses lowering = POT lowering? Scraping upstream of loss monitor
Scraping closer to loss monitor
Expect to see symmetric losses

## Slide 15
Chart: Loss Over Mean Beam Distribution From Multiwires, -2mm Pivot
No scraping?
Scraping closer to loss monitor
Expect to see symmetric losses
1
2

## Slide 16
Chart: Loss Over Mean Beam Distribution From Multiwires, -2mm Pivot
How well do we know our pivot point?
What could beam be scraping on upstream?
How can we understand the beam shape better?
Is there a quicker, easier way to import these data and get analyses done more efficiently and more frequently?