## Slide 1
Kyle Leleux
RF Detector Meeting
25 July 2019
Data Acquisition System for RF Beam Detector

## Slide 2: How are we Collecting Data?

## Slide 3: Front-end Display

## Slide 4: Dataflow Operations
Specify Parameters
  Samples
  Time base
  File path
  File name
Initialize Device
Start Sampling
  Check trigger
  Generate timestamp
  Fetch waveform
  Save waveform
  Plot Waveform
Post Processing
  Add headers
  Add time column

## Slide 5: Challenges During the Development Cycle
Reacquainting with LabVIEW
Driver Issues
Different Iterations
Design Optimizations
Benchtop Testing

## Slide 6: Future Plans
Benchtop TTL Signal
Implement Data Processing
Implement Safety Measures
Documentation and Comments
Poster and Paper
Implement the DAQ System for the Beam Signal
Not only DAQ, but Control

## Slide 7: Questions?
Notes: So just a little background before we talk about the data acquisition system… where is the data coming from? So as we can see, this is a diagram of the target wall. When a beam pulse, it hits the target. The horns collimate the created beam before it enters the decay pipe. Directly after the decay pipe is my system: the hadron monitor system. You could used well tested and implemented systems such as ionization chambers, but these systems experience problems with low gain because its design necessitates an insulator, which is susceptible to radiation damage. Keep in mind that the beam pulses for 10us every 1.33s for most of the year. The propose system is an array of gas filled aluminum rf cavities. The purpose of this is to determine the beam spread, beam centroid, and target deterioration. As you can see here is one of the aluminum gas filled rf cavities. It is currently being tested in an abort chamber at fermilab.
2.4 GHz gas-filled RF resonator
Detector and wave guide made of aluminum for rad-hard
Test cavity can be pressurized up to 2 atm
Beam ionizing gas and form plasma in the cavity
Plasma consumes RF power
Consumption is proportional to the amount of incident beam
Shunt impedance (𝑅) can be measured without beam
It suggests that beam intensity can be reproduced without beam calibration