## Slide 1: Accelerating discovery in the era of ‘Big Data’ Science
Inder Monga
Executive Director, Energy Sciences Network
Division Director, Scientific Networking
Lawrence Berkeley National Lab
OSG Council Meeting,
October 10th, 2019

## Slide 2: DOE’s high-performance network (HPN) user facility optimized for enabling big-data science
Provides connectivity to all of the DOE labs, experiment sites, & user facilities (> 34417 users)
26
user facilities
OLCF
ALCF
NERSC
ARM
JGI
SNS
HFIR
EMSL
APS
LCLS
NSLS-II
SSRL
ALS
CINT
CNM
CNMS
TMF
CFN
NSTX-U
ATLAS
RHIC
DIII-D
ATF
Fermilab AC
CEBAF
FACET
Notes: While the user facility serves the connectivity needs of all DOE labs, from experiments to supercomputers, the special sauce is optimization to meet the every growing needs of big-data science
Advanced Scientific Computing Research (ASCR) National Energy Research Scientific Computing Center (NERSC) LBNL Argonne Leadership Computing Facility (ALCF) ANL Oak Ridge Leadership Computing Facility (OLCF) ORNL Energy Sciences Network (ESnet) LBNL Basic Energy Sciences (BES) Light Sources Advanced Light Source (ALS) LBNL Advanced Photon Source (APS) ANL Linac Coherent Light Source (LCLS) SLAC National Synchrotron Light Source II (NSLS-II) BNL Stanford Synchrotron Radiation Light Source (SSRL) SLAC Neutron Sources High Flux Isotope Reactor (HFIR) ORNL Spallation Neutron Source (SNS) ORNL Nanoscale Science Research Centers Center for Functional Nanomaterials (CFN) BNL Center for Integrated Nanotechnologies (CINT) Sandia/LANL Center for Nanophase Materials Sciences (CNMS) ORNL Center for Nanoscale Materials (CNM) ANL The Molecular Foundry (TMF) LBNL Biological and Environmental Research (BER) Environmental Molecular Sciences Laboratory (EMSL) PNNL Atmospheric Radiation Measurement Climate Research Facility (ARM) Global network Joint Genome Institute (JGI) LBNL Fusion Energy Sciences (FES) DIII-D General Atomics National Spherical Torus Experiment Upgrade (NSTX-U) PPPL High Energy Physics (HEP) Accelerator Test Facility (ATF) BNL Fermilab Accelerator Complex FNAL Facility for Advanced Accelerator Experimental Tests (FACET) SLAC Nuclear Physics (NP) Continuous Electron Beam Accelerator Facility (CEBAF) TJNAF Relativistic Heavy Ion Collider (RHIC) BNL Argonne Tandem Linac Accelerator System (ATLAS)

## Slide 3: Our vision:
    Scientific progress will be completely unconstrained by the physical location of instruments, people, computational resources, or data.

## Slide 4
Even though ESnet builds and operates a network,
it’s focus is on data…
... offering unique capabilities aka “services”, and optimizing the network for
data acquisition, data placement, data sharing, data mobility
Notes: How does ESnet accelerate science? It provides unique services or capabilities like the OSCARS reservation service and is optimized for handling data - from acquisition, placement, sharing as well as high-speed data transfers aka mobility.

## Slide 5: An ~exabyte network today
~10x growth every 4 years
1078 PB in FY 2019
exponential traffic growth over past 28 years
measures ingress or egress only, not traffic per link
Notes: Consistent exponential increase in traffic over the past 28 years. We have seen the slope slow down a little the past few years and Chin will talk about how we are taking it into account for our capacity projections.

## Slide 6: LHCONE ESnet Traffic Matrix - Dynamic Heatmap Month: April 2019
Online at: https://downloads.es.net/public/richard/
LHCONE traffic from our peers (e.g., between Compute Canada to CERN via our Canet peering in pnwg-cr5)

## Slide 7: LHCONE US Only Traffic Matrix - Dynamic Heatmap Month: April 2019
Online at: https://downloads.es.net/public/richard/
CMS
ATLAS

## Slide 8: Transatlantic - LHCONE TA
Tier model in operation: most traffic from EU comes to BNL and FNAL.
FNAL T1 EU->US
BNL T1 EU->US
ATLAS
CMS

## Slide 9: Instrument upgrades will generate ~10x data
Year | Facility |  |  |  | 
 | ALS | APS | LCLS/LCLS-II | NSLS-II | SSRL
2021 | 3 PB | 7 PB | 30 PB | 42 PB | 15 PB
2028 | 31 PB | 243 PB | 300 PB | 85 PB | 15 PB

## Slide 10
Big Data
Data Generation
Data Logistics
Data Analysis and Storage
Science Instruments like LHC, Telescopes, Light Sources.
Data Transfer Nodes at user facilities, Networks, Caching, Data streaming, Orchestration etc.
Algorithms (CAMERA++), HPC Systems, Analytics Software Stack, HPSS etc.

## Slide 11: Data ‘Tsunami’ is driving network transformation
Network Performance
(End-to-End) Data Workflow
Human manageable
Automation
Experience (gut) Driven
Analytics
Driven
Fixed/
Scheduled
Flexible/
Interactive
Notes: Talk about how the current initiatives have been impactful on DOE science and the larger research community

## Slide 12: Each major upgrade transforms the facility with innovative, cutting edge technologies
2005
ESnet (Gen 3)
Asynchronous Transfer Mode technology (new, now obsolete), provided by Carrier Sprint
2011
ESnet (Gen 4)
Traditional IP Routing with ESnet innovation OSCARS (new) to build Science Data Network (SDN)
2021
ESnet (Gen 5)
Shared optical substrate (New) with traditional IP routing. Acquisition of Dark Fiber resource
2027
ESnet (Gen 6)
Innovative architecture with capability to meet capacity, reliability, and flexibility mission need
2014:
Transatlantic network
Notes: Before we talk about ESnet6, I would like to give you a sense of the multiple upgrades the facility has gone through. Our success in upgrades is when the users don’t even know that the upgrade happened. For each upgrade we have transformed the technology base to the most innovative to meet the science needs of that decade. For example, ESnet3, the third generation, was using a technology called ATM (asynchronous Transfer mode), now obsolete. Gen4 saw the birth of OSCARS, our virtual circuit service, and Gen5 is where we delved into the optical layer in addition to the packet layer. In all previous generations, the optical network was provided by a commercial carrier.

## Slide 13
Optical Core
Packet Core
“Low-Touch Path”
Service Edge
“High-Touch Path”
Service Edge
ESnet6 architecture components (Layered View)
Layer 0
(Transmission Medium)
Layer 1 (Optical)
Layer 2.5 (MPLS)
Layer 2 (Ethernet Switching)
Layer 3 (IP Routing)
“Above the Net” Services
(Virtual Network Functions)
Mission Needs:
Capacity, Resiliency, Flexibility
Mission Needs:
Flexibility
Mission Needs:
Capacity, Resiliency
Mission Needs:
Capacity
Services Edge
“Hollow” Core
Network
Storage
Code / Software
Compute
Data

## Slide 14: ESnet6: software automation architecture
orchestration
provisioning
analytics & ML
telemetry
Notes: Animation on slide. The software architecture integrates orchestration, provisioning, telemetry and analytics

## Slide 15: When will I get home?
LAX– Caltech, 6 pm: 1 hr – 1hr 50 min
LAX– Caltech, 11 pm: 32 min

## Slide 16: Even well tuned infrastructure does not get consistent service
Chard K, Dart E, Foster I, Shifflett D, Tuecke S, Williams J. (2018) The Modern Research Data Portal: a design pattern for networked, data-intensive science. PeerJ Computer Science4:e144 https://doi.org/10.7717/peerj-cs.144
Nine orders of
variability

## Slide 17: How to ‘crack open the network black box’ without destroying the power of the abstraction?
High-precision telemetry
Scalable analytics infrastructure
Model-based approach to request network services
Network prediction using machine learning techniques

## Slide 18: 1. High-precision telemetry: deep insight into flows
  Per flow, high-precision telemetry
  Per packet-metadata tracking (e.g. timestamp, ingress location, etc)
  10 ns precision in timing
Jupiter with the naked eye
Jupiter Close Up
Use high-fidelity data to get better insights and analytics:
Packet Microbursts
Path deviations ( RTT and Delay )
Security / anomaly detection
Head of Queue Blocking
Many others…
Notes: Telemtry

## Slide 19: 1 Gbps iPerf flow - 600,000 packets
Note: Average rate is calculated using a time-weighted average of per-packet rates.
1 Gbp/s average flow rate (100 pkt window)
Per-packet rates reaching 10 Gbit/s (line rate of the sender)

## Slide 20: 1 Gbps iPerf flow - 1% packet drop
Note: only 23 packets were dropped all together, taking bandwidth down to 5 Mb/s from 1 Gb/s.
5 Mb/s average flow rate (100 pkt window)
Per-packet rates maximum: 1 Gb/s

## Slide 21: Usually alert when something is broken…
…and then get expert help
Why is this so?
Notes: Why is this so? Answer is simple:
Doctors and Nurses don’t have time evaluate your daily data
They do not know what the data means in many cases (the small variations per day)

## Slide 22: 2. Scalable analytics infrastructure
Real-time telemetry from the network
netbeam platform: Using Apache BEAM and Google Cloud Platform
Both Batch and Stream processing in parallel
In production for ESnet SNMP data
Streams telemetry
On-demand analytics infrastructure

## Slide 23: 3. Model based approach to request network services
DTN
DTN
DTN
DTN
MAX
ESnet
SENSE Resource Manager
RM
RM
RM
RM
RM
RM
Application Workflow Agent
SENSE Orchestrator
SENSE End-to-End Model
SENSE project is a research project funded by ASCR, DOE, US
Realtime system based on Resource Manager developed infrastructure and service models
UMD
DTN
RM
RM
Multi-resource models abstracts the network specifics away and allows for higher-level service request

## Slide 24: 3. Enables an end-to-end service model that includes compute, storage, instrument and the network
Application Workflow
Resource Orchestrator
CMS
ALICE
ATLAS
LHC-B
Experiment Resource
Manager
Network Resource Manager
Compute / Storage Resource Manager
Network of Facilities
Notes: Resource Types - Compute (e.g. HPC, local cluster, edge compute), Storage (e.g. HPS, local storage, DTNs), Network (e.g. WAN, LAN, exchanges), Experiment (e.g. colliders, light sources, tokamaks).
Resource Managers - Manages local resources within the domain and communicates with Resource Orchestrator(s).
Resource Orchestrator - Interacts with application workflow and coordinates end-to-end resource provisioning with Resource Managers.
Network of Facilities - Represents a specific set of resources that have been committed as per the request of an application workflow.

## Slide 25
Application Workflow
Resource Orchestrator
Requests, Credentials
Confirmation, Status, telemetry
Capabilities, Availability,
Confirmation, Status
Requests, Credentials
CMS
ALICE
ATLAS
LHC-B
Experiment Resource
Manager
Network Resource Manager
Compute / Storage Resource Manager
CMS
Compute
Storage
Network
Instrument
Network of Facilities
Interconnected Facilities
3. Enables an end-to-end service model that includes compute, storage, instrument and the network
Notes: Resource Types - Compute (e.g. HPC, local cluster, edge compute), Storage (e.g. HPS, local storage, DTNs), Network (e.g. WAN, LAN, exchanges), Experiment (e.g. colliders, light sources, tokamaks).
Resource Managers - Manages local resources within the domain and communicates with Resource Orchestrator(s).
Resource Orchestrator - Interacts with application workflow and coordinates end-to-end resource provisioning with Resource Managers.
Network of Facilities - Represents a specific set of resources that have been committed as per the request of an application workflow.

## Slide 26: ExaFEL: A science example for streaming data end-to-end
DTNs
FFB Layer (nVRAM)
ESNET
Compressor Nodes
PGP
PGP
PGP
PGP
Eth
IB
Beam Line Data
LCLS
LCLS
ESNET
Exascale HPC
1 TB/s
DTNs
NERSC
Router
Burst Buffer nVRAM: Streaming Analysis
Software ETH Routers
NGF / Lustre: Offline from HDF/XTC files.
IB
Exascale
HSN
Aggregate detector data, EPICS data, beamline data -
selection and compression
10 GB/s - 1Tb/s
EPICS Data
Timing
Online Monitoring & FFB Nodes
Event builder nodes
ExaFEL Data Flow
SDN for End-to-End Networking @ Exascale (SENSE)
SENSE Orchestrator
SENSE Network-RM
SENSE DTN-RM
LCLS Data Transfer Workflow

## Slide 27: 4. Network prediction using Machine Learning techniques
Network traffic prediction will help us bring route and re-route flows appropriately and on-the-fly
Understanding which sites are busiest at different times
High-Speed classifying of big and small flows to redirect packet routes
Prevent congestion and links failures by anticipating traffic 24 hours in advance

## Slide 28: ESnet6 with distributed compute and storage – aligned with OSG’s approach
Compute Cluster
Edge Switch Router
Open Line System
Compute Cluster
Edge Switch Router
Compute Cluster
Edge Switch Router
West
East
Centralized
Compute and Storage
Open Line System
SmartNIC
SmartNIC
SmartNIC
Storage
Storage

## Slide 29: Why FABRIC?
The mantra of the last 20 years – ‘Internet is showing its age.’
  Applications designed around discrete points in the solution space
  Inability to program the core of the network
What changed?
  Cheap compute/storage that can be put directly in the network
  Multiple established methods of programmability (OpenFlow, P4, eBPF, DPDK, BGP flowspec)
  Advances in Machine Learning/AI
  Emergence of 5G, IoT, various flavors of cloud technologies
Opportunity for the community to push the boundaries of distributed, stateful, ‘everywhere’ programmable infrastructure
  More control or dataplane state, or some combination? Multiple architectures (co)exist in this space.
  Network as a big-data instrument? Autonomous network control?
  New protocols and applications that program the network?
  Security as an integral component?
Notes: when showing this slide say that a) we take no position as to which architecture is ‘correct’ and b) the list of possible ideas is non-exhaustive and we want the community to tell what else they might use it for.

## Slide 30: FABRIC Core
Notes: Only Esnet footprint shown. Additional core nodes to be located in several regionals (TBD)

## Slide 31: FABRIC Edge
Notes: Metcalfe’s law

## Slide 32: What is a FABRIC node?
Core and edge nodes have compute, storage and programmable networking capabilities
  Network programming at the level of OpenFlow, P4, eBPF, DPDK
  GPUs to support ML applications
  Ability to interpose compute, memory and storage into the path of fast packet flows
  Processing speeds at 25Gbps, 40Gbps, 100Gbps, Nx100Gbps
  Experimenters access hardware directly (programmable network cards, GPUs, FPGA cards)
The key is node placement
  13 core nodes located in telco locations at the intersection of multiple high-capacity dedicated optical links. Provide sliceable, programmable switching, hierarchical storage and in-network compute
  16 initial edge nodes (also known as ‘hanks’) located on campuses, in lab datacenters to provide base load, serve as gateways for facilities to connect to FABRIC
Notes: 13 core = 9 in Esnet footprint, 4 additional in regionals (TBD)

## Slide 33: Four year Construction Timeline
Year 1
Year 2
Year 3
Year 4
Planning
Prototyping
Software development
Community building
Begin phase 1 deployment
Testing, commissioning
Design driver on-boarding
Complete Phase 1
Design driver experiments and early users
Begin Phase 2 deployment
Complete Phase 2 deployment
Prepare for operations

## Slide 34: Why ESnet?
Compute, storage and network are converging in interesting ways and are creating new opportunities
  End-to-end orchestration, resource allocation, caching, edge-computing, etc.
With the advent of exascale, AI/ML, extreme heterogeneity – the computing model, and the use of network is bound to change
  Opportunity rather than a problem
FABRIC is a potential strategic platform to test some of the new workflow ideas for science
Larger effort by ESnet to understand how storage can integrate into network to enable more efficient use of the network (e.g., resource scheduling, load-balancing, proactive resiliency, intelligent feedback)
  OSG has similar objectives, and can leverage the change in the network to optimize the data placement for better distributed computing, edge computing, etc.
Leveraging the cloud for cores-on-demand for science applications will require scale and connectivity that ESnet can provide

## Slide 35: The Data Circulatory System for DOE Collaborative Science
Networking tailored to meeting science demands
  Bandwidth reservations, performance monitoring, Science “DMZ” model for the last mile,..
An effective network design and application interaction is extremely important to meet the needs of next-generation of data science
ESnet
100G
ESnet
100G
ESnet
100G
ESnet 100G/10G
ESnet 100G
ESnet 100G
ESnet 2*100G
Notes: ESnet is one of the oldest, fastest parts of the internet

## Slide 36: Thank you.
imonga@es.net

## Slide 37: GRETA dataflow architecture – in-instrument integration of data, compute and network [Data Management and workflow tools]