## Slide 1
M. Baldini
8th August 2019
Fiber optics and future accelerator magnets

## Slide 2
Project Summary (goals, novelty, relation to mission)
Goal: Developing a novel instrumentation tools and analysis technique to enable a deep understanding of magnet training process and to design free of quench magnets in future accelerators.
Focus: to use the fibers to characterize external disturbances in order to drive and give feedback for designing free of quench magnets. A novel approach to investigate the disturbance spectrum: energy and localization.
Strategic relevance:
  Match the Laboratory distinctive capability on accelerator magnets and bring enduring benefit in magnet diagnostic.
  Lab mission: significant impact on cost and schedule of future High Energy Hadron Colliders; possibly enabling them.
LDRD: optical fiber sensors

## Slide 3: LDRD Project focus
Use fiber optic sensors for bridging the technology gap on superconductive magnet diagnostic
FBG fibers: discrete sensors
Rayleigh fibers: continuous sensors

## Slide 4
Project work plan
PHASE 1 (1 year): develop a novel magnet diagnostic using bonded FBG fiber sensor to measure strain and temperature during magnet fabrication and training.
Short term goals:
  Handling and bonding
  Fiber coating
  Fiber calibration
PHASE 2 (2-3 year): use Rayleigh fibers
Embed and wind fibers along a coil
Consult with vendor for measurements and data analysis/interpretation
Fabricate a coil and test a short mirror magnet/short model
Disturbance spectrum analysis

## Slide 5
Fiber optics and future accelerator magnets
FBG (Bragg grating) fibers to measure strain and temperature on shell and coil
Goal: bring a novel and advantageous diagnostic probe at FNAL
Monitor strain and temperature during magnet service life:
Coil fabrication
Assembly
Cold down
Training
Heat treatment/
impregnation
Pre-stress effects
Temperature and strain
distribution

## Slide 6
FBG fibers: costs and needs
5-6 gratings per fibers + 2 accesses: 1500$ per fiber
Spectrometer with 1kHz acquisition rate: Si255 Hyperion from Micron optics. Price is 35000$ (multiplexing capability)
Resplice fiber instrumentation: 4000$
R&D goals:
fiber handling and bonding
Fiber coating for T estimation
Calibrations of the fiber: cryostat down to 4.2 K
Testing: short model (Synergy with MDP/HFM)

## Slide 7
Fiber optics and future accelerator magnets
Quench detections for HTS magnets
Mechanical perturbation spectrum for superconducting magnets:
  Localization of quench in the pole turn: tip of the cable/distributed?
  Determination of energy releases
New coil design and novel diagnostic
Goal: bridging the technology gap on superconductive magnet diagnostic

## Slide 8
Rayleigh fibers cost and needs
Someone from the vendor Lupine visit and help set up the system and acquire data: 40-50k. They bring the instrumentations and test it with you
Interrogators 75000 $ to > 100000 $
Fibers itself are 500$
Fiber embedded in the coil
Determine spatial and temporal resolution required

## Slide 9
R&D effort:
fiber handling and bonding
Fiber coating for T estimation
Calibrations of the fiber: cryostat down to 1.9 K
Understand how to wind multiple fibers around the pole
Fabricate and test at least one short coil with fibers embedded and wound around the pole.
Test of a short magnet with new instrumentation
Disturbance spectrum analysis
Rayleigh fibers cost and needs