## Slide 1: Electrical Test Plans
Andrew Laundrie
UW Physical Sciences Lab
DUNE Electronics Review
2019 November 18

## Slide 2: APA Production Testing
X, V, and U wires will be tested for continuity and isolation by probing through X head boards
Probe cards will be mounted in place of CR boards
A separate set of probe cards will be mounted in place of G-bias boards
Similar or identical probe cards would be used for Electronic Tension Testing

## Slide 3: APA Production Testing
Continuity and low-impedance isolation tests will be streamlined by injecting signals with four different audio frequencies on all wires simultaneously
Foot board terminations are probed individually
Test points probed in rapid succession will produce a repeating succession of four tones
Missing or mixed tones will indicate a problem

## Slide 4: APA Production Testing
High-voltage isolation and leakage tests can be streamlined by testing groups of 10 or 12 wires connected in parallel
When a group fails, individual wires can be probed to isolate the problem
Normal testing would proceed 10-12 times faster than testing wires individually

## Slide 5: Wire Tension Testing
An upgraded laser tensometer is easier to position, computes the resonance frequency, and records data with less user intervention
Upgrades will cut measurement times in half
Still needed as a backup to Electronic Tension Testing

## Slide 6: CR and G-bias Board Tests
Probing of individual capacitors and resistors is very slow due to exponential decay of charging currents (pre-charging helps)
Automated testing is challenging because of high voltage (1 kV) and high impedance (10^10 Ohms)
A high-impedance comparator that monitors current thresholds as small as 0.1 nA has been demonstrated

## Slide 7: CR and G-bias Board Production Tests
An envisioned test system would check the power-up response of an entire PCB by monitoring the charge current through each coupling capacitor (or G-bias filter output)
Defective components would alter the transient signatures of individual channels
Threshold crossings that occur too soon or too late would reliably indicate defective parts