## Slide 1: Bias Wire Harness Design and Construction
Andrew Laundrie
UW Physical Sciences Lab
DUNE Electronics Review
2019 November 18

## Slide 2: Bias Wire Harness Features
Brings bias voltages to CR and G-bias boards
Fed from the SHV receptacles in the SHV panel
ProtoDUNE bias connectors probably should be upgraded to more secure locking method
Better connectors could justify less redundant
Pastel wire colors are difficult to differentiate
Seeking ways to label bias connectors or wires

## Slide 3: Bias Harness: A Mess of Wires
Two bundles of 12 wires span the head tube
Sixty bias pigtails have to be managed
DUNE APAs ship without CR boards installed
Harnesses could be installed on-site
The wider DUNE head tube helps

## Slide 4: Looped Daisy-Chain (Ring) Architecture
A single disconnected bias connector drops bias voltage to only one head board
Redundant loops ensure that a single disconnected bias connector does not leave any X, U, or G wires unbiased

## Slide 5
P10XA
P10XB
X layer bias
CR Board 10
P9XA
P9XB
X layer bias
CR Board 9
P1XA
P1XB
X layer bias
CR Board 1
P11XA
P11XB
X layer bias
CR Board 11
P12XA
P12XB
X layer bias
CR Board 12
P20XA
P20XB
X layer bias
CR Board 20
Bias Input X
SHV
N.C.
Bias wires are 20 AWG stranded
hook-up wire, color-coded, with
silicone insulation rated for 3 kV
Bias plugs are Phoenix
type 1778832 with heat-
shrink tubing applied
to improve insulation

## Slide 6
P10UA
P10UB
U layer bias
CR Board 10
P9UA
P9UB
U layer bias
CR Board 9
P1UA
P1UB
U layer bias
CR Board 1
P11UA
P11UB
U layer bias
CR Board 11
P12UA
P12UB
U layer bias
CR Board 12
P20UA
P20UB
U layer bias
CR Board 20
Bias Input U
SHV
N.C.
Bias wires are 20 AWG stranded
hook-up wire, color-coded, with
silicone insulation rated for 3 kV
Bias plugs are Phoenix
type 1778832 with heat-
shrink tubing applied
to improve insulation

## Slide 7
P10GA
P10GB
G layer bias
Filter Bd 10
P9GA
P9GB
G layer bias
Filter Bd 9
P1GA
P1GB
G layer bias
Filter Bd 1
P11GA
P11GB
G layer bias
Filter Bd 11
P12GA
P12GB
G layer bias
Filter Bd 12
P20GA
P20GB
G layer bias
Filter Bd 20
Bias Input G
SHV
N.C.
Bias wires are 20 AWG stranded
hook-up wire, color-coded, with
silicone insulation rated for 3 kV
Bias plugs are Phoenix
type 1778832 with heat-
shrink tubing applied
to improve insulation

## Slide 8: Bias Connectors
Plugs have small wedge-shaped protrusions that expand the receptacle body slightly when inserted. The protrusions lock into cut-outs in the receptacle body.
Separation force is about 1 pound.
Surface-mount receptacles are compact and mount securely to circuit boards. The insulation material is a liquid-crystal polymer with high heat tolerance and good low-temperature performance.

## Slide 9: Wire harness construction
Field cage bias will bypass SHV panels in DUNE. The SHV panel will have fewer connectors and a smaller footprint.

## Slide 10: Backup Slides