## Slide 1: Development of an X-band Field Emission RF Gun at Tsinghua University
LY Zhou, Hao Zha, Jiaru Shi†, Huaibi Chen
Department of Engineering Physics, Tsinghua University, Beijing, China
Apr 19, 2021
Email: shij@tsinghua.edu.cn

## Slide 2: Content
Advantages of field emission rf gun
Design of field emission rf gun at THU
Testing
Observation after conditioning
Plans

## Slide 3: Content
Advantages of field emission rf gun
  higher initial brightness
  compact size
Design of field emission rf gun at THU
Testing
Observation after conditioning
Plans

## Slide 4: Advantages of field emission rf gun
Brightness at cathode:
Image charge limitation:
,
To make the emission phase close to 90°, shorter length of the gun’s first cavity is needed
[REF]J. B. Rosenzweig, Next generation high brightness electron beams from ultrahigh field cryogenic rf photocathode sources, Phys. Rev. Accel. Beams 22, 023403

## Slide 5: Advantages of field emission rf gun
Field emission gun naturally emits beam at 90°
The thermal emittance of field emission cathode is comparable to that of photocathode
Compact size – Laser free
[REF] Xiangkun Li, Study of field emission cathode rf gun, PhD dissertation, 2015, Tsinghua University
cathode | condition | 
 | 1700K | 0.268mrad
Cu | 266nm | 0.297mrad
Mo | 7e9V/m | 0.285mrad
cathode | condition | 
 | 1700K | 0.268mrad
Cu | 266nm | 0.297mrad
Mo | 7e9V/m | 0.285mrad

## Slide 6: Content
Advantages of field emission rf gun
Design of field emission rf gun at THU
  rf design
  cooling and vacuum
  cathode emitter
  dynamics
Testing
Observation after conditioning
Plans

## Slide 7: Design of field emission rf gun at THU
Frequency: 11.424GHz
Target energy: ~4MeV
Breakdown research
Gradient: ~200MV/m
Length: ~2.35Cells
Cathode pluggable
[REF] Xiaowei Wu, Design and experiment of x-band high-gradient choke-mode accelerating structure, PhD dissertation, 2017, Tsinghua University

## Slide 8: Design of field emission rf gun at THU
rf design
  The first cavity is designed to work in the TM02 mode, and the cathode is separated from the cavity wall at the minimal place of the magnetic field.
E_surfmax/E_axismax | 1.15
P100MV/m | 2.55MW
Electric field
Magnetic field

## Slide 9: Design of field emission rf gun at THU
cooling system
  4 cooling pipes
  27°C, 0.6m3/h
  200ns, 23MW rf
  66.37°C highest
Vacuum system
  6.2e-7Pa

## Slide 10: Design of field emission rf gun at THU
cathode with an emitter
surface topography
Process of cathode replacement
ID | h/μm | β
1 | 5±2 | 6.2
2 | 100±20 | 19.8
3 | 150±20 | 26.7
4 | 200±20 | 32.3

## Slide 11: Design of field emission rf gun at THU
Joule heating effect
  Due to the low resistivity and good thermal conductivity of copper, the emitter can withstand large emission current
Field emission
  The process of field emission is simulated by Monte Carlo method under the following assumptions:
    energy distribution
    tunneling probability

## Slide 12: Design of field emission rf gun at THU
RF Filling process
  The electron beam is emitted in each pulse
  When the acceleration gradient is close to 80 MV / m, the electron beam can be detected at the exit of the gun
Wakefield
  A wakefield mode (TM01) at a frequency of 4.856GHz is trapped in the gun
  The subsequent beam will be subjected to a decelerating force

## Slide 13: Content
Advantages of field emission rf gun
Design of field emission rf gun at THU
Testing
  cold testing
  high power testing
Observation after conditioning
Plans

## Slide 14: Testing
cold testing
  A tuning method based on field distribution of different modes was applied
  A testing cathode with an aperture of 1.5mm was used to process bead pulling
Final Parameters
Parameter | Design | Measured
f0 | 11.424GHz | 11.4232GHz
Q0 | 6870 | 6542
beta | 1.2 | 1.33
[REF] Jiaru Shi, Calculating RF Parameters of Individual Cell by Electric Field Distribution of a Coupled Cavity Chain, High Energy Physics and Nuclear Physics, 029.008(2005), pp.818-823.

## Slide 15: Testing
high power testing

## Slide 16: Testing
high power testing
Breakdown signal
  A part of RF breakdown signals appear after the end of microwave signal

## Slide 17: Content
Advantages of field emission rf gun
Design of field emission rf gun at THU
Testing
Observation after conditioning
  visual observation
  white light interference
  SEM
Plans

## Slide 18: Observation after conditioning
visual observation & white light interference
A circle where electric field is 0 caved around 0.1μm
The surface damage includes protrusions and craters, They are more likely to appear on the ups of machining marks

## Slide 19: Observation after conditioning
SEM
  The element contents of protrusions and craters are different
  The craters are composed with cooper
  The protrusions contain more impurity elements
  The formation mechanism and time of these two types of damage could be different
C
O
Cu
Fe
Mg
Al
Si
Cl
Ca
S
base
measured are

## Slide 20: Content
Advantages of field emission rf gun
Design of field emission rf gun at THU
Testing
Observation after conditioning
Plans

## Slide 21: Plans
Cathode imaging system
  A cathode imaging beamline will be built in this summer, to image the transformation of cathode surface during conditioning

## Slide 22: Conclusion
An x-band field emission rf gun with a pluggable cathode was developed at Tsinghua University
  11.424GHz, 200MV/m, 50ns
A cathode imaging beamline will be built soon

## Slide 23: Thanks for your attention